## Slide 1: Security of BIOS/UEFI System Firmware from Attacker and Defender Perspectives Section 3. Hands-On Learning of Platform Hardware and Firmware
Yuriy Bulygin *
Alex Bazhaniuk *
Andrew Furtak *
John Loucaides **
* Advanced Threat Research, McAfee
** Intel

## Slide 2: License
Training materials are shared under Creative Commons “Attribution” license CC BY 4.0
Provide the following attribution:
Derived from “Security of BIOS/UEFI System Firmware from Attacker and Defender Perspective” training by Yuriy Bulygin, Alex Bazhaniuk, Andrew Furtak and John Loucaides available at https://github.com/advanced-threat-research/firmware-security-training

## Slide 3: Section 3. Hands-On Learning of Platform Hardware and Firmware

## Slide 4: 3.0 Building and Installing CHIPSEC

## Slide 5: Bootable Linux USB with CHIPSEC

## Slide 6: Bootable Linux USB with CHIPSEC
Ubuntu bootable USB with CHIPSEC (includes all dependencies)
Building and running CHIPSEC:
# cd ~/Desktop/chipsec/source/
# git pull (you already have latest CHIPSEC on USB)
# python setup.py build_ext -i
# sudo python chipsec_util.py platform

## Slide 7: Installing CHIPSEC on Windows
Install Python 2.7.x (http://www.python.org/download/)
Install additional packages for installed Python release
    pip install setuptools
    pip install pywin32
Build CHIPSEC Windows driver. Skip this step if you already have chipsec_hlpr.sys built
Copy CHIPSEC driver (chipsec_hlpr.sys) to proper path in CHIPSEC \chipsec\chipsec\helper\win\win7_amd64 or win7_x86
Install CHIPSEC
    pip install chipsec
Turn off kernel driver signature checks in Windows 8, 8.1, 10 64-bit
Refer to CHIPSEC manual:
https://github.com/chipsec/chipsec/blob/master/chipsec-manual.pdf

## Slide 8: 3.1 Access to Hardware Resources

## Slide 9: Hardware Configuration
CPU
x86 state: GPR (RAX, …), Control Registers (CRx), Debug Registers (DRx), etc.
CPU Model Specific Registers (MSR)
CPU and Chipset (SoC)
Processor I/O space: I/O ports and I/O BARs
PCIe devices configuration space
Memory-mapped PCIe configuration access a.k.a. Enhanced Configuration Access Mechanism (ECAM)
Memory-mapped I/O ranges
IOSF Message Bus registers

## Slide 10: Processor I/O Space: I/O Ports and BARs
Legacy I/O interface accessible via x86 IN and OUT assembly instructions
Offset in I/O space is I/O register or I/O port. I/O space contains multiple ranges assigned to some device or controller
I/O ranges can be fixed:
    60h/62h/64h/66h: keyboard/embedded uController
    CF8h/CFCh: PCIe devices CFG access
    CF9h: platform reset
    B2h/B3h: APMC/SMI
Or variable (defined by I/O BAR registers)
    SMBus
    ACPI/PMBASE
    GPIO
    I/O Trap

## Slide 11: Processor I/O Space: I/O Ports and BARs
# chipsec_util io <io_port> <width> [value]
# chipsec_util.py io 0xcf8 dword 0x80000000
[CHIPSEC] OUT 0x0CF8 <- 0x80000000 (size = 0x04)
# chipsec_util.py io 0xcfc dword
[CHIPSEC] IN 0x0CFC -> 0x0A048086 (size = 0x04)

## Slide 12: PCIe Configuration Space Access
SW uses one these mechanisms to access config space:
Legacy configuration access via control CF8h & data CFCh processor I/O ports
    PCI config register address
    bus << 16 | device << 11 | function << 8 | offset & ~3
    CF8h  1<<31 | bdf_address
    Read data from or write data to port (CFCh + off[1:0])
Extended (memory-mapped) config access (see later)
100h bytes of CFG header
8 * 100h per device
32* 8 * 100h per bus

## Slide 13: PCIe Configuration Space and Registers
Enumerate all available PCIe devices:
# chipsec_util pci enumerate
[CHIPSEC] Enumerating available PCIe devices..
BDF | VID:DID | Vendor | Device
--------------------------------------------------------------------------------
00:00.0 | 8086:0A04 | Intel Corporation |
00:02.0 | 8086:0A16 | Intel Corporation |
Reading from/writing to PCIe device’s configuration space:
# chipsec_util.py pci <bus> <dev> <fun> <off> <width> [value]
# chipsec_util.py pci 0 0 0 0x0 dword
[CHIPSEC] reading PCI B/D/F 0/0/0, off 0x00: 0xA048086
# chipsec_util.py pci 0 0x1F 0 0xDC byte
[CHIPSEC] reading PCI B/D/F 0/31/0, off 0xDC: 0x2A

## Slide 14: Extended PCIe Configuration
Enhanced Configuration Access Mechanism (ECAM) allows accessing PCIe extended configuration space (4kB) beyond PCI configuration space (256 bytes)
To access entire PCIe extended configuration space CPU reserves memory-mapped range in physical addressable memory (MMCFG)
    Range is re-locatable (e.g. PCIEXBAR register in B.D:F 0.0:0 on Core/Xeon, ECBASE msgbus register on Atom, MSR on AMD APUs…)
All access to MMCFG range is mapped to PCI configuration cycles
MMCFG is split into consecutive 4kB large chunks, each is extended CFG header per bus/device/function
Access is done at memory offset within MMCFG range
MMCFG offset =
bus*32*8*1000h + dev*8*1000h + fun*1000h + offset

## Slide 15: ECAM (MMCFG) Address Mapping
Memory Address | PCI Express Configuration Space
A[(20+n-1):20] | Bus Numbers 1 ≤ n ≤ 8
A[19:15] | Device Number
A[14:12] | Function Number
A[11:8] | Extended Register Number
A[7:2] | Register Number
A[1:0] | Along with size of the access, used to generate Byte Enable

## Slide 16: Memory Mapped PCIe Configuration
chipsec_util.py mmio with ‘MMCFG’ BAR
# chipsec_util.py mmio list
-------------------------------------------------------------------------------
MMIO Range | BAR | Base | Size | En? | Description
-------------------------------------------------------------------------------
...
MMCFG | 00:00.0 + 60 | 00000000F8000000 | 00001000 | 1 | PCI Express Range
...
# chipsec_util.py mmio read MMCFG 0x0 0x4
[CHIPSEC] Read MMCFG + 0x0: 0x0A048086
# chipsec_util.py mmcfg <b> <d> <f> <off> <width> [value]
# chipsec_util.py mmcfg
[CHIPSEC] Memory Mapped Config Base: 0x00000000F8000000
# chipsec_util.py mmcfg 0 0 0 0x0 dword
[CHIPSEC] reading MMCFG register (00:00.0 + 0x00): 0xA048086
# chipsec_util.py mmcfg 0 0 0 0xF80DC byte
[CHIPSEC] reading MMCFG register (00:00.0 + 0xF80DC): 0x2A
It doesn’t work at MinnowBoard, because Bay Trail has different interface for MMCFG (use address 0xE0000000 as MMCFG)

## Slide 17: Memory Mapped I/O Registers
Devices may have more registers than I/O and PCIe CFG spaces can fit so BIOS may reserve physical address ranges for devices
Ranges are defined by Base Address Registers (BAR). MMIO registers are offsets off of base of MMIO ranges
Any access to such MMIO range is forwarded to the device which owns this range (local in the CPU or over a system bus to chipset) rather than decoded to DRAM
mmio command in CHIPSEC can be used to list predefined MMIO BARs, dump entire BAR, and read/write MMIO registers
# chipsec_util.py mmio list
-------------------------------------------------------------------------------
MMIO Range | BAR | Base | Size | En? | Description
-------------------------------------------------------------------------------
GTTMMADR | 00:02.0 + 10 | 00000000F0000000 | 00001000 | 1 | Graphics Translation Table Range
SPIBAR | 00:1F.0 + F0 | 00000000FED1F800 | 00000200 | 1 | SPI Controller Register Range
HDABAR | 00:03.0 + 10 | 0000007FFFFFF000 | 00001000 | 1 | HD Audio Controller Register Range
GMADR | 00:02.0 + 18 | 00000000E0000000 | 00001000 | 1 | Graphics Memory Range
DMIBAR | 00:00.0 + 68 | 00000000FED18000 | 00001000 | 1 | Root Complex Register Range
MMCFG | 00:00.0 + 60 | 00000000F8000000 | 00001000 | 1 | PCI Express Register Range
RCBA | 00:1F.0 + F0 | 00000000FED1C000 | 00004000 | 1 | PCH Root Complex Register Range
MCHBAR | 00:00.0 + 48 | 00000000FED10000 | 00008000 | 1 | Host Memory Mapped Register Range
...
# chipsec_util.py mmio read|write|dump <BAR_name> <off> <width> [value]
# chipsec_util.py mmio read SPIBAR 0x78 4
[CHIPSEC] Read SPIBAR + 0x78: 0x8FFF0F40

## Slide 18: CPU Model Specific Registers (MSR)
CPU contains many Model Specific Registers (MSR) to enable/disable/configure various features & read statuses
MSRs can be architectural (e.g. IA32_APIC_BASE) and specific to some CPU models (e.g. LBR_TO/FROM_MSR)
MSRs can be per logical CPU, core or entire CPU package
Reading from / writing to CPU MSRs:
# chipsec_util.py msr <msr> [eax] [edx] [cpu_id]
Specifying cpu_id allows access to MSRs of specific logical CPU
  When omitted the command reads/writes MSR for all logical CPU in the package

## Slide 19: IA-32 Control Registers (CR)
x86 CPU CRs control behavior/state of the logical CPU
Example:
  CR0.PG - paging enabled
  CR0.PE - protection enabled
  CR3 (PDBR) - physical address of page directory
  CR4.SMEP / CR4.SMAP
Reading from / writing to CRs:
# chipsec_util.py cpu cr <cpu_id> <cr_number> [value]
Access to CRs is per logical CPU, you need to specify the # of the logical CPU (cpu_id) in CHIPSEC

## Slide 20: Exercise 3.1
Read BIOS/SPI Security Configuration

## Slide 21: Exercise 3.2
Access Hardware Resources

## Slide 22: 3.2 Overview of Open Source CHIPSEC Framework

## Slide 23
*Other names and brands may be claimed as the property of others.

## Slide 24: Structure
chipsec_main.py runs modules (see modules dir below)
chipsec_util.py runs manual utilities (see utilcmd dir below)
/chipsec
/cfg platform specific configuration
/hal all the HW stuff you can interact with
/helper support for OS/environments
/modules modules (tests/tools/PoCs) go here
/utilcmd utility commands for chipsec_util

## Slide 25: OS/Environment Specific Helpers
CHIPSEC supports Windows, Linux and UEFI shell environment.
OS/environment specific helpers for:
Windows : helper\win\win32helper.py
Linux : helper\linux\helper.py
UEFI (shell) : helper\efi\efihelper.py
Abstracts for support various OS/environments, wrapper around platform specific code that invokes kernel driver implemented in: helper/oshelper.py
Call path:
Module (or util)  HAL component  oshelper
 helper [Linux]  OS native code [LKM]

## Slide 26: Helper Code Example
helper/oshelper.py
# Read/Write CR registers
def read_cr(self, cpu_thread_id, cr_number):
return self.helper.read_cr( cpu_thread_id, cr_number )
helper\linux\helper.py
def IOCTL_RDCR(): return _IOCTL_BASE + 0x10
. . .
class LinuxHelper:
def __init__(self):
import platform
self.os_system = platform.system()
self.os_machine = platform.machine()
. . .
self.init()
. . .
def read_cr(self, cpu_thread_id, cr_number):
self.set_affinity(cpu_thread_id)
cr = 0
in_buf = struct.pack( "3"+_PACK, cpu_thread_id, cr_number, cr)
unbuf = struct.unpack("3"+_PACK, fcntl.ioctl( _DEV_FH, IOCTL_RDCR(), in_buf ))
return (unbuf[2])
read_cr function in Linux helper invokes IOCTL within the kernel module
OS specific (Linux) helper class specific to each OS
IOCTL invoking handler in the kernel module (“read CR”)
OS independent function which all HAL components invoke (read_cr)

## Slide 27: Detecting the Platform
Each platform supports its own set of hardware resources (interfaces, configuration registers)
Different modules may be applicable to only specific platforms or family of platforms
To support above, CHIPSEC detects the platform it’s running on
Detection is done using Host Controller Device ID (b.d:f 00.00:0). Supported DIDs are in chipsec/chipset.py
    Tip: to add support of a new platform, add its description in Chipset_Dictionary. Alternatively, create custom_chipsets.py, add my_dict with additional DIDs and add them to the main dictionary using chipset.Chipset_Dictionary.update(my_dict)
After detection, configuration (XMLs) for the detected platform is initialized (chipset.init_xml_configuration)

## Slide 28: Detecting the Platform
# chipsec_util.py platform
Supported platforms:
DID | Name | Code | Long Name
-------------------------------------------------------------------------------------
...
0xa04 | Haswell | hsw | 4th Generation Core Processor (Haswell U/Y)
0xc08 | Haswell | hsw | Intel Xeon Processor E3-1200 v3 (Haswell CPU, C220 Series PCH)
0xa08 | Haswell | hsw | 4th Generation Core Processor (Haswell U/Y)
0xa00 | Haswell | hsw | 4th Generation Core Processor (Haswell U/Y)
0xc00 | Haswell | hsw | Desktop 4th Generation Core Processor (Haswell CPU / Lynx Point PCH)
0xc04 | Haswell | hsw | Mobile 4th Generation Core Processor (Haswell M/H / Lynx Point PCH)
0x158 | Ivy Bridge | ivb | Intel Xeon Processor E3-1200 v2 (Ivy Bridge CPU, C200/C216 Series PCH)
0x150 | Ivy Bridge | ivb | Desktop 3rd Generation Core Processor (Ivy Bridge CPU / Panther Point PCH)
0x154 | Ivy Bridge | ivb | Mobile 3rd Generation Core Processor (Ivy Bridge CPU / Panther Point PCH)
...
Platform: 4th Generation Core Processor (Haswell U/Y)
VID: 8086
DID: 0A04
Additional command-line options:
    --platform (-p): use it if you know the platform but CHIPSEC doesn’t auto detect the platform
    --ignore_platform (-i): avoid platform detection when using platform agnostic functionality (e.g. access to UEFI variables)

## Slide 29: HW Abstraction Layer (HAL)
HAL is the set of components providing access to various hardware resources on the platform
HAL components abstract HW access specific to OS environment and expose it via a set of common APIs consumed by all modules in any OS environment
HAL components are OS unaware and invoke common helper functions from OS agnostic oshelper.py
HAL components can be basic primitives or complex
  Basic primitive HAL components provide access to basic HW resource (Example: CPU I/O, MMIO, etc.)
  Complex HAL components use basic primitive HAL to implement access to higher level HW resources (Example: SPI access is implemented via MMIO access)

## Slide 30: HW Abstraction Layer (HAL)
File name | Description
hal/pci.py | Access to PCIe configuration space
hal/physmem.py | Access to physical memory
hal/msr.py | Access to CPU resources (for each CPU thread): Model Specific Registers (MSR), IDT/GDT
hal/mmio.py | Access to MMIO (Memory Mapped IO) BARs and Memory-Mapped PCI Configuration Space (MMCFG)
hal/spi.py | Access to SPI Flash parts
hal/ucode.py | Microcode update specific functionality
hal/io.py | Access to Port I/O Space
hal/smbus.py | Access to SMBus Controller in the PCH
hal/uefi.py | Main UEFI component using platform specific and common UEFI functionality
hal/uefi_common.py | Common UEFI functionality (EFI variables, db/dbx decode, etc.)
hal/uefi_platform.py | Platform specific UEFI functionality (parsing platform specific EFI NVRAM, capsules, etc.)
hal/interrupts.py | CPU Interrupts specific functions (SMI, NMI)
hal/cmos.py | CMOS memory specific functions (dump, read/write)
hal/cpuid.py | CPUID information
hal/spi_descriptor.py | SPI Flash Descriptor binary parsing functionality

## Slide 31: HAL: Basic HW Access
Basic HAL primitives is a set of HAL components which provide access to basic HW resources which are used to access any other HW resources
Each basic HAL primitive has its own OS native functions (e.g. in kernel module) implementing access to corresponding HW resource specific to that OS
Basic HAL primitives are IO, MEM, MSR, MMIO, PCIE, CR, CPUID, etc.
All other HAL components are complex and can be implemented using the above set of basic HAL primitives
Basic primitives can be accessed through Chipset instance:
cs = chipsec.chipset.cs()
pci_devs = cs.pci.enumerate_devices()

## Slide 32: HAL Example: SPI Flash Memory Access
SPI Flash Memory Access is a HAL component which implements access to system SPI flash memory devices
Current SPI HAL implementation uses hardware sequencing access (which predefines SPI flash opcodes and can operate in descriptor mode only)
Exposes the following API:
    read_spi, write_spi, erase_spi_block – access to SPI flash
    get_SPI_regions – returns SPI flash regions
    get_SPI_Protected_Range – returns SPI flash protected ranges
    display_SPI_Flash_Descriptor – decodes SPI flash descriptor
Accessed through chipsec_util spi/decode commands

## Slide 33: HAL Example: CPU Configuration Access
SPI Flash Memory Access is a HAL components which implement access to CPU HW resources (MSR, descriptor tables, microcode updates, CPUID, CR, interrupts ..)
Provide the following API:
    msr.read_msr, msr.write_msr – access to CPU MSRs
    msr.get_IDTR, msr.get_GDTR – read IDT/GDT
    ucode.ucode_update_id – read microcode update ID
    cpuid.cpuid – read CPU CPUID
    interrupts.send_SMI_APMC – send SMI through port B2h
    cr.read_cr, cr.write_cr – access to CPU Control Registers
Accessed through chipsec_util spi/cr/ucode/cupid/smi/idt/gdt commands

## Slide 34: HAL Example: UEFI
UEFI HAL components implements functionality to work with UEFI interfaces and structures
    Dumping UEFI Variables at run-time through UEFI API
    Extracting UEFI Variables from NVRAM store in SPI memory dump
    Decoding certificates/hashes from UEFI variables
    Parsing UEFI Volumes with executables from SPI memory dump
    Extracting and decoding S3 resume boot script
Common UEFI API consumed by modules is exposed through chipsec.hal.uefi
UEFI functionality can be common for all UEFI based firmware or can depend on BIOS implementation or UEFI version
    Common UEFI functionality is in hal/uefi_common.py
    BIOS dependent UEFI functionality is in hal/uefi_platform.py
Accessed through chipsec_util uefi command

## Slide 35: Platform Configuration
Each platform (chipset, CPU, devices) has it’s own configuration defined by registers/ranges in I/O, MMIO, PCIe CFG, MSR spaces...
  The same register may be defined at different offsets, even in different places on different platforms
  The definition of the register may change (bits, masks ..)
  Definitions of I/O or MMIO ranges change (location, size ..)
  Each platform may have its own set of internal devices or controllers
We don’t want to re-write modules for every new platform
It would be nice to be able do this (regardless of where register is):
reg = read_register( “MY_REGISER” )
reg_field = read_register_field( “MY_REGISER”, “MY_FIELD” )
CHIPSEC does that using configuration described in XML files for each platform, or per-feature, or common (chipsec/cfg directory)
Look for these lines in the output:
[*] loading common platform config from ‘..\chipsec/cfg\common.xml'..
[*] loading 'hsw' platform config from ‘..\chipsec/cfg\hsw.xml'..

## Slide 36: Platform Configuration: IO, MMIO…
Internal PCIe devices (devices, controllers, interfaces ..)
<pci>
<device name='HOSTCTRL' bus=‘0x0' dev='0x0' fun='0x0'../>
Memory Mapped I/O ranges (BARs)
<mmio>
<bar name=‘SPIBAR'.. reg=‘0xF0‘ enable_bit=‘0‘ ../>
Legacy port I/O ranges (BARs)
<io>
<bar name=‘ABASE'.. reg=‘0x40‘ ../>
Memory ranges
<memory>
<range name=‘LEGACY‘ address=‘0x00‘ size=‘0x100000‘ ../>

## Slide 37: Platform Configuration: Registers
Configuration registers
<registers>
<register name='BC' type='pcicfg' desc='BIOS Control'>
<field name='BIOSWE' bit='0' />
<field name='BLE' bit='1' />
..
<field name='SMM_BWP' bit='5' />
</register>
<register name='HSFS' type='mmio'>
..
<field name='FLOCKDN' bit='15'/>
</register>
<register name='IA32_SMRR_PHYSMASK' type='msr'>
<field name='Valid' bit='11'/>
</register>
</registers>

## Slide 38: Platform Configuration: “Controls”
Controls are important hardware lock bits, hardware protection enables, etc.
<control name=‘FlashLock' register=‘HSFS' field=‘FLOCKDN'/>
Modules can read the value of controls on any platform by the name regardless of where this control is (which register)
flock = chipsec.chipset.get_control(self.cs, 'FlashLockDown')

## Slide 39: CHIPSEC Has Two Entry-Points
chipsec_main.py (module launcher)
    Runs modules/tools automatically in a “security regression suite” mode
    Runs only modules applicable to current platform
    chipsec_main.py [--type BIOS]
    Or individually via “--module” command-line option
    chipsec_main.py --module common.bios_wp
chipsec_util.py (manual utilities)
    Provides manual access to HW resources (io, mem, pci ..)
    Individual utility commands are in utilcmd/*_cmd.py
    chipsec_util.py spi dump spi.bin
    (e.g. spi util command is implemented in spi_cmd.py file)

## Slide 40: Useful Options
-a (--module_args): Specifies arguments to each module individually
-n (--no_driver): Tells CHIPSEC to not launch Windows kernel driver (in case module doesn’t need it)
-x (--xml):Outputs result in JUnit compatible XML form which may be useful to integrate in validation env.
-t (--module_type): Run only modules of a specific type. Examples: BIOS, SMM, SECUREBOOT, HWCONFIG
    New types may be defined in chipsec/module_common.py
-v (--verbose): Logs all output from HAL components, helpers, dumps buffers, logs exception back-traces, etc.

## Slide 41: The Meat: CHIPSEC Modules
Modules encapsulate the main functionality of CHIPSEC:
Tests for known vulnerabilities in firmware
Tests for insufficient or incorrectly configured hardware protections
Hardware/firmware-level security tools
  Fuzzing tools for firmware interfaces/formats
  Manual security checkers (e.g. TE checker, DMA dumper)
  Reside in modules/tools directory are not launched automatically (only through –m command-line option)
PoC exploit modules demonstrating vulnerabilities

## Slide 42: The Meat: CHIPSEC Modules
All modules reside in chipsec/modules directory
Modules can be specific to one or more platforms or common for all supported platforms
  Modules in modules/<platform_code> directory will only be executed on <platform_code> platform
  Modules in modules/common directory will always be executed
Modules can implement is_supported function which can further check for supported platforms, OS environments (legacy vs UEFI boot), etc.

## Slide 43: Raising the Bar for Platform Security
Security Research
Platform Validation
Risk Profile
New Attacks
Test Modules for OEMs/IBVs
End-user Risk
Empowering End-Users to Make a Risk Decision
Source: https://cansecwest.com/slides/2014/Platform%20Firmware%20Security%20Assessment%20wCHIPSEC-csw14-final.pdf

## Slide 44: Summary of Modules in CHIPSEC
Issue | CHIPSEC Module | References
SMRAM Locking | common.smm | CanSecWest 2006
BIOS Keyboard Buffer Sanitization | common.bios_kbrd_buffer | DEFCON 16
SMRR Configuration | common.smrr | ITL 2009, CanSecWest 2009
BIOS Protection | common.bios_wp | BlackHat USA 2009, CanSecWest 2013, Black Hat 2013, NoSuchCon 2013
SPI Controller Locking | common.spi_lock | Flashrom, Copernicus
BIOS Interface Locking | common.bios_ts | PoC 2007
Secure Boot variables with keys and configuration are protected | common.secureboot.variables | UEFI 2.4 Spec , All Your Boot Are Belong To Us (here & here)
Memory remapping attack | remap | Preventing and Detecting Xen Hypervisor Subversions
DMA attack against SMRAM | smm_dma | Programmed I/O accesses: a threat to VMM?, System Management Mode Design and Security Issues
SMI suppression attack | common.bios_smi | Setup for Failure: Defeating Secure Boot
Access permissions to SPI flash descriptor | common.spi_desc | Flashrom
Access permissions to UEFI variables defined in UEFI Spec | common.uefi.access_uefispec | UEFI 2.4 Spec
Module to detect PE/TE Header Confusion Vulnerability | tools.secureboot.te | All Your Boot Are Belong To Us
Module to detect SMI input pointer validation vulnerabilities | tool.smm.smm_ptr | CanSecWest 2015

## Slide 45: 3.3 Developing Modules in CHIPSEC

## Slide 46: Module template
from chipsec.module_common import *
_MODULE_NAME = 'module_template'
class module_template (BaseModule):
def __init__(self):
BaseModule.__init__(self)
def check_something( self ):
self.logger.start_test( "Module Template" )
self.logger.log_passed_check( "Test Passed" )
return ModuleResult.PASSED
def is_supported(self):
return False
# --------------------------------------------------------------------------
# run( module_argv )
# Required function: run here all tests from this module
# --------------------------------------------------------------------------
def run( self, module_argv ):
return self.check_something()
Module starts here.
Can pass arguments to each module
Check if this module can run on this platform/OS
Return result
FAILED
PASSED
WARNING
SKIPPED
DEPRECATED
ERROR
Inherits BaseModule template

## Slide 47: Example: common.spi_lock
from chipsec.module_common import *
TAGS = [MTAG_BIOS]
class spi_lock(BaseModule):
def __init__(self):
BaseModule.__init__(self)
def is_supported(self):
return (self.cs.get_chipset_id() in \
[chipsec.chipset.CHIPSET_FAMILY_CORE,chipsec.chipset.CHIPSET_FAMILY_XEON])
def check_spi_lock(self):
self.logger.start_test( "SPI Flash Controller Configuration Lock" )
spi_lock_res = ModuleResult.FAILED
hsfs_reg = chipsec.chipset.read_register( self.cs, 'HSFS' )
chipsec.chipset.print_register( self.cs, 'HSFS', hsfs_reg )
flockdn = chipsec.chipset.get_register_field( self.cs, 'HSFS', hsfs_reg, 'FLOCKDN' )
if 1 == flockdn:
spi_lock_res = ModuleResult.PASSED
self.logger.log_passed_check( "SPI Flash Controller configuration is locked" )
else:
self.logger.log_failed_check( "SPI Flash Controller configuration is not locked" )
return spi_lock_res
def run( self, module_argv ):
return self.check_spi_lock()
Type of the check (e.g. BIOS security)
Checks SPI controller configuration is locked down

## Slide 48: Logging
Output module’s result:
log_passed/failed/skipped/warn_check()
Various output modes:
log(),error(),warning(),log_bad(),log_good(), log_important()
Turning VERBOSE output mode. Verbose mode logs everything from HAL, OS helpers etc.
self.logger.VERBOSE = True
# chipsec_main.py -m common.spi_lock –-verbose
Turn on/off logging by HAL components
self.logger.HAL
Utility logging (ON by default when CHIPSEC_UTIL is used)
self.logger.UTIL_TRACE
Flushing log output to a file (what if a fuzzer crashes OS?)
self.logger.flush()
self.logger.set_always_flush( True )

## Slide 49: 3.4 Developing Fuzzers for the System Firmware

## Slide 50: Passing arguments to CHIPSEC modules
More complex modules (e.g. tools, fuzzers, PoCs..) may define module specific command-line arguments to be passed by CHIPSEC via “-a” option:
# chipsec_main -m tools.fuzzer –a rnd,1000,0xDEADBEEF
def run( module_argv ):
logger.start_test( “Some fuzzer" )
if len(module_argv) > 2:
_mode = module_argv[0]
_attempts = int(module_argv[1])
_address = int(module_argv[2],16)
fuzz( _mode, _attempts, _address )
return ModuleResult.PASSED

## Slide 51
Training materials are available on Github
https://github.com/advanced-threat-research/firmware-security-training
Yuriy Bulygin @c7zero
Alex Bazhaniuk @ABazhaniuk
Andrew Furtak @a_furtak
John Loucaides @JohnLoucaides