## Slide 1: Advanced x86: BIOS and System Management Mode Internals SPI Flash Programming
Xeno Kovah && Corey Kallenberg
LegbaCore, LLC

## Slide 2: All materials are licensed under a Creative Commons “Share Alike” license.
http://creativecommons.org/licenses/by-sa/3.0/
Attribution condition: You must indicate that derivative work
"Is derived from John Butterworth & Xeno Kovah’s ’Advanced Intel x86: BIOS and SMM’ class posted at http://opensecuritytraining.info/IntroBIOS.html”
Notes: Attribution condition: You must indicate that derivative work
"Is derived from John Butterworth & Xeno Kovah’s ’Advanced Intel x86: BIOS and SMM’ class posted at http://opensecuritytraining.info/IntroBIOS.html”

## Slide 3: SPI note:
We’re not really going to care about low level SPI protocol details
We’re just going to care about the way that it’s exposed to the BIOS, so that we can understand the BIOS’s view of the world, and therefore interpret its actions accordingly

## Slide 4: SPI (Serial Peripheral Interface) Flash
Intel provides a programmable interface to the SPI flash device
  System BIOS lives here
  Other stuff does too
Copernicus programs this interface to dump a binary of the SPI flash
Intel IO Controller Hub 10 Datasheet, page 31

## Slide 5: How you should think of reading & writing the flash chip
CPU
ICH or PCH
RAM
(“SPIBAR” = RCRB + X
MMIO to ICH or PCH)
Flash Chip
SPI
All you see/need to care about
Behind the scenes

## Slide 6: Programming the SPI Flash
RCBA holds RCRB
RCRB + X = SPIBAR
  (for X = 0x3800 on all newer systems, but not old ones)
SPIBAR + Y = flash programming registers
An app can choose either “Hardware Sequencing” (meaning the hardware picks the actual SPI commands that get sent for read/write) or Software Sequencing (meaning you pick the actual SPI commands)
  For simplicity of discussion, we’ll be referring to only those operations/details pertaining to Hardware Sequencing
    Software Sequencing just offers a little more fine-grain control
  All SPI registers in the following slides are from:
  http://www.intel.com/content/www/us/en/io/io-controller-hub-10-family-datasheet.html
You’re welcome!
Bwahahaha!

## Slide 7: Since I didn’t have anywhere better to put this…

## Slide 8: SPI Programming Flash Address Register
Specifies starting address of the SPI I/O cycle
  Flash address, not a system RAM address
  Valid range is 0 to <size of flash chip – 1>

## Slide 9: SPI Programming Data Registers
Contains the data we just read from the SPI flash (up to 64 bytes), or data we’re about to write to the flash chip
R/W (since it can be used to specify data to write to flash)
…

## Slide 10: SPI Programming Control Register
Set the type to read (bits 2:1 == 00b)

## Slide 11: SPI Programming Control Register
Initiates the SPI I/O cycle
  Used by programming app (Copernicus)
Defines the number of bits to read (or write) in the I/O cycle
Notes: Can paste in images from ICH datasheet and circle applicable bits

## Slide 12: SPI Programming Status Register
Indicates that an SPI I/O cycle is in progress
Set automatically by hardware, nothing we need to really care much about
Notes: Can paste in images from ICH datasheet and circle applicable bits

## Slide 13: SPI Programming Status Register 2
Indicates the SPI I/O cycle has completed
Software must poll on this bit to determine when the hardware is done reading/writing data
Notes: Can paste in images from ICH datasheet and circle applicable bits

## Slide 14: Reading the flash chip
BIOS reading software sets up the location it wants to read (as part of reading the entire chip) and how many bytes to read
FADDR=00000…
FDATA0=00000…
FDONE=0
SCIP=0
FCYCLE=0
FGO=0
FADDR = 0x1000, FCYCLE=00(read)
FDBC = 111111b (64 byte read)
Ring 0

## Slide 15: Reading the flash chip
BIOS reading software says to start the read
FADDR=0x1000
FDATA0=00000…
FDONE=0
SCIP=0
FCYCLE=0
FGO=0
HSFC |= 1 (aka FGO=1)
Ring 0

## Slide 16: Reading the flash chip
Cycle in progress
We need to poll on FDONE, waiting for it to be set to 1
FADDR=0x1000
FDATA0=00000…
FDONE=0
SCIP=1
FCYCLE=0
FGO=1
Ring 0

## Slide 17: Reading the flash chip
Once the cycle is done (FDONE=1) we can do read the FDATA registers
FADDR=0x1000
FDATA0=0xf005ba11
FDONE=1
SCIP=0
FCYCLE=0
FGO=0
Ring 0

## Slide 18: Reading the flash chip
BIOS reading software will get the contents out of the FDATA register(s) and store to memory and/or disk
FADDR=0x1000
FDATA0=0xf005ba11
FDONE=1
SCIP=0
FCYCLE=0
FGO=0
Read FDATA0
0xf005ba11
Ring 0

## Slide 19: Lab: RYOFC! (Read Your Own Flash Chip!)
We’re going to be cool and manually program the flash registers in RWE to read the reset vector from our flash chip
DISCLAIMER! DISCLAIMER! DISCLAIMER!
Don’t follow along unless you’re super careful! You could accidentally brick your system! :D
I am not responsible if you brick your system (or your enemies’ :P)
DISCLAIMER! DISCLAIMER! DISCLAIMER!

## Slide 20: Register Access: SPI Base Address Register (SPIBAR)
SPI extends it’s Base Address Registers (BARs) to memory starting at an address called SPIBAR
SPIBAR is offset from the Root Complex Register Block (RCRB)
The offset from RCRB is chipset-dependent, but will be listed in the SPI section of the datasheet
SPIBAR
Offset | Name | Value
F0h | RCBA | FED18000
LPC Device | B0:D31:F0
ICH or PCH
RCRB
SPIBAR
offset
memory
Notes: http://superradnow.files.wordpress.com/2012/09/spy.jpeg

## Slide 21: Lab: Locate SPIBAR
Per your datasheet, the SPI host interface registers (SPIBAR) is located at an offset from RCRB
In the Mobile 4-Series chipset on our lab laptop, SPIBAR is located at:
RCRB + 3800h = FED1_B800h
déjà vu!

## Slide 22: Back to “Fun things to do in SMM”!

## Slide 23: Attack 1 – Manipulate Copernicus output
From within the OS, targeted hooks into Copernicus code
From within the OS with “DDefy” [20] rootkit style hooks into file writing routines
From within the HD controller firmware [21][22][23]
From within the OS with a network packet filter driver
From within the NIC firmware [24][25]
Etc. Lots more options
From https://cansecwest.com/slides/2014/Copernicus2-SENTER_the-Dragon-CSW.pptx

## Slide 24: Attack 2 – A new generic attack.
It is possible for SMM to be notified when SPI reads or writes occur
An attacker who controls the BIOS controls the setup of SMM
In this way a BIOS-infecting attacker can perform a SMM MitM attack against those who would try to read the BIOS to integrity check it
We call our SMM MitM “Smite’em, the Stealthy”
Notes: http://www.creativeuncut.com/gallery-11/gw2-dragon-eye.html

## Slide 25: Eye of the dragon - FSMIE - hw sequencing
This is what allows an attacker in SMM to know when someone is trying to access the flash chip
The Flash Cycle Done bit is set to 1 after every read and write

## Slide 26: Reading the flash chip in the presence of Smite'em
BIOS reading software sets up the location it wants to read (as part of reading the entire chip) and how many bytes to read
FADDR=00000…
FDATA0=00000…
FDONE=0
SCIP=0
FCYCLE=0
FGO=0
FSMIE=1(already set)
SMM
Smite'em
FADDR = 0x1000, FCYCLE=00(read)
FDBC = 111111b (64 byte read)
Ring 0

## Slide 27: Reading the flash chip in the presence of Smite'em
BIOS reading software says to start the read
FADDR=0x1000
FDATA0=00000…
FDONE=0
SCIP=0
FCYCLE=0
FGO=0
FSMIE=1
SMM
Smite'em
HSFC |= 1 (aka FGO=1)
Ring 0

## Slide 28: Reading the flash chip in the presence of Smite'em
Cycle in progress
FADDR=0x1000
FDATA0=00000…
FDONE=0
SCIP=1
FCYCLE=0
FGO=1
FSMIE=1
SMM
Smite'em
Ring 0

## Slide 29: Reading the flash chip in the presence of Smite'em
Once the cycle is done, and the data is available for reading, if the FSMIE = 1, an SMI is triggered, giving Smite'em the first look
FADDR=0x1000
FDATA0=0x1badd00d
FDONE=1
SCIP=0
FCYCLE=0
FGO=0
FSMIE=1
SMM
Smite'em
SMI
Ring 0

## Slide 30: Reading the flash chip in the presence of Smite'em
Smite'em can change any data that would reveal its presence to the original benign data
FADDR=0x1000
FDATA0=0x1badd00d
FDONE=1
SCIP=0
FCYCLE=0
FGO=0
FSMIE=1
SMM
Smite'em
FDATA0=0xf005ba11
Ring 0

## Slide 31: Reading the flash chip in the presence of Smite'em
BIOS reading software will be misled!
FADDR=0x1000
FDATA0=0xf005ba11
FDONE=1
SCIP=0
FCYCLE=0
FGO=0
FSMIE=1
SMM
Smite'em
Read FDATA0
0xf005ba11
Ring 0

## Slide 32: Think it can't happen?
Flashrom 0.9.7 source
If you don't account for hw/sw sequencing's FSMIE bit (as no previous software did), you will just lose and provide false assurances of a lack of BIOS compromise

## Slide 33: What you don't know can bite you
The basic solution would seem to be just for querying tools to set FSMIE = 0 before trying to read
Multiple ways for an adversary to counter
  Kernel agent continuously setting FSMIE = 1
    So you just clear it and check if it's getting re-set, and if so…?
  VMX interception of MMIO to SPI space, falsifying that you successfully cleared FSMIE
    But then if they're using VMX too, they can also just directly forge FDATA
  Target your security software specifically
    If your tool is good enough to detect attacker, he's incentivized to go after you specifically

## Slide 34: Terror at 35,000 feet (high level overview) Another attack…
Let's assume that Smite'em wants to pick another generic, low-effort way to avoid detection (i.e. doesn't want to use VMX until absolutely necessary)
Smite'em recruits a Dragon Knight avatar
  Could be kernel-based code or a DMA device and independent of CPU
Avatar polls SPI configuration registers to detect if an SPI cycle is in progress
Upon detecting an SPI cycle in progress, the avatar triggers an SMI
Smite’em running in SMM has exclusive access to the CPU, and can stall until the cycle completes and then replace the data read from flash before Copernicus can read it

## Slide 35: Reading the flash chip in the presence of Smite'em
Copernicus sets up the location it wants to read (as part of reading the entire chip) and how many bytes to read
FADDR=00000…
FDATA0=00000…
FDONE=0
SCIP=0
FCYCLE=0
FGO=0
FSMIE=0
SMM
Smite'em
FADDR = 0x1000, FCYCLE=00(read)
FDBC = 111111b (64 byte read)
Ring 0

## Slide 36: Reading the flash chip in the presence of Smite'em
Then says go
FADDR=0x1000
FDATA0=00000…
FDONE=0
SCIP=0
FCYCLE=0
FGO=0
FSMIE=0
SMM
Smite'em
FGO=1
Ring 0

## Slide 37: Reading the flash chip in the presence of Smite'em
Copernicus sets up the location it wants to read (as part of reading the entire chip) and how many
FADDR=0x1000
FDATA0=00000…
FDONE=0
SCIP=1
FCYCLE=0
FGO=1
FSMIE=0
SMM
Smite'em
Poll for SCIP=1 and once found
poll faster for FDONE=1
Ring 0

## Slide 38: Reading the flash chip in the presence of Smite'em
Once it sees the data, it tries not to race with Copernicus, but instead stops itself and Copernicus by signaling Smite'em with an SMI
FADDR=0x1000
FDATA0=0x1badd00d
FDONE=1
SCIP=0
FCYCLE=0
FGO=0
FSMIE=0
SMM
Smite'em
SMI
Ring 0

## Slide 39: Reading the flash chip in the presence of Smite'em
Smite'em then cleans up as usual
FADDR=0x1000
FDATA0=0x1badd00d
FDONE=1
SCIP=0
FCYCLE=0
FGO=0
FSMIE=0
SMM
Smite'em
FDATA0=0xf005ba11
Ring 0
Notes: http://th04.deviantart.net/fs71/PRE/f/2012/220/9/6/dragon_knight_by_nickhuddlestonartist-d58112b.png

## Slide 40: Better luck next time?
We then implemented a basic “Copernicus 2” that used Intel TXT to try and defeat this
  We care about trustworthy detection tools. It’s no good to have detection tools if your attacker can easily bypass them and give you a false sense of trust that your system is clean
    But we know that we have to start somewhere
We thought it would work because the manuals implied that TXT automatically suppresses SMIs until they’re explicitly turned back on
  It turned out that it does on *old* hardware, but newer hardware turns on SMIs automatically, so our TXT code is back to being vulnerable to SMM subversion until STMs are available
    That’s part of why we want STMs so much
  :’(
  TT
Our only consolation is that Copernicus 2 *does* take OS level attackers off the table…But really if we’re trying to detect BIOS level attackers, we need to counter SMM in order for it to matter

## Slide 41: Coming soon?(ever?)
“Copernicus 3” would take our existing research on “timing-based attestation” and port it into TXT-land
Unfortunately since I said that idea while I was at MITRE, even though I didn’t implement it, probably MITRE owns the idea and I can’t do it without their permission/cooperation :-/
So for today, your only option is…

## Slide 42
Trustworthy BIOS malware detection!
(note: doesn’t measure SMM :))
Notes: This is the best possible case, where the BIOS is exposed for easy reflash.