## Slide 1: Security of BIOS/UEFI System Firmware from Attacker and Defender Perspectives Introduction
Yuriy Bulygin *
Alex Bazhaniuk *
Andrew Furtak *
John Loucaides **
* Advanced Threat Research, McAfee
** Intel

## Slide 2: License
Training materials are shared under Creative Commons “Attribution” license CC BY 4.0
Provide the following attribution:
Derived from “Security of BIOS/UEFI System Firmware from Attacker and Defender Perspective” training by Yuriy Bulygin, Alex Bazhaniuk, Andrew Furtak and John Loucaides available at https://github.com/advanced-threat-research/firmware-security-training

## Slide 3
CPU 0 Haswell EP –EP (Socket R3)
CPU 1 Haswell EP –EP (Socket R3)
PCH Wellsburg C612
ASpeed AST2400 / AST1400
Mini SAS HD
PCI Express x8
OCP SLOT2 X8
OCP SLOT1 X8
PCI Express x8
Intel i350 Gb Lan
TPM / Debug Header
DDR3 Frame Buffer Memory
Smart Fan Controller
COM Port
MINI SAS0
USB 3.0
D-Sub Connector
RJ45
RJ45
LPC
PCIE Gen2
UART
RGB
PWM
DDR III
NC SI Interface
USB2.0*3/3.0*4
PCIE Gen2 x4
PCIE Gen3 x8
PCIE Gen3 x8
PCIE Gen3 x8
PCIE Gen3 x8
PCIE Gen3 x4
PCIE Gen3 x4
PCIE Gen3 x4
PCIE Gen3 x4
Mini SAS HD
Mini SAS HD
Mini SAS HD
SATA (6.0Gb/s)*4
SATA (6.0Gb/s)*6
SATA4
MINI S1SA
SATA5
Rear
Front
USB 3.0
USB 2.0
USB 2.0
USB 3.0
USB 3.0
USB 2.0
DMI Gen2 x4
4GB/S
FW
FW
FW
FW
FW
FW
FW
FW
FW
DDR4 channel A
DDR4 channel B
DDR4 channel C
DDR4 channel D
DDR4 channel E
DDR4 channel F
DDR4 channel G
DDR4 channel H
QPI
Port 0
(9.6GT/s)
QPI
Port 1
(9.6GT/s)
RDIMM / LRDIMM
1600/1866/2133 MHz
RDIMM / LRDIMM
1600/1866/2133 MHz
RDIMM / LRDIMM
1600/1866/2133 MHz
RDIMM / LRDIMM
1600/1866/2133 MHz
RDIMM / LRDIMM
1600/1866/2133 MHz
RDIMM / LRDIMM
1600/1866/2133 MHz
RDIMM / LRDIMM
1600/1866/2133 MHz
RDIMM / LRDIMM
1600/1866/2133 MHz
FW

## Slide 4: Firmware Everywhere
  GBe NIC, WiFi, Bluetooth, WiGig
  Baseband (3G, LTE) Modems
  Sensor Hubs
  NFC, GPS Controllers
  HDD/SSD
  Keyboard and Embedded Controllers
  Battery Gauge
  Baseboard Management Controllers (BMC)
  Graphics/Video
  USB Thumb Drives, keyboards/mice
  Chargers, adapters
  TPM, security coprocessors
  Routers, network appliances
  Main system firmware (BIOS, UEFI firmware, coreboot)

## Slide 5: In-the-wild Firmware Attacks
  Legacy Bootkits (TDL4, Gapz…)
  Mebromi BIOS rootkit
  Stuxnet
  EQUATION Group HDD firmware malware
  ] Hacking Team [ UEFI rootkit
  Petya MBR Ransomware
  Legitimate BIOS “backdoors”: Superfish, Computrace

## Slide 6: Why Attack Firmware?
  Extreme persistence
  Stealth
  Bypass software (OS or VMM) based security
  Unfettered access to hardware
  OS independence
  Making the system unbootable (bricking)

## Slide 7: Extreme Persistence
  System firmware rootkit (in SMM or BIOS/UEFI)
  Replaces OS boot loader every boot
  Which patches OS kernel
  Firmware rootkit is protected by the hardware write protections
  Only way to fully remove the infection is to physically re-flash the flash “ROM” chip

## Slide 9: Stealth
  Security software usually doesn’t monitor all firmware on the platform
  How can software reliably tell infected from good firmware
  Devices use obscure hardware interfaces to their firmware
  Which tool do we use to find BIOS/UEFI infection? And rootkit in firmware of SSD, NIC, EC, BMC, modem, USB thumb-drive, battery gauge, charger?

## Slide 10: Bypass Software Security – FDE
Source: Evil Maid Just Got Angrier: Why Full-Disk Encryption with TPM is not Secure on Many Systems

## Slide 11: Bypass Software Security – Secure Boot
Source: A Tale of One Software Bypass of Windows 8 Secure Boot

## Slide 12: Bypass Software Security - VMM
Source: Attacking Hypervisors via Firmware and Hardware

## Slide 13: Unfettered Access to Hardware - DRAM
Reference: I/O Attacks in Intel-PC Architecture and Countermeasures by F. Lone Sang et al
CPU Skt
PCH
PCI Express
PCI Express
Gbe NIC
PCIE Gen2
PCIE Gen3
PCIE Gen3
DMI
DDR4 channel A
DDR4 channel B
DRAM
SW
Attacks compromising firmware on peripheral I/O devices can use inbound direct memory access (DMA) to expose sensitive contents in DRAM or modify software directly in DRAM

## Slide 14: Unfettered Access to Hardware – HDD/SSD
Access to all data stored on HDD/SDD
Even when data is stored on self-encrypting drives (SED)
Example: Equation Group HDD firmware malware
Destroying your hard driver is the only way to stop this super-advanced malware

## Slide 15: Unfettered Access to Hardware
NIC, WiFi, baseband modem firmware rootkits have direct access to network communications
EC or BMC firmware rootkit has access to platform management functions (power, thermal, NIC, keystrokes)
…

## Slide 16: Making System Unbootable (Bricking)
Corrupt firmware or
Corrupt critical configuration
Stored in flash “ROM” memory
Of a device which is critical for system to boot or operate

## Slide 17: References

## Slide 18: UEFI/BIOS Security
Security Issues Related to Pentium System Management Mode (CSW 2006)
Implementing and Detecting an ACPI BIOS Rootkit (BlackHat EU 2006)
Implementing and Detecting a PCI Rootkit (BlackHat DC 2007)
Programmed I/O accesses: a threat to Virtual Machine Monitors? (PacSec 2007)
Hacking the Extensible Firmware Interface (BlackHat USA 2007)
BIOS Boot Hijacking And VMWare Vulnerabilities Digging (PoC 2007)
Bypassing pre-boot authentication passwords (DEF CON 16)
Using SMM for "Other Purposes“ (Phrack65)
Persistent BIOS Infection (Phrack66)
A New Breed of Malware: The SMM Rootkit (BlackHat USA 2008)
Preventing & Detecting Xen Hypervisor Subversions (BlackHat USA 2008)
A Real SMM Rootkit: Reversing and Hooking BIOS SMI Handlers (Phrack66)
Attacking Intel BIOS (BlackHat USA 2009)
Getting Into the SMRAM: SMM Reloaded (CSW 2009, CSW 2009)
Attacking SMM Memory via Intel Cache Poisoning (ITL 2009)
BIOS SMM Privilege Escalation Vulnerabilities (bugtraq 2009)
System Management Mode Design and Security Issues (IT Defense 2010)
Analysis of building blocks and attack vectors associated with UEFI (SANS Institute)
(U)EFI Bootkits (BlackHat USA 2012 @snare, SaferBytes 2012 Andrea Allievi, HITB 2013)
Evil Maid Just Got Angrier (CSW 2013)
A Tale of One Software Bypass of Windows 8 Secure Boot (BlackHat USA 2013)
BIOS Chronomancy (NoSuchCon 2013, BlackHat USA 2013, Hack.lu 2013)
Defeating Signed BIOS Enforcement (PacSec 2013, Ekoparty 2013)
UEFI and PCI BootKit (PacSec 2013)
Meet ‘badBIOS’ the mysterious Mac and PC malware that jumps airgaps (#badBios)
All Your Boot Are Belong To Us (CanSecWest 2014 Intel and MITRE)
Setup for Failure: Defeating Secure Boot (Syscan 2014)
Setup for Failure: More Ways to Defeat Secure Boot (HITB 2014)
Analytics, and Scalability, and UEFI Exploitation (INFILTRATE 2014)
PC Firmware Attacks, Copernicus and You (AusCERT 2014)
Thunderstrike (https://trmm.net/Thunderstrike)
Extreme Privilege Escalation (BlackHat USA 2014)
Attacks on UEFI Security (31C3)
A new class of vulnerabilities in SMI Handlers (CanSecWest 2015)
Attacking and Defending BIOS in 2015 (RECon 2015)
Exploiting UEFI boot script table vulnerability (My aimful life)
Technical details of the S3 resume boot script vulnerability (ATR)
How you Mac firmware security is completely broken (reverse.put.as)
Building reliable SMM backdoor for UEFI based systems (My aimful life)
Breaking UEFI security with software DMA attacks (My aimful life)
Attacking Hypervisors Using Firmware and Hardware (Black Hat USA 2015)
Exploiting SMM Callout Vulnerabilities in Lenovo firmware (My aimful life)

## Slide 19: Other Firmware Security
  CPU/SoC
    ITL papers (website)
    AMD x86 SMU firmware analysis (https://events.ccc.de/congress/2014/Fahrplan/system/attachments/2503/original/ccc-final.pdf) by Rudolf Marek
    The Memory Sinkhole (https://www.blackhat.com/docs/us-15/materials/us-15-Domas-The-Memory-Sinkhole-Unleashing-An-x86-Design-Flaw-Allowing-Universal-Privilege-Escalation.pdf) by Christopher Domas
    Full TrustZone Exploit for MSM8974 (http://bits-please.blogspot.com/2015/08/full-trustzone-exploit-for-msm8974.html?m=1)
    QSEE privilege escalation vulnerability CVE-2015-6639 (http://bits-please.blogspot.com/2016/05/qsee-privilege-escalation-vulnerability.html?m=1)
  USB
    Turning USB Peripheral to BadUSB (https://srlabs.de/badusb/)
    Practical BadUSB attack software (https://github.com/adamcaudill/Psychson)
  DRAM
    Cold Boot attacks (https://citp.princeton.edu/research/memory/)
    Exploiting the DRAM rowhammer bug (http://googleprojectzero.blogspot.com/2015/03/exploiting-dram-rowhammer-bug-to-gain.html?m=1)
  Battery
    Battery Firmware Hacking (https://reverse.put.as/wp-content/uploads/2011/06/Battery-Firmware-Hacking.pdf) by Charlie Miller
  NIC
    NIC SSH Rootkit (http://cryptome.org/2014/02/nic-ssh-rootkit.htm) by Arrigo Triulzi
    Project Maux Mk.II (http://www.alchemistowl.org/arrigo/Papers/Arrigo-Triulzi-PACSEC08-Project-Maux-II.pdf) by Arrigo Triulzi
  Management Controllers
    IPMI: Freight Train to Hell (http://fish2.com/ipmi/bp.pdf) by Dan Farmer
    Sticky finger and KBC custom shop (http://esec-lab.sogeti.com/static/publications/11-recon-stickyfingers_slides.pdf) by Alexandre Gazet
    Illuminating the security issues surrounding Lights-Out server management (https://jhalderm.com/pub/papers/ipmi-woot13.pdf)

## Slide 20
Training materials are available on Github
https://github.com/advanced-threat-research/firmware-security-training
Yuriy Bulygin @c7zero
Alex Bazhaniuk @ABazhaniuk
Andrew Furtak @a_furtak
John Loucaides @JohnLoucaides

## Slide 21: Security of BIOS/UEFI System Firmware from Attacker and Defender Perspectives Section 1. BIOS and UEFI Firmware Fundamentals
Yuriy Bulygin *
Alex Bazhaniuk *
Andrew Furtak *
John Loucaides **
* Advanced Threat Research, McAfee
** Intel

## Slide 22: License
Training materials are shared under Creative Commons “Attribution” license CC BY 4.0
Provide the following attribution:
Derived from “Security of BIOS/UEFI System Firmware from Attacker and Defender Perspective” training by Yuriy Bulygin, Alex Bazhaniuk, Andrew Furtak and John Loucaides available at https://github.com/advanced-threat-research/firmware-security-training

## Slide 23: Section 1. BIOS and UEFI Firmware Fundamentals

## Slide 24: 1.1 Introduction to Platform Hardware

## Slide 25: Main PC Platform Components
Source: 4th Generation Intel Core Processor Family Datasheet

## Slide 26: PCI Express Overview
PCI Express Fabric consists of PCIe components connected over PCIe interconnect in a certain topology (e.g. hierarchy)
Root Complex is a root component in a hierarchical PCIe topology with one or more PCIe root ports
Components: Endpoints (I/O Devices), Switches, PCIe-to-PCI/PCI-X Bridges
All components are interconnect via PCI Express Links
Physical components can have up to 8 physical or virtual functions
Some endpoints are integrated into Root Complex

## Slide 27: PCI Express Overview
Reference: https://www.mindshare.com/files/ebooks/PCI%20Express%20System%20Architecture.pdf
CPU
DRAM
Root Complex
PCI Express Endpoint
PCI Express to PCI/PCI-X Bridge
Legacy Endpoint
Legacy Endpoint
PCI Express Endpoint
PCI Express Endpoint
Switch
PCI/PCI-X
PCI Express
PCI Express
PCI Express
PCI Express
PCI Express

## Slide 28: PCIe Configuration Space Layout
Each function has its own configuration (256 bytes of PCI config space and 4kB of PCIe extended config space)
Reference: PCI Express Base Specification Revision 3.0
0
3Fh
FFh
FFFh
PCI Express Extended Configuration Space (Not available for legacy operating system)
PCI Configuration Space (Available on legacy OS through legacy PCI mechanisms)
Extended configuration space for PCI Express parameters and capabilities (Not available on legacy OS)
PCI Express Capability Structure
Capability needed by BIOS or by driver software on non PCI Express aware OS
PCI 3.0 Compatible Configuration Space Header

## Slide 29: PCIe Configuration Space Access
SW uses one these mechanisms to access config space:
Legacy configuration access via control CF8h & data CFCh processor I/O ports
    PCI config register address
    bus << 16 | device << 11 | function << 8 | offset & ~3
    CF8h  1<<31 | bdf_address
    Read data from or write data to port (CFCh + off[1:0])
Enhanced configuration access mechanism (ECAM) to PCIe extended configuration registers
100h bytes of CFG header
8 * 100h per device
32* 8 * 100h per bus

## Slide 30: Low Pin Count (LPC) Interface
LPC specification
Substitutes Industry Standard Architecture (ISA) X-bus
7 required signals (LAD3-0,LFRAME,LRESET,LCLK), 6 optional
33 MHz PCI compatible host controller driven clock
LPC controller is integrated into PCH or ICH
Host decodes IO or MMIO cycles on PCI to LPC cycles:
    Memory Rd/Wr
    I/O Rd/Wr
    DMA Rd/Wr (via Intel 8237 DMA controller)
    Bus Master Memory Rd/Wr
    Bus Master I/O Rd/Wr
    Firmware Memory Rd/Wr

## Slide 31: Low Pin Count (LPC) Interface
Firmware Hub: legacy Boot ROM (BIOS)
Discrete Trusted Platform Module (TPM)
    MMIO 0xFED4xxxx
Super I/O (Floppy Disk Controller, PS/2 KBC, serial and parallel ports)
    KB IO 60h/64h
    FDD IO 3F0h-3F7h …
    SP IO 3F8h-3FFh …
    PP IO 378h-37Fh …
Embedded Controller
    IO 62h/66h
Audio, AC’97, MIDI…
Reference: LPC specification
Super I/O
KBC, PP, SP, FDC
Host
Flash
BIOS
Embedded Controller
ISA (optional)
PCI/Host Bus

## Slide 32: Serial Peripheral Interface (SPI)
4-pin synchronous serial interface
    SCLK, MOSI, MISO, CSn/SSn (1 per slave device); optional IOx signals for fast read modes
    Master - Slave protocol: 1 master, N slaves
    Lower cost for system flash (BIOS) than FWH on LPC
SPI Controller is in PCH or ICH
    Supports JEDEC Serial Flash Discoverable Parameter (SFDP) to query capabilities of SPI flash device
    Boot BIOS straps (BBS) define if firmware is in LPC or SPI
SPI peripherals: sensors, serial NOR flash memory, MMC/SD...
Devices connected to SPI bus in chipset:
    Flash Memory Devices
    TPM over SPI (CS2#) on newer systems

## Slide 33: Chipset SPI Controller
PCH supports 3 SPI flash devices up to 16MB each
Descriptor and non-descriptor Modes
    CS0# must be flash memory device with a valid Flash Descriptor (FD)
    Descriptor mode is required on PCH based platforms
    Flash descriptor describes contents of the flash memory
Hardware and Software Sequencing operational modes
    Hardware sequencing preprograms SPI bus cycles and CS0#
    Software sequencing allows software to choose SPI cycles and CS

## Slide 34: System Flash Memory
Direct Access (e.g. FFFFFFFFh PA mapped to SPI direct read cycle), Program Register Access (SW programs Flash Linear Address to SPI MMIO registers)
For multiple masters SPI flash should support HW seq
FLA FFFFFFh maps to the top of Flash device
Erase cycles set all Fs: 0  1
In descriptor mode, SPI flash memory devices contain multiple ranges
Reference:
Intel 7 Series Chipset PCH datasheet
Region | Content
0 | Flash Descriptor
1 | BIOS
2 | Intel Management Engine
3 | Gigabit Ethernet
4 | Platform Data

## Slide 35: SPI Flash Descriptor
Region 0 at FLA 0 – FFFh (4 KB)
Signature: 0FF0A55Ah at 10h LBA
Contains the following sections:
    Component: flash device configuration
    Region: describes other regions
    Master: defines Rd/Wr Access Control table
    CPU and PCH soft straps
    ME VSCC Table: JEDEC ID & VSCC info
    OEM: reserved for OEM use
Access Control table defines which masters (CPU, ME, GbE) can access regions (FD has to be write-protected)
Reference: Intel 7 Series Chipset PCH datasheet
Signature
Descriptor MAP
Component
Region
Master
PCH Soft Straps
Reserved
Management Engine VSCC Table
Descriptor Upper MAP
OEM Section
10h
4KB

## Slide 36: System Flash Security
Chipset (SPI controller) based protections
  SMM based BIOS Write Protection: write-protects entire BIOS region from software other than SMI handler firmware executing in SMM
  SPI Protected Range registers (PR0-PR4): read/write protection of SPI flash regions based on FLA for program register access
  Flash Descriptor based access control: defines read/write access to each flash region by each master
Firmware may use SPI flash chips write protection (WP#)

## Slide 37: System Management Bus (SMBus)
SMBus 2.0 specification
2-pin interface (SMBDATA, SMBCLK), opt. SMBALERT#
SMBus host controller to communicate over SMBus:
    DIMM Serial Presence Detect (SPD) EEPROM
    DIMM Thermal Sensors
    EC or BMC (host-to-uC, uC-to-sensors, BMC-to-NIC)
    Commands: Read/Write Byte/Word, Send/Receive Byte, Process Call..
    Can operate in I2C mode
Intel ME has SMBus controller(s)
PCIe connectors include SMBus pins for side band management
DMTF Alert Standard Format (ASF) sensors
PMBus for power supplies

## Slide 38: Where is system firmware?
SMM / BIOS
CPU
App
OS
App
VM
App
OS
App
VM
VMM / Hypervisor
Memory
Peripherals
Firmware
Hardware
Platform
Privilege
System firmware (BIOS/SMM, EFI) & OS/VMM share access, but not trust
Hypervisor can grant VM direct hardware access
DMA
A specific Peripheral may have its own processor, and its own firmware, which is undetectable by host CPU/OS.
Source: Symbolic execution for BIOS security

## Slide 39: Hardware Boot Sequence
External power supplied (e.g. 12V) to the system and settles
Power is driven in a sequence to multiple processor and chipset voltage rails
Platform clocks are derived from external clock and oscillators
Processor reset signal is de-asserted
Power management logic in the CPU executes reset sequence (samples fuses, handshake with the PCH, reads Power-On configuration etc.)
Power management logic brings cores out of reset
Processor cores execute reset microcode (initializes x86 state, parses FW interface table, etc.)
Finally, reset microcode fetches the first instruction at physical address FFFFFFF0h known as reset vector

## Slide 40: x86 Reset Vector
CPU starts in Real-Address Mode (or Real Mode)
    CS = F000h, CS limit = FFFFh, EIP = FFF0h
    So reset vector should be at F000:FFF0 = (F000h << 4) + FFF0h = 000FFFF0h
In 8086 BIOS ROM was mapped under 1MB. Now CPU/chipset map larger BIOS ROM under 4GB (FFFFFFFFh)
CPU asserts upper 12 address bits high by programming reset value of CS descriptor cache CS base to FFFF0000h
So reset vector is CS base + EIP = FFFF0000h + FFF0h = FFFFFFF0h
Until firmware executes FAR JMP to reload CS with F000h to stay in real mode under 1MB or enter protected mode early

## Slide 41: Reset Vector Decode
CPU decodes addresses FFFxxxxxh down to system bus (DMI) to chipset
Chipset decoded memory reads to SPI flash controller (or Firmware Hub) per configurable decoding rules
Memory reads are claimed by SPI flash controller which sends them as direct SPI read cycle to FFFFF0h flash address (FLA)
This ensures that memory reads (i.e. reset vector code fetch) to mapped BIOS ROM range are directed to firmware ROM (e.g. SPI flash memory device)

## Slide 42: x86 Reset Vector Example
Reset vector: near jump to the rest of the BIOS Boot Block
NOP
NOP
JMP SHORT Rel16 ; EarlyBSPInit or SEC entry-point

## Slide 43: Firmware Start
CPU start executing system firmware code at reset vector which is mapped to firmware ROM
Reset vector contains a jump to the initial firmware known as [Initial] Boot Block
Boot block consists of most of the early platform initialization functionality (SEC and PEI phases for UEFI based firmware)
Boot block executes early pre-memory initialization code, and memory initialization code (Memory Reference Code)

## Slide 44: Firmware Boot Sequence – Early Boot
Firmware in multiprocessor system chooses Bootstrap Processor (BSP). Other processors are in Wait-For-SIPI
Firmware on BSP initializes BSP CPU
    Loads early CPU microcode update on BSP
    Initializes Local APIC
    Ensure all APs are in Wait-For-SIPI or broadcast INIT IPI
    Initializes IDT/GDT and switches to flat 32-bit protected mode (CR0.PE)
    Configure fixed and variable memory types (MTRR)
    Enable cache on BSP (CR0.CD/CR0.NW)
    Enable No-Evict Mode (NEM) to set up Cache-As-RAM (CAR) for stack and code
    Initialize basic chipset interfaces (Root Complex, SMBus controller, MMCFG…)

## Slide 45: Firmware Boot Sequence – DRAM Init
FW performs SoC specific DRAM initialization (MRC)
    Read DIMM parameters from SPD EEPROM over SMBus
    Trains DDR busses
    Initializes memory controller
    Initializes memory map, stolen ranges
Memory shadowing: FW Copies the rest of the firmware to DRAM
    Decompression code decompresses FV from SPI flash and copies below 1MB
    Exit CAR mode and transition to shadowed code in DRAM
    Modify Programmable Attribute Map (PAM) registers to decode to DRAM

## Slide 46: Firmware Boot Sequence – DRAM Init
Wake other processors (APs)
    APs will execute wake-up init code
SMRAM Init
    BSP copies SMM relocation handler at 0x30000p
    Allocates TSEG and copies run-time SMI handler
    Sends SMI to relocate SMI handler to TSEG
    SMM relocation handler will configure SMRR
Continue with chipset initialization (DXE for UEFI)
    USB, SATA …
Enumerate and initialize PCI devices
    PCI devices enumeration
    Allocate MMIO spaces for device MMIO BARs
    Load and execute PCI Expansion/Option ROMs

## Slide 47: Memory Map: System View
Low DRAM
Memory vs MMIO
Low MMIO
4GB boundary
High DRAM
High MMIO
Top of Low DRAM
Low MMIO
Top of High DRAM
4GB
BAR 1 – BAR n
ECAM
Reference: 4th Gen Intel Core Processor Family Datasheet
High MMIO

## Slide 48: Memory Map (Below 4GB)
Legacy Ranges (PAMx)
ISA Hole
SMRAM
Graphics Stolen Memory
Low DRAM (TOLUD)
Memory vs MMIO
PCIe MMCFG
MMIO BARs
Reserved Ranges (APIC, TPM, TXT)
High BIOS
Reference: 4th Gen Intel Core Processor Family Datasheet
Low DRAM
SMM Memory
Low MMIO (PCI memory range)
Direct-mapped BIOS, APIC, TPM
TOLUD
4GB
BAR 1 – BAR n
ECAM
Low DRAM
OS invisible
Reclaim
Memory area
SMM Memory
Graphics Stolen
& GTT Memory
TSEG
BGSM
Legacy Memory
1 MB
0
System View
Memory Controller View

## Slide 49: Memory Map (Above 4GB)
Memory Reclaim
High DRAM (TOUUD)
ME Stolen Range
Top Of Memory
Reference: 4th Gen Intel Core Processor Family Datasheet
4GB
OS invisible
Reclaim
Memory area
High MMIO
High DRAM
High DRAM
ME Stolen Mmeory
REMAP BASE
TOM
TOUUD
OS invisible
Reclaim
Memory area
MESEG
System View
Memory Controller View

## Slide 50: 1.2 Platform Firmware: BIOS

## Slide 52: Legacy BIOS
The Basic Input / Output System (BIOS) is the software embedded on a ROM chip (SPI flash memory devices) located on the computer’s main board
The BIOS is fetched by the processor at reset vector address (FFFFFFF0h) and executes Power-On Self Test (POST) to test and initialize the system components, initializes add-on devices and then boots the OS.
The BIOS also handles the low-level input/output to the various peripheral devices connected to the computer
Plug and Play BIOS Specification

## Slide 53: Legacy BIOS Stages
CPU Reset vector in BIOS ’ROM’ (Boot Block) 
Boot Block
Basic CPU, chipset initialization 
Initialize CAR, load and run from cache 
Initialize DRAM memory 
POST (Power-On Self Test)
Decompress and relocate system BIOS in DRAM 
Enumerate add-on devices (ISA, PCI).. 
Execute Option ROMs on expansion cards 
INT 19h
Locate, load and execute Initial Boot Loader code in MBR (at 0x7C00 PA) 
2nd Stage Boot Loader  OS Loader  OS kernel
Also Technical Note: UEFI BIOS vs. Legacy BIOS, Advantech

## Slide 54: Legacy Option ROMs
Legacy option ROMs are BIOS extensions required to initialize add-on devices (ISA, PCI, PCIe) not supported by the system BIOS nor required to boot the system
Option ROMs are detected by the BIOS during after POST and their entry points are called
    Scanned in physical memory between addresses C0000h and F0000h and detected by 0x55 0xAA signature
During initialization, an Option ROM may hook any IVT vectors and update any data structures required for it to access attached devices and perform the necessary identifications and initializations
BIOS Boot Specification

## Slide 55: 1.3 Platform Firmware: (U)EFI Firmware

## Slide 56: Industry Transition
Pre-2000
All Platforms BIOS were proprietary
2000
Intel invented the Extensible Firmware Interface (EFI) and provided sample implementation under free BSD terms
tianocore.org, open source EFI community launched
2004
Unified EFI (UEFI)
Industry forum, with 11 members, was formed to standardize EFI
2005
240 members
Major MNCs shipping; UEFI platforms crossed most of IA worldwide units; Microsoft* UEFI x64 support in Server 2008, Vista* and Win7*; RedHat* and SuSEl* OS support. Mandatory for Windows 8 client. ARM 32 and 64 bit support. ACPI added.
2015
Source: http://www.slideshare.net/k33a/uefi

## Slide 57: (Unified) Extensible Firmware Interface
Industry Standard Interface Between Firmware & OS
Processor Architecture and OS Independent
C Development Environment (EDK2/UDK)
Rich GUI Pre-Boot Application Environment
Includes Modular Driver Model
UEFI executables: PE/COFF or TE executable files
UEFI file system is FAT32
UEFI OS uses UEFI compliant bootloader:
/efi/boot/bootx64.efi /efi/redhat/grub.efi
Secure Boot of Microsoft Windows 8 or above requires UEFI
UEFI firmware supports booting legacy OS from legacy MBR via Compatibility Support Module (CSM)

## Slide 58: UEFI Firmware Evolution
Class 0:
Legacy BIOS
Class 1:
UEFI CSM only
Class 2:
UEFI switch:
CSM & UEFI
Class 3:
UEFI only

## Slide 59: Compatibility Support Module (CSM)
CSM is a UEFI component which allows legacy OS boot loader (MBR) and legacy Option ROM to execute on top of UEFI based firmware without modifications
CSM has to emulate some legacy BIOS runtime services required for legacy boot
CSM consists of the following components:
    EfiCompatoibility (Legacy BIOS driver, drivers for legacy devices like PIC 8259)
    Compatibility16BIOS (provides legacy BIOS runtime services as INT13, INT15, INT19 etc.)
    Compatibility16SMM (provides legacy SMI handlers)
    Thunk/ReserveThunk (switching between 32-bit and 16-bit modes)
    Legacy Option ROM interface

## Slide 60: (U)EFI Firmware
Hardware
I/O
Memory
Network
Graphics
UEFI DXE Core / Dispatcher
UEFI OS Loaders
System Firmware (SEC/PEI)
DXE
Driver
UEFI
Boot Loader
Bootx64.efi
Bootmgfw.efi
DXE
Driver
OS Kernel / Drivers
DXE
OROM
DXE
OROM
UEFI App
UEFI App
HDD

## Slide 61: (U)EFI Firmware
Hardware
I/O
Memory
Network
Graphics
UEFI DXE Core / Dispatcher
UEFI OS Loaders
System Firmware (SEC/PEI)
DXE
Driver
UEFI
Boot Loader
Bootx64.efi
Bootmgfw.efi
DXE
Driver
OS Kernel / Drivers
DXE
OROM
DXE
OROM
UEFI App
UEFI App
HDD

## Slide 62: UEFI Boot
From Secure Boot, Network Boot, Verified Boot, oh my and almost every publication on UEFI

## Slide 63: UEFI [Compliant] Firmware
SEC
Pre-EFI Init (PEI)
Driver Exec Env (DXE)
Boot Dev Select (BDS)
Runtime / OS
S-CRTM; Init caches/MTRRs; Cache-as-RAM (NEM); Recovery; TPM Init
S-CRTM: Measure DXE/BDS
Early CPU/PCH Init
Memory (DIMMs, DRAM) Init, SMM Init
Continue initialization of platform & devices
Enum FV, dispatch drivers (network, I/O, service..)
Produce Boot and Runtime Services
Boot Manager (Select Boot Device)
EFI Shell/Apps; OS Boot Loader(s)
ExitBootServices. Minimal UEFI services (Variable)
ACPI, UEFI SystemTable, SMBIOS table
CPU Reset

## Slide 64: UEFI OS Booting
Exit UEFI Boot Services
Looking into UEFI boot variable: BootXXXX for discover UEFI storage devices
UEFI transfer control to OS bootloader from storage device
GPT
DISK
UEFI FS FAT32 partition with /EFI/BOOT/OS-loader.efi
OS partition
other partition…

## Slide 65: UEFI Shell
UEFI shell is a shell command line environment
Used to run shell commands and UEFI applications: dmpstore
UEFI OS boot loaders are also UEFI “applications”

## Slide 66: BIOS Configuration: CMOS Memory
256 bytes (low & high 128)
Backed by a small battery. Can be cleared by removing the “coin” battery (or a jumper)
Stores BIOS specific configuration settings
# chipsec_util.py cmos dump

## Slide 67: UEFI Configuration: UEFI “Variables”
UEFI variables contain configuration setup, vendor information, language information, input/output console, error console, and boot order setting, secure boot configuration, long information after capsule update, pointer to S3 boot script and so on.
Attributes of UEFI variables:
NV (Non-Volatile)
BS (Boot Service)
RT (Run-Time)
Authentication attributes
NV variables are stored in NVRAM in SPI flash memory

## Slide 68: Windows API to access UEFI variables
Windows 8+ provides user mode API to access run-time UEFI variables
GetFirmwareEnvironmentVariable http://msdn.microsoft.com/en-us/library/windows/desktop/ms724325(v=vs.85).aspx
SetFirmwareEnvironmentVariable http://msdn.microsoft.com/en-us/library/windows/desktop/ms724934(v=vs.85).aspx

## Slide 69: UEFI, EDK I, EDK II, UDK, Tianocore
TianoCore is an open source implementation of UEFI, the Unified Extensible Firmware Interface
EDK II is a modern, feature-rich, cross-platform firmware development environment for the UEFI and PI specifications: http://www.tianocore.org/edk2/
UDK (UEFI Developers Kit) is a stable release of portions of the EDK II (UDK2015)
    The UDK2015 is the EDKII support for all currently published UEFI specifications UDK2015 currently supports UEFI 2.5 and PI 1.4 level of specifications
EDK I is the older EFI 1.x development environment

## Slide 70: UEFI Working Groups
USWG
BOD
UNST
USST
……
USRT
USWG
  UEFI Specification Working Group
PIWG
  Platform Initialization Working Group
ASWG
  ACPI Specification Working Group
BOS
  Board Of Directors
USST
  USWG Security Sub-team
  Chaired by Vincent Zimmer (Intel)
  Responsible for all security related material and the team that has added security infrastructure in the UEFI spec
USRT
  UEFI Security Response Team
  Chaired by Dick Wilkins (Phoenix)
  Provide response to security issues.
UNST
  UEFI Network Sub-team (VZ chairs, too)
  Evolve network boot & network security infrastructure for UEFI Specification
Note: Engaged in firmware/boot
Related WG’s of Trusted Computing Group (TCG), IETF, DMTF
www.uefi.org
ASWG, PIWG

## Slide 71: The road from core to platform
Reference Tree
tianocore.org
OEM BIOS
New product
IBV
Existing product
ODM BIOS
New product
Existing ODM product
Commercial product in the field
Consumer product in the field
End users updating?
ODMs updating?
Time
Open Source
Open Source
All
Intel
OEM
IBV
ODM

Source: http://vzimmer.blogspot.com/2015_05_01_archive.html

## Slide 72: 1.4 Platform Firmware: SMI Handlers

## Slide 73: x86 System Management Mode (SMM)
Source: Intel® 64 and IA-32 Architectures Software Developer’s Manual
Real-Address Mode
Protected Mode
Virtual-8086
Mode
System Management Mode
IA-32e
Mode
SMI#
SMI#
SMI#
SMI#
RSM
RSM
Reset
VM=0
VM=1
Reset or
PE=0
PE=1
LME=1,CR0.PG=1
RSM

## Slide 74: System Management Mode (SMM)
SMRAM is a range of DRAM reserved by BIOS for runtime part - SMI handlers
CPU enters System Management Mode (SMM) upon receiving System Management Interrupt (SMI#) from the chipset or other logical CPU
SMI handler firmware is executing in SMM
CPU (OS) state is saved in SMRAM upon entry to SMM and restored upon exit from SMM
CPU exits SMM to the interrupted OS when SMI handler executes RSM instruction (“Resume from SMM”)

## Slide 75: Initial SMM Execution Environment
Separate address space (SMRAM)
SMM starts as Read-Address Mode with flat 32-bit addressable space without paging (CR0 PE/PG = 0)
    SMI handler firmware can enable paging later
    Segments: base = 0, limit = FFFFFFFFh
    Addressable physical memory: 0 to FFFFFFFFh (4G)
CS.base = SMBASE (30000h at reset), EIP=8000h
   SMM entry point = SMBASE + 8000h
All hardware interrupts are disabled upon entry

## Slide 76: System Management RAM (SMRAM)
SMRR_PHYSBASE
SMRAM
0x00000000
0xFFFFFFFF
SMI handlers
SMM state save area
SMBASE + 8000h
SMBASE
SMBASE + FFFFh
SMRAM
SMBASE + FE00h

## Slide 77: x64 SMM Save State
Reference: Intel® 64 and IA-32 Architectures Software Developer’s Manual
Offset (Added to SMBASE + 8000H) | Register | Writable?
7FF8H | CR0 | No
7FF0H | CR3 | No
7FE8H | RFLAGS | Yes
7FE0H | IA32_EFER | Yes
7FD8H | RIP | Yes
7FD0H | DR6 | No
7FC8H | DR7 | No
7FC4H | TR SEL1 | No
7FC0H | LDTR SEL1 | No
7FBCH | GS SEL1 | No
7FB8H | FS SEL1 | No
7FB4H | DS SEL1 | No
7FB0H | SS SEL1 | No
7FACH | CS SEL1 | No
7FA8H | ES SEL1 | No
7FA4H | IO_MISC | No
7F9CH | IO_MEM_ADDR | No
7F94H | RDI | Yes

## Slide 78: x64 SMM Save State (cont’d)
Offset (Added to SMBASE + 8000H) | Register | Writable?
7F8CH | RSI | Yes
7F84H | RBP | Yes
7F7CH | RSP | Yes
7F74H | RBX | Yes
7F6CH | RDX | Yes
7F64H | RCX | Yes
7F5CH | RAX | Yes
7F54H | R8 | Yes
7F4CH | R9 | Yes
7F44H | R10 | Yes
7F3CH | R11 | Yes
7F34H | R12 | Yes
7F2CH | R13 | Yes
7F24H | R14 | Yes
7F1CH | R15 | Yes
7F1BH-7F04H | Reserved | No
7F02H | Auto HALT Restart Field (Word) | Yes
7F00H | I/O Instruction Restart Field (Word) | Yes
7EFCH | SMM Revision Identifier Field (Doubleword) | No
7EF8H | SMBASE Field (Doubleword) | Yes
Reference: Intel® 64 and IA-32 Architectures Software Developer’s Manual

## Slide 79: Locating SMRAM using CHIPSEC
python chipsec_util.py msr 0x1f2
..
[*] loading common platform config from ‘..chipsec\tool\chipsec/cfg\common.xml'..
[*] loading 'hsw' platform config from ‘..chipsec\tool\chipsec/cfg\hsw.xml'..
[CHIPSEC] Executing command 'msr' with args ['0x1f2']
[CHIPSEC] CPU0: RDMSR( 0x1f2 ) = 00000000DA000006 (EAX=DA000006, EDX=00000000)
[CHIPSEC] CPU1: RDMSR( 0x1f2 ) = 00000000DA000006 (EAX=DA000006, EDX=00000000)
[CHIPSEC] CPU2: RDMSR( 0x1f2 ) = 00000000DA000006 (EAX=DA000006, EDX=00000000)
[CHIPSEC] CPU3: RDMSR( 0x1f2 ) = 00000000DA000006 (EAX=DA000006, EDX=00000000)
python chipsec_util.py msr 0x1f3
..
[*] loading common platform config from ‘..chipsec\tool\chipsec/cfg\common.xml'..
[*] loading 'hsw' platform config from ‘..chipsec\tool\chipsec/cfg\hsw.xml'..
[CHIPSEC] Executing command 'msr' with args ['0x1f3']
[CHIPSEC] CPU0: RDMSR( 0x1f3 ) = 00000000FF000800 (EAX=FF000800, EDX=00000000)
[CHIPSEC] CPU1: RDMSR( 0x1f3 ) = 00000000FF000800 (EAX=FF000800, EDX=00000000)
[CHIPSEC] CPU2: RDMSR( 0x1f3 ) = 00000000FF000800 (EAX=FF000800, EDX=00000000)
[CHIPSEC] CPU3: RDMSR( 0x1f3 ) = 00000000FF000800 (EAX=FF000800, EDX=00000000)

## Slide 80: System Management Interrupt (SMI) Handler
SMM Core dispatcher
SMI
SMST
CPU info
Memory info
I/O info
SMM Driver
SMM Driver
SMM Driver
SMM callback
SMM callback
SMM callback
...
RSM
SMM code flow

## Slide 81: 1.4 Platform Firmware: Hardware Reference Code, etc.

## Slide 82: Hardware Reference Code
Reference Code is a part of BIOS / system firmware which initializes specific piece of platform
  CPU reference code (microcode update, CAR/NEM init)
  Memory reference code trains DDR, initializes DIMMs, initializes memory controller, creates memory map
  Chipset reference code initializes internal PCH interfaces
Provided by CPU/chipset vendors to original equipment manufacturers (OEMs) or BIOS vendors (IBV) for integration into the final BIOS for specific platform

## Slide 83: Intel® Firmware Support Package (FSP)
  Silicon initialization binaries (CPU, mem, PCH/SoC) packaged into FSP
  Plugs into existing FW frameworks
  Binary customization
Reference: www.intel.com/fsp
Final BIOS
Reference
BIOS
EDKII Repo
FSP FV
FSP
Core PEIMs
CPU RC
Mem RC
Chipset RC
Platform PEIMs
Other Glue
Si Init
PeiCore
The Intel FSP provides processor, memory & chipset initialization in a format that can easily be incorporated into existing boot loader (firmware) frameworks

## Slide 84: References and Further Reading
For further details on platform and BIOS fundamentals take
Advanced x86: Introduction to BIOS & SMM
class by John Butterworth, Xeno Kovah and Corey Kallenberg at http://OpenSecurityTraining.info

## Slide 85: References and Further Reading
Advanced x86: Introduction to BIOS & SMM by John Butterworth and Xeno Kovah at OpenSecurityTraining.info
4th Generation Intel® Core™ Processor Family Datasheet (vol 1, vol 2)
PCI Express System Architecture by Budruk, Anderson and Shanley (MindShare)
PCI System Architecture by Shanley and Anderson (MindShare)
An Introduction to PCI Express by Budruk (MindShare)
PCI/PCI Express Configuration Space Access (AMD)
PCI Express Base Specification Revision 3.0 (https://pcisig.com/specifications)
LPC specification
SPI Block Guide (Motorola, Inc.)
SMBus specification
Designing with SMBus 2.0 by Dale Stolitzka (Analog Devices, Inc.)
Minimal Intel Architecture Boot Loader by Jenny M Pelner & James A Pelner (Intel)
Pentium Processor Family Developer’s Manual (Initialization and Mode Switching)
Power Sequence and Reset Utilizing the Intel® EP80579 Processor by Julio Pineda (Intel)
Plug and Play BIOS Specification
BIOS Boot Specification
Booting an Intel Architecture System by Pete Dice (Intel)
Intel® 64 and IA-32 Architectures Software Developer’s Manual
UEFI Platform Initialization Specification 1.5
UEFI Specification 2.6
A Tour Beyond BIOS: Using Intel FSP with EDKII

## Slide 86
Training materials are available on Github
https://github.com/advanced-threat-research/firmware-security-training
Yuriy Bulygin @c7zero
Alex Bazhaniuk @ABazhaniuk
Andrew Furtak @a_furtak
John Loucaides @JohnLoucaides

## Slide 87: Security of BIOS/UEFI System Firmware from Attacker and Defender Perspectives Section 2. Bootkits and Secure Boot
Yuriy Bulygin *
Alex Bazhaniuk *
Andrew Furtak *
John Loucaides **
* Advanced Threat Research, McAfee
** Intel

## Slide 88: License
Training materials are shared under Creative Commons “Attribution” license CC BY 4.0
Provide the following attribution:
Derived from “Security of BIOS/UEFI System Firmware from Attacker and Defender Perspective” training by Yuriy Bulygin, Alex Bazhaniuk, Andrew Furtak and John Loucaides available at https://github.com/advanced-threat-research/firmware-security-training

## Slide 89: Section 2. Bootkits and Secure Boot

## Slide 90: 2.1 In the beginning

## Slide 91: Early days. Boot sector infection
Elk Cloner – one of the first known viruses. Created by CAS freshman Richard Skrenta (Sprengelmeyer) in 1981. Infected Apple II DOS 3.3 OS, occupied unused space inside “boot sector”. Resident in memory. Infects uninfected floppy disks.
http://virus.wikidot.com/elk-cloner

## Slide 92: Early days. Boot sector infection
Brain – considered to be the first PC virus.
This virus originated in January, 1986, in Lahore Pakistan. The first noticeable infection problems did not surface until 1988.
The Brain is a boot sector infector, approximately 3 K in length, that infects 5 1/4" floppies.
The virus stores the original boot sector, and six extension sectors, containing the main body of the virus, in available sectors which are then flagged as bad sectors.
Brain is the only virus yet discovered that contains the valid names, phone numbers and addresses of the creators.
http://virus.wikidot.com/brain
http://www.textfiles.com/virus/braininf.vir (David Stang, NCSA)

## Slide 93: Early days. BIOS infection
BIOS Meningitis – the worlds first flash BIOS infecting virus. Infects floppy boot-sector and hard drive MBR as well. It was coded by Qark of VLAD and appeared in Issue 2 of VLAD magazine in November 1994.
BIOS Meningitis uses various INT 16h AH=E0h (BIOS Flash routines) calls to manipulate the Flash memory. Hooks INT 19h (BIOS Boot Strap Loader) handler. The virus INT 19h handler copies the virus to 0000:7C00h (standard boot sector load address), emulates an infected MBR execution and then does the job of a standard INT 19h handler – boots from floppy or HDD.
http://virus.wikidot.com/bios-meningitis
http://www.wiw.org/~meta/vlad/vlad2/art44.htm (source code)

## Slide 94: BIOS damage - CIH
  In 1998-99 CIH (“Chernobyl”) virus infected 60 million and damaged 0.5 million computers causing ~$1B in damages
  CIH destructive payload, when activated, attempts to corrupt system BIOS in ROM and 2048 sectors on all hard drives including boot sectors
Sources: Wikipedia, F-Secure, Kaspersky Lab, GRC

## Slide 95: 2.2 Boot Sectors

## Slide 96: Master Boot Record (MBR)
MBR helps BIOS to locate OS partition and boot the OS
MBR is located at LBA 0 (the first boot sectors) of the disk
MBR contains:
  boot code (initial program loader) which is loaded and invoked by the BIOS
  up to four partition records each defining starting and ending logical block addresses (LBA) for corresponding partitions on a disk
Source: https://technet.microsoft.com/en-us/library/cc976786.aspx
Legacy MBR
Partition
Partition
Partition
LBA 0
Partition

## Slide 97: Legacy MBR structure
As defined in UEFI Spec 2.5, Chapter 5 GPT Disk Layout
Source: https://technet.microsoft.com/en-us/library/cc976786.aspx
Mnemonic | Byte Offset | Byte Length | Description
BootCode | 0 | 424 | X86 code used on a no-UEFI system to select an MBR partition record and load the first logical block of the partition. This code shall not be executed on UEFI systems
UniqueMBRDiskSignature | 440 | 4 | Unique Disk Signature. This may be used by the OS to identify the disk from other disks in the system. This value is always written by the OS and is never written by EFI firmware
Unknown | 444 | 2 | Unknown. This field shall not be used in UEFI firmware
PartitionRecord | 446 | 16*4 | Array of four legacy MSR partition records
Signature | 510 | 2 | Set to 0xAA55 (i.e., byte 510 contains 0x55 and byte 511 contains 0xAA)
Reserved | 512 | Logical BlockSize - 512 | The rest of the logical block, if any, is reserved.

## Slide 98: Legacy MBR partition record
The partition defined by each MBR Partition Record must physically reside on the disk (i.e., not exceeding the capacity of the disk).
Each partition must not overlap with other partitions.
Source: https://technet.microsoft.com/en-us/library/cc976786.aspx
Mnemonic | Byte Offset | Byte Length | Description
BootIndicator | 0 | 1 | 0x80 indicates that this is the bootable legacy partition. Other values indicate that this is not a bootable legacy partition. This field shall not be used by UEFI firmware
StartingCHS | 1 | 3 | Start of partition in CHS address format. This field shall not be used by UEFI firmware
OSType | 4 | 1 | Type of partition.
EndingCHS | 5 | 3 | Array of four legacy MSR partition records
StartingLBA | 8 | 4 | End of partition in CHS address format. This field shall not be used by UEFI firmware.
SizeInLBA | 12 | 4 | Size of the partition of LBA units of logical blocks. This field is used by UEFI firmware to determine the size of the partition

## Slide 99: Protective MBR
Instead of legacy MBR a protective MBR may be located at LBA0 of the disk if it is using the GPT disk layout
One of the Partition Records shall be defined in a way reserving the entire space on the disk after the Protective MBR itself for the GPT disk layout
Reference: http://blog.fpmurphy.com/2011/10/fedora-16-mbr-grub-legacy-to-gpt-grub2.html
Primary GPT
UEFI system partition
Partition
Partition
Partition
Backup GPT
LBA 0
GPT Protective partition
Protective MBR

## Slide 100: Protective MBR structure
The Protective MBR precedes the GUID Partition Table Header to maintain compatibility with existing tools that do not understand GPT partition structures
Reference: https://en.wikipedia.org/wiki/GUID_Partition_Table#Protective_MBR_.28LBA_0.29
Mnemonic | Byte Offset | Byte Length | Description
Boot Code | 0 | 424 | Unused by UEFI systems
Unique MBR Disk Signature | 440 | 4 | Unused. Set to zero
Unknown | 444 | 2 | Unused. Set to zero
Partition Record | 446 | 16*4 | Array of four MSR partition records. Contains: One partition record Three partition record each set to zero
Signature | 510 | 2 | Set to 0xAA55 (i.e., byte 510 contains 0x55 and byte 511 contains 0xAA)
Reserved | 512 | Logical BlockSize - 512 | The rest of the logical block, if any, is reserved. Set to zero

## Slide 101: Volume Boot Record (VBR)
A Volume Boot Record (VBR) is the first sector of a partition (opposite to MBR which is the first sector of a hard disk).
VBR (just like MBR) also contain some code and data, but it's far less standard.
The code is always OS specific, but in common all versions does the same: locate the kernel on the partition, load and execute it.
A really good example for VBR is the original DOS bootsector, which used FAT and loaded IO.SYS and MSDOS.SYS from the root directory.
Source: OS Dev Wiki http://wiki.osdev.org/Volume_Boot_Record

## Slide 102: 2.3 Bootkits (Boot Rootkits)

## Slide 103: eEye BootRoot
eEye BootRoot was the first pubic proof-of-concept bootkit developed by Derek Soeder and Ryan Permeh
Hooked INT 13h (Disk access ISR) to patch OSLOADER
OSLOADER patch was able to modify OS further, e.g. patch boot drivers

## Slide 104: Chronology
  OS Kernel Rootkits (~ 1999+)
    Research: NTRootkit, SucKIT, adore, knark
    In-the-Wild: HackerDefender, Haxdoor
  MBR,VBR Bootkits (~ 2005+)
    Defense: Windows DSE, Patch Guard
    Research: eEye BootRoot, BOOT-KIT, Vbootkit, Stoned Bootkit, Deep Boot, EvilCore
    In-the-Wild: Mebroot, TDL4, FIN1, Rovnix, Olmasco, XPAJ, Gapz, Petya and Goldeneye
  BIOS Rootkits (~ 2006+)
    Research: Heasman’s ACPI and PCI OpROM Rootkits, Clear Hat SMM Rootkit, Phrack 65 SMM, Persistent BIOS Infection, Phrack 66 “A Real SMM Rootkit”, Rakshasa
    In-the-Wild: IceLord BIOS Rootkit, Mebromi, ANT catalog
  UEFI Bootkits (~ 2012+)
    EFI/UEFI (support in Windows Vista, Windows 7, Server 2008)
    Research: Andrea Allievi’s UEFI Bootkit, Dreamboot
  (U)EFI Firmware Rootkits (~ 2012+)
    Defense: Windows 8 and UEFI Secure Boot
    Research: Angry Evil-Maid SRTM rootkit, A Tale of Secure Boot Bypass UEFI Bootkit, Project Maux, snare’s Mac EFI Rootkit, Thunderstrike 1 and 2, Light Eater, firmware rootkit vs VMM, Dmytro Oleksiuk’s SmmBackdoor
    In-the-Wild: HackingTeam UEFI Rootkit, Mac EFI Der Starke/DarkMatter implant, Sonic Scredriver

## Slide 105: Types of Bootkits
  MBR
    MBR Bootstrap code area modification (TDL4 here & here, Goblin, Petya & Goldeneye ransomware)
    MBR Partition Table modification (Olmasco)
  VBR
    VBR boot code (IPL) modification (FIN1, Rovnix)
    VBR BIOS Parameter Block (BPB) modification (Gapz here & here)
  BIOS, UEFI
    Injecting malicious Option ROMs (Mebromi)
    Replacing EFI boot loaders
    Installing custom firmware (EFI DXE) executables (HackingTeam UEFI Rootkit)
  Additional references: Bootkits step by-step

## Slide 106: MBR Bootkit: TDL4 (Olmarik, Alureon)
Source: What's different with TDL4 and TDL3
BIOS
VBR
bootmgr
bootmgfw.efi
Winload.exe
ntoskrnl.exe
Hall.dll
CI.dll
MBR
Kdcom.dll
Process BCD
EFI
Load ldr32
Load drv32 or drv64
BcdLibraryBoolean_DisableIntegrityCheck
BcdOSLoaderBoolean_WinPEMode
Load ldr16
Hook INT 13h
Driver Signing Check
Driver Signing Check
Code Integrity Check

## Slide 107: VBR Bootkit: Fin1
  The installer (BOOTRASH) reads the original boot sector into memory
  Saves an backup copy of the VBR code at 0xE sectors from the start of the partition. Apple integrity check.
  Installer decodes the new bootstrap code from one of its embedded resources and overwrites the existing bootstrap code
  BOOTRASH hijacks boot process in order to load the Nemesis payload before the OS.
  BOOTRASH creates its own custom virtual file system (VFS) to store the components of the Nemesis
  Source: fin1 targets boot record
BIOS
MBR
bootmgr
VBR
Nemesis payload
Virtual File System (VFS)

## Slide 108: Ransomware Bootkit: Petya
Source: Petya – Taking Ransomware To The Low Level
Launched by Windows executable dropper
Overwrites the beginning of the disk (including MBR) and makes an XOR encrypted backup of the original data
The second stage is executed by the fake CHKDSK scan. After this, the file system is destroyed and cannot be read
This first ransomware targeting disk with MBR rather than individual files

## Slide 109: Mebromi BIOS Infection
Mebromi malware includes BIOS infector & MBR bootkit components
Patches BIOS ROM binary injecting malicious ISA Option ROM with legitimate BIOS image mod utility
Triggers SW SMI 0x29/0x2F to erase SPI flash then write patched BIOS binary
# chipsec_util.py smi 0x2F
Infected BIOS injects boot strap code to MBR

## Slide 110: Exercise 2.1
Extract and Parse Master Boot Record

## Slide 111: 2.3 GUID Partition Table

## Slide 112: GUID Partition Table
GUID Partition Table (GPT) is a hard disk partition table layout using GUIDs defined as part of UEFI standard
The GPT Header defines the range of LBAs that are usable by GPT Partition Entries
Disk GUID is a GUID that uniquely identifies the entire GPT Header and all its associated storage

## Slide 113: GUID Partition Table Disk Layout
Source: http://kurtqiao.github.io/uefi/2014/12/31/GUID-Partition-Table-Disk.html
PMBR
Partition Table HDR
Partition 1
0
1
…
n
LBA0
LBA1
0
1
…
n
Start partition
End partition
End partition
Start partition
LBAn
Last useable block
Partition Table HDR
Primary Partition
Table
Backup Partition
Table
First useable block

## Slide 114: GUID Partition Table Header
Source: http://ntfs.com/guid-part-table.htm
Offset | Length | Contents
0x00 | 8 bytes | Signature ("EFI PART", 45h 46h 49h 20h 50h 41h 52h 54h or 0x5452415020494645ULL on littleendian machines)
0x08 | 4 bytes | Revision (for GPT version 1.0 (through at least UEFI version 2.3.1), the value is 00h 00h 01h 00h)
0x0C | 4 bytes | Header size in little endian (in bytes, usually 5Ch 00h 00h 00h or 92 bytes)
0x10 | 4 bytes | CRC32 of header (offset +0 up to header size), with this field zeroed during calculation
0x14 | 4 bytes | Reserved; must be zero
0x18 | 8 bytes | Current LBA (location of this header copy)
0x20 | 8 bytes | Backup LBA (location of the other header copy)
0x28 | 8 bytes | First usable LBA for partitions (primary partition table last LBA + 1)
0x30 | 8 bytes | Last usable LBA (secondary partition table first LBA 1)
0x38 | bytes | Disk GUID (also referred as UUID on UNIXes)
0x48 | 8 bytes | Starting LBA of array of partition entries (always 2 in primary copy)
0x50 | 4 bytes | Number of partition entries in array
0x54 | 4 bytes | Size of a single partition entry (usually 80h or 128)
0x58 | 4 bytes | CRC32 of partition array
0x5C | * | Reserved; must be zeroes for the rest of the block (420 bytes for a sector size of 512 bytes; but can be more with larger sector sizes)
GPT Entry

## Slide 115: GUID Partition Table Entry
Source: http://www.datarecovery.institute/guid-partition-table-windows-10/
Offset | Length | Contents
0 (0x00) | 16 bytes | Partition type GUID
16 (0x10) | 16 bytes | Unique partition GUID
32 (0x20) | 8 bytes | First LBA (little endian)
40 (0x28) | 8 bytes | Last LBA (inclusive, usually odd)
48 (0x30) | 8 bytes | Attribute flags (e.g. bit 60 denotes readonly)
56 (0x38) | 72 bytes | Partition name (36 UTF16LE code units)

## Slide 116: Exercise 2.2
Access ESP from Linux, UEFI shell and Windows; find OS boot loaders and GPT

## Slide 117: 2.4 UEFI Bootkits

## Slide 118: UEFI Based Windows Boot
Source: Windows Boot Environment by Murali Ravirala
UEFI Firmware
Windows Boot Manager (bootmgfw.efi)
UEFI Boot Manager
Windows OS Loader (winload.efi)
Kernel
(ntoskrnl.exe)
Performs CPU and Chipset initialization, load drivers, etc.
Loads UEFI device drivers (based on NVRAM DriverXxx variable), loads boot application
Load Windows OS loader selected by user
Loads the Windows OS, calls ExitBootServices()

## Slide 119: Types of UEFI Bootkits
Replacing Windows Boot Manager
    EFI System Partition (ESP) on Fixed Drive
    ESP\EFI\Microsoft\Boot\bootmgfw.efi
    UEFI technology: say hello to the Windows 8 bootkit! by ITSEC
Replacing Fallback Boot Loader
    ESP\EFI\Boot\bootx64.efi
    Dreamboot by Sébastien Kaczmarek, QUARKSLAB
Adding New Boot Loader (bootkit.efi)
  Modified BootOrder / Boot#### EFI variables
Adding/Replacing DXE Driver
    Stored on Fixed Drive
    Not embedded in Firmware Volume (FV) in ROM
    Modified DriverOrder / Driver#### EFI variables

## Slide 120: Types of UEFI Bootkits
Patching UEFI “Option ROM”
    UEFI DXE Driver in Add-On Card (Network, Storage..)
    Non-Embedded in FV in ROM
    Mac EFI Rootkits by @snare, Black Hat USA 2012
    Thunderstrike Mac EFI Rootkit by Trammell Hudson
Replacing OS Loaders (winload.efi, winresume.efi)
Patching GUID Partition Table (GPT)

## Slide 121: Replacing Boot Loaders
Hardware
I/O
Memory
Network
Graphics
UEFI DXE Core / Dispatcher
UEFI OS Loaders
System Firmware (SEC/PEI)
UEFI
Boot Loader
Bootx64.efi
Bootmgfw.efi
OS Kernel / Drivers
Malware
DXE
Driver
DXE
Driver
UEFI
OROM
UEFI
OROM
HDD

## Slide 122: Adding/Replacing DXE Drivers
Hardware
I/O
Memory
Network
Graphics
UEFI DXE Core / Dispatcher
UEFI OS Loaders
System Firmware (SEC/PEI)
UEFI
Boot Loader
Bootx64.efi
Bootmgfw.efi
OS Kernel / Drivers
Malware
DXE
Driver
DXE
Driver
UEFI
OROM
UEFI
OROM
HDD

## Slide 123: Replacing DXE Option ROM Drivers
Hardware
I/O
Memory
Network
Graphics
UEFI DXE Core / Dispatcher
UEFI OS Loaders
System Firmware (SEC/PEI)
UEFI
Boot Loader
Bootx64.efi
Bootmgfw.efi
OS Kernel / Drivers
Malware
DXE
Driver
DXE
Driver
UEFI
OROM
UEFI
OROM
HDD

## Slide 124: UEFI Bootkits
Hardware
I/O
Memory
Network
Graphics
UEFI DXE Core / Dispatcher
UEFI OS Loaders
System Firmware (SEC/PEI)
UEFI
Boot Loader
Bootx64.efi
Bootmgfw.efi
OS Kernel / Drivers
Malware
DXE
Driver
DXE
Driver
UEFI
OROM
UEFI
OROM
HDD

## Slide 125: UEFI Bootkit: Dreamboot
Source: UEFI and Dreamboot by Sebastien Kaczmarek
Replaces Windows 8 loader
Patches OS to disable kernel protections
  Disables DEP (NX flag)
  Disables Windows Patch Guard
Open source: https://github.com/quarkslab/dreamboot

## Slide 126: Windows 8 UEFI Bootkit
Source: A Tale of One Software Bypass of Windows 8 Secure Boot

## Slide 127: 2.5 UEFI Secure Boot

## Slide 128: Secure Boot (UEFI + OS)
Hardware
I/O
Memory
Network
Graphics
UEFI DXE Core / Dispatcher
UEFI OS Loaders
System Firmware (SEC/PEI)
DXE
Driver
UEFI
Boot Loader
Bootx64.efi
Bootmgfw.efi
Signed BIOS
Update
DXE
Driver
OS Kernel
OS Driver
OS Driver
DXE
OROM
DXE
OROM
UEFI App
UEFI App
UEFI
Secure
Boot
OS
Secure
Boot

## Slide 130: UEFI Secure Boot Configuration
SecureBoot
Enables/disables image signature checks
SetupMode
PK is installed (USER_MODE) or not (SETUP_MODE)
SETUP_MODE allows updating KEK/db(x), self-signed PK
CustomMode
Modifiable by physically present user
Allows updating KEK/db/dbx/PK even when PK is installed
SecureBootEnable
Global non-volatile Secure Boot Enable
Modifiable by physically present user

## Slide 131: Secure Boot Key Hierarchy
Platform Key (PK)
    Verifies KEKs
    Platform Vendor’s Cert
Key Exchange Keys (KEKs)
    Verify db and dbx
    Earlier rev’s: verifies image signatures
Authorized Database (db)
Forbidden Database (dbx)
    X509 certificates, SHA1/SHA256 hashes of allowed & revoked images
    Earlier revisions: RSA-2048 public keys, PKCS#7 signatures
PK
KEK
db
dbx
Update
Update
Update
If signed by key in db, executable can be loaded
If signed by key in dbx, executable load is forbidden

## Slide 132: PK (openssl x509 -in PK.pem –text)
Certificate:
Data:
Version: 3 (0x2)
Serial Number:
53:41:e0:15:c4:3a:f8:a8:48:36:b9:a5:ff:69:14:88
Signature Algorithm: sha256WithRSAEncryption
Issuer: CN=ASUSTeK MotherBoard PK Certificate
Validity
Not Before: Dec 26 23:34:50 2011 GMT
Not After : Dec 26 23:34:49 2031 GMT
Subject: CN=ASUSTeK MotherBoard PK Certificate
Subject Public Key Info:
Public Key Algorithm: rsaEncryption
Public-Key: (2048 bit)
Modulus:
00:d9:84:15:36:c5:d4:ce:8a:a1:56:16:a0:e8:74:
..
Exponent: 65537 (0x10001)
X509v3 extensions:
2.5.29.1:
?=.../0-1+0)..U..."ASUSTeK MotherBoard PK Certificate..SA...:..H6...i..
Signature Algorithm: sha256WithRSAEncryption
73:27:1a:32:88:0e:db:13:8d:f5:7e:fc:94:f2:1a:27:6b:c2:
..
-----BEGIN CERTIFICATE-----
MIIDRjCCAi6gAwIBAgIQU0HgFcQ6+KhINrml/2kUiDANBgkqhkiG9w0BAQsFADAt
..
-----END CERTIFICATE-----

## Slide 133: Secure Boot Modes
Source: https://www.wzdftpd.net/blog/tag/debian.html
USER MODE
SETUP MODE
Enroll PK
Delete PK
Platform specific Clear PK

## Slide 134: Secure Boot Modes
PK variable exists in NVRAM?
Yes: Set SetupMode variable to USER_MODE
No: Set SetupMode variable to SETUP_MODE
SecureBootEnable variable exists in NVRAM?
Yes
  SecureBootEnable variable is SECURE_BOOT_ENABLE and SetupMode is USER_MODE? Set SecureBoot to ENABLE
  Else? Set SecureBoot to DISABLE
No
  SetupMode variable is USER_MODE? Set SecureBoot to ENABLE
  SetupMode variable is SETUP_MODE? Set SecureBoot to DISABLE

## Slide 135: Image Verification Policies
DxeImageVerificationLib defines policies applied to different types of images and on security violation
IMAGE_FROM_FV (ALWAYS_EXECUTE), IMAGE_FROM_FIXED_MEDIA,
IMAGE_FROM_REMOVABLE_MEDIA, IMAGE_FROM_OPTION_ROM
ALWAYS_EXECUTE, NEVER_EXECUTE,
ALLOW_EXECUTE_ON_SECURITY_VIOLATION
DEFER_EXECUTE_ON_SECURITY_VIOLATION
DENY_EXECUTE_ON_SECURITY_VIOLATION
QUERY_USER_ON_SECURITY_VIOLATION

## Slide 136
Let’s have a look at the Secure Boot image verification process
SecurityPkg\Library\DxeImageVerificationLib
http://sourceforge.net/apps/mediawiki/tianocore/index.php?title=SecurityPkg

## Slide 137: Verifying Policies
Image Verification Policy
(IMAGE_FROM_FV) ALWAYS_EXECUTE? EFI_SUCCESS
NEVER_EXECUTE? EFI_ACCESS_DENIED

## Slide 138: Image Verification Handler
SecureBoot EFI variable doesn’t exist or equals to SECURE_BOOT_MODE_DISABLE? EFI_SUCCESS
File is not valid PE/COFF image? EFI_ACCESS_DENIED
SecureBootEnable NV EFI variable doesn’t exist or equals to SECURE_BOOT_DISABLE? EFI_SUCCESS
SetupMode NV EFI variable doesn’t exist or equals to SETUP_MODE? EFI_SUCCESS

## Slide 139: Authenticating EFI Images (EDK2)
Image is not signed
    Image signature or SHA256 hash in DBX? EFI_ACCESS_DENIED
    Image signature or SHA256 hash in DB? EFI_SUCCESS
Image is signed
For each signature in PE file:
    Signature verified by root/intermediate cert in DBX? EFI_ACCESS_DENIED
    Image signature or SHA256 hash in DBX? EFI_ACCESS_DENIED
For each signature in PE file:
    Signature verified by root/intermediate cert in KEK or DB? EFI_SUCCESS
    Image signature or SHA256 hash in DB? EFI_SUCCESS
Else EFI_ACCESS_DENIED

## Slide 140: Open source packages for Secure Boot Flow
Source: A Tour Beyond BIOS into UEFI Secure Boot by Rosenbaum, Zimmer
SecurityPkg
DxeImageVerificationLib
DxeImageVerificationHandler()
HashPeImage()
HashPeImageByType()
VerifyWinCertificateForPkcsSignedData()
DxeImageVerificationLibImageRead()
IsSignatureFoundInDatabase()
IsPkcsSignedDataVerifiedBySignatureList()
VerifyCertPkcsSignedData()
Authenticated Variables
gRT->GetVariable
MdeModulePkg
LoadImage Boot Service
gBS->LoadImage
CoreLoadImage()
EFI_SECURITY_ARCH_PROTOCOL
SecurityStubDxe
SecurityStubAuthenticateState()
DxeSecurityManagementLib
RegisterSecurityHandler()
ExecuteSecurityHandlers()
MdePkg
BasePeCoffLib
PeCoffLoaderGetImageInfo()
CryptoPkg
BaseCryptLib
Sha256Init()
Sha256Update()
Sha256Final()
Sha256GetContextSize()
AuthenticodeVerify()
Pkcs7Verify()
WrapPkcs7Data()
OpenSslLib
Openssl-0.9.8w
IntrinsicLib

## Slide 141: 2.6 Linux Secure Boot

## Slide 142: Linux Secure Boot with Shim
shim
UEFI
db
Signature
Signature
UEFI CA
SUSE
verify
verify
Microsoft UEFI CA cert
SUSE UEFI cert
Either the UEFI public key or SUSE public key will let the shim boot with UEFI secure boot
Source: UEFI Open Platforms by Vincent Zimmer

## Slide 143: Multiple OS Boot with MOK
Source: UEFI Open Platforms by Vincent Zimmer
shim
MOKList
kernel
grub2
grub2
Kernel
SUSE
User
SUSE
User
DB
User
load
load
Load
Load
Load
BS Var
SUSE UEFI key
SUSE boot path
custom boot path

## Slide 144: Exercise 2.3
Secure Boot on Linux

## Slide 145
Training materials are available on Github
https://github.com/advanced-threat-research/firmware-security-training
Yuriy Bulygin @c7zero
Alex Bazhaniuk @ABazhaniuk
Andrew Furtak @a_furtak
John Loucaides @JohnLoucaides

## Slide 146: Security of BIOS/UEFI System Firmware from Attacker and Defender Perspectives Section 3. Hands-On Learning of Platform Hardware and Firmware
Yuriy Bulygin *
Alex Bazhaniuk *
Andrew Furtak *
John Loucaides **
* Advanced Threat Research, McAfee
** Intel

## Slide 147: License
Training materials are shared under Creative Commons “Attribution” license CC BY 4.0
Provide the following attribution:
Derived from “Security of BIOS/UEFI System Firmware from Attacker and Defender Perspective” training by Yuriy Bulygin, Alex Bazhaniuk, Andrew Furtak and John Loucaides available at https://github.com/advanced-threat-research/firmware-security-training

## Slide 148: Section 3. Hands-On Learning of Platform Hardware and Firmware

## Slide 149: 3.0 Building and Installing CHIPSEC

## Slide 150: Bootable Linux USB with CHIPSEC

## Slide 151: Bootable Linux USB with CHIPSEC
Ubuntu bootable USB with CHIPSEC (includes all dependencies)
Building and running CHIPSEC:
# cd ~/Desktop/chipsec/source/
# git pull (you already have latest CHIPSEC on USB)
# python setup.py build_ext -i
# sudo python chipsec_util.py platform

## Slide 152: Installing CHIPSEC on Windows
Install Python 2.7.x (http://www.python.org/download/)
Install additional packages for installed Python release
    pip install setuptools
    pip install pywin32
Build CHIPSEC Windows driver. Skip this step if you already have chipsec_hlpr.sys built
Copy CHIPSEC driver (chipsec_hlpr.sys) to proper path in CHIPSEC \chipsec\chipsec\helper\win\win7_amd64 or win7_x86
Install CHIPSEC
    pip install chipsec
Turn off kernel driver signature checks in Windows 8, 8.1, 10 64-bit
Refer to CHIPSEC manual:
https://github.com/chipsec/chipsec/blob/master/chipsec-manual.pdf

## Slide 153: 3.1 Access to Hardware Resources

## Slide 154: Hardware Configuration
CPU
x86 state: GPR (RAX, …), Control Registers (CRx), Debug Registers (DRx), etc.
CPU Model Specific Registers (MSR)
CPU and Chipset (SoC)
Processor I/O space: I/O ports and I/O BARs
PCIe devices configuration space
Memory-mapped PCIe configuration access a.k.a. Enhanced Configuration Access Mechanism (ECAM)
Memory-mapped I/O ranges
IOSF Message Bus registers

## Slide 155: Processor I/O Space: I/O Ports and BARs
Legacy I/O interface accessible via x86 IN and OUT assembly instructions
Offset in I/O space is I/O register or I/O port. I/O space contains multiple ranges assigned to some device or controller
I/O ranges can be fixed:
    60h/62h/64h/66h: keyboard/embedded uController
    CF8h/CFCh: PCIe devices CFG access
    CF9h: platform reset
    B2h/B3h: APMC/SMI
Or variable (defined by I/O BAR registers)
    SMBus
    ACPI/PMBASE
    GPIO
    I/O Trap

## Slide 156: Processor I/O Space: I/O Ports and BARs
# chipsec_util io <io_port> <width> [value]
# chipsec_util.py io 0xcf8 dword 0x80000000
[CHIPSEC] OUT 0x0CF8 <- 0x80000000 (size = 0x04)
# chipsec_util.py io 0xcfc dword
[CHIPSEC] IN 0x0CFC -> 0x0A048086 (size = 0x04)

## Slide 157: PCIe Configuration Space Access
SW uses one these mechanisms to access config space:
Legacy configuration access via control CF8h & data CFCh processor I/O ports
    PCI config register address
    bus << 16 | device << 11 | function << 8 | offset & ~3
    CF8h  1<<31 | bdf_address
    Read data from or write data to port (CFCh + off[1:0])
Extended (memory-mapped) config access (see later)
100h bytes of CFG header
8 * 100h per device
32* 8 * 100h per bus

## Slide 158: PCIe Configuration Space and Registers
Enumerate all available PCIe devices:
# chipsec_util pci enumerate
[CHIPSEC] Enumerating available PCIe devices..
BDF | VID:DID | Vendor | Device
--------------------------------------------------------------------------------
00:00.0 | 8086:0A04 | Intel Corporation |
00:02.0 | 8086:0A16 | Intel Corporation |
Reading from/writing to PCIe device’s configuration space:
# chipsec_util.py pci <bus> <dev> <fun> <off> <width> [value]
# chipsec_util.py pci 0 0 0 0x0 dword
[CHIPSEC] reading PCI B/D/F 0/0/0, off 0x00: 0xA048086
# chipsec_util.py pci 0 0x1F 0 0xDC byte
[CHIPSEC] reading PCI B/D/F 0/31/0, off 0xDC: 0x2A

## Slide 159: Extended PCIe Configuration
Enhanced Configuration Access Mechanism (ECAM) allows accessing PCIe extended configuration space (4kB) beyond PCI configuration space (256 bytes)
To access entire PCIe extended configuration space CPU reserves memory-mapped range in physical addressable memory (MMCFG)
    Range is re-locatable (e.g. PCIEXBAR register in B.D:F 0.0:0 on Core/Xeon, ECBASE msgbus register on Atom, MSR on AMD APUs…)
All access to MMCFG range is mapped to PCI configuration cycles
MMCFG is split into consecutive 4kB large chunks, each is extended CFG header per bus/device/function
Access is done at memory offset within MMCFG range
MMCFG offset =
bus*32*8*1000h + dev*8*1000h + fun*1000h + offset

## Slide 160: ECAM (MMCFG) Address Mapping
Memory Address | PCI Express Configuration Space
A[(20+n-1):20] | Bus Numbers 1 ≤ n ≤ 8
A[19:15] | Device Number
A[14:12] | Function Number
A[11:8] | Extended Register Number
A[7:2] | Register Number
A[1:0] | Along with size of the access, used to generate Byte Enable

## Slide 161: Memory Mapped PCIe Configuration
chipsec_util.py mmio with ‘MMCFG’ BAR
# chipsec_util.py mmio list
-------------------------------------------------------------------------------
MMIO Range | BAR | Base | Size | En? | Description
-------------------------------------------------------------------------------
...
MMCFG | 00:00.0 + 60 | 00000000F8000000 | 00001000 | 1 | PCI Express Range
...
# chipsec_util.py mmio read MMCFG 0x0 0x4
[CHIPSEC] Read MMCFG + 0x0: 0x0A048086
# chipsec_util.py mmcfg <b> <d> <f> <off> <width> [value]
# chipsec_util.py mmcfg
[CHIPSEC] Memory Mapped Config Base: 0x00000000F8000000
# chipsec_util.py mmcfg 0 0 0 0x0 dword
[CHIPSEC] reading MMCFG register (00:00.0 + 0x00): 0xA048086
# chipsec_util.py mmcfg 0 0 0 0xF80DC byte
[CHIPSEC] reading MMCFG register (00:00.0 + 0xF80DC): 0x2A
It doesn’t work at MinnowBoard, because Bay Trail has different interface for MMCFG (use address 0xE0000000 as MMCFG)

## Slide 162: Memory Mapped I/O Registers
Devices may have more registers than I/O and PCIe CFG spaces can fit so BIOS may reserve physical address ranges for devices
Ranges are defined by Base Address Registers (BAR). MMIO registers are offsets off of base of MMIO ranges
Any access to such MMIO range is forwarded to the device which owns this range (local in the CPU or over a system bus to chipset) rather than decoded to DRAM
mmio command in CHIPSEC can be used to list predefined MMIO BARs, dump entire BAR, and read/write MMIO registers
# chipsec_util.py mmio list
-------------------------------------------------------------------------------
MMIO Range | BAR | Base | Size | En? | Description
-------------------------------------------------------------------------------
GTTMMADR | 00:02.0 + 10 | 00000000F0000000 | 00001000 | 1 | Graphics Translation Table Range
SPIBAR | 00:1F.0 + F0 | 00000000FED1F800 | 00000200 | 1 | SPI Controller Register Range
HDABAR | 00:03.0 + 10 | 0000007FFFFFF000 | 00001000 | 1 | HD Audio Controller Register Range
GMADR | 00:02.0 + 18 | 00000000E0000000 | 00001000 | 1 | Graphics Memory Range
DMIBAR | 00:00.0 + 68 | 00000000FED18000 | 00001000 | 1 | Root Complex Register Range
MMCFG | 00:00.0 + 60 | 00000000F8000000 | 00001000 | 1 | PCI Express Register Range
RCBA | 00:1F.0 + F0 | 00000000FED1C000 | 00004000 | 1 | PCH Root Complex Register Range
MCHBAR | 00:00.0 + 48 | 00000000FED10000 | 00008000 | 1 | Host Memory Mapped Register Range
...
# chipsec_util.py mmio read|write|dump <BAR_name> <off> <width> [value]
# chipsec_util.py mmio read SPIBAR 0x78 4
[CHIPSEC] Read SPIBAR + 0x78: 0x8FFF0F40

## Slide 163: CPU Model Specific Registers (MSR)
CPU contains many Model Specific Registers (MSR) to enable/disable/configure various features & read statuses
MSRs can be architectural (e.g. IA32_APIC_BASE) and specific to some CPU models (e.g. LBR_TO/FROM_MSR)
MSRs can be per logical CPU, core or entire CPU package
Reading from / writing to CPU MSRs:
# chipsec_util.py msr <msr> [eax] [edx] [cpu_id]
Specifying cpu_id allows access to MSRs of specific logical CPU
  When omitted the command reads/writes MSR for all logical CPU in the package

## Slide 164: IA-32 Control Registers (CR)
x86 CPU CRs control behavior/state of the logical CPU
Example:
  CR0.PG - paging enabled
  CR0.PE - protection enabled
  CR3 (PDBR) - physical address of page directory
  CR4.SMEP / CR4.SMAP
Reading from / writing to CRs:
# chipsec_util.py cpu cr <cpu_id> <cr_number> [value]
Access to CRs is per logical CPU, you need to specify the # of the logical CPU (cpu_id) in CHIPSEC

## Slide 165: Exercise 3.1
Read BIOS/SPI Security Configuration

## Slide 166: Exercise 3.2
Access Hardware Resources

## Slide 167: 3.2 Overview of Open Source CHIPSEC Framework

## Slide 168
*Other names and brands may be claimed as the property of others.

## Slide 169: Structure
chipsec_main.py runs modules (see modules dir below)
chipsec_util.py runs manual utilities (see utilcmd dir below)
/chipsec
/cfg platform specific configuration
/hal all the HW stuff you can interact with
/helper support for OS/environments
/modules modules (tests/tools/PoCs) go here
/utilcmd utility commands for chipsec_util

## Slide 170: OS/Environment Specific Helpers
CHIPSEC supports Windows, Linux and UEFI shell environment.
OS/environment specific helpers for:
Windows : helper\win\win32helper.py
Linux : helper\linux\helper.py
UEFI (shell) : helper\efi\efihelper.py
Abstracts for support various OS/environments, wrapper around platform specific code that invokes kernel driver implemented in: helper/oshelper.py
Call path:
Module (or util)  HAL component  oshelper
 helper [Linux]  OS native code [LKM]

## Slide 171: Helper Code Example
helper/oshelper.py
# Read/Write CR registers
def read_cr(self, cpu_thread_id, cr_number):
return self.helper.read_cr( cpu_thread_id, cr_number )
helper\linux\helper.py
def IOCTL_RDCR(): return _IOCTL_BASE + 0x10
. . .
class LinuxHelper:
def __init__(self):
import platform
self.os_system = platform.system()
self.os_machine = platform.machine()
. . .
self.init()
. . .
def read_cr(self, cpu_thread_id, cr_number):
self.set_affinity(cpu_thread_id)
cr = 0
in_buf = struct.pack( "3"+_PACK, cpu_thread_id, cr_number, cr)
unbuf = struct.unpack("3"+_PACK, fcntl.ioctl( _DEV_FH, IOCTL_RDCR(), in_buf ))
return (unbuf[2])
read_cr function in Linux helper invokes IOCTL within the kernel module
OS specific (Linux) helper class specific to each OS
IOCTL invoking handler in the kernel module (“read CR”)
OS independent function which all HAL components invoke (read_cr)

## Slide 172: Detecting the Platform
Each platform supports its own set of hardware resources (interfaces, configuration registers)
Different modules may be applicable to only specific platforms or family of platforms
To support above, CHIPSEC detects the platform it’s running on
Detection is done using Host Controller Device ID (b.d:f 00.00:0). Supported DIDs are in chipsec/chipset.py
    Tip: to add support of a new platform, add its description in Chipset_Dictionary. Alternatively, create custom_chipsets.py, add my_dict with additional DIDs and add them to the main dictionary using chipset.Chipset_Dictionary.update(my_dict)
After detection, configuration (XMLs) for the detected platform is initialized (chipset.init_xml_configuration)

## Slide 173: Detecting the Platform
# chipsec_util.py platform
Supported platforms:
DID | Name | Code | Long Name
-------------------------------------------------------------------------------------
...
0xa04 | Haswell | hsw | 4th Generation Core Processor (Haswell U/Y)
0xc08 | Haswell | hsw | Intel Xeon Processor E3-1200 v3 (Haswell CPU, C220 Series PCH)
0xa08 | Haswell | hsw | 4th Generation Core Processor (Haswell U/Y)
0xa00 | Haswell | hsw | 4th Generation Core Processor (Haswell U/Y)
0xc00 | Haswell | hsw | Desktop 4th Generation Core Processor (Haswell CPU / Lynx Point PCH)
0xc04 | Haswell | hsw | Mobile 4th Generation Core Processor (Haswell M/H / Lynx Point PCH)
0x158 | Ivy Bridge | ivb | Intel Xeon Processor E3-1200 v2 (Ivy Bridge CPU, C200/C216 Series PCH)
0x150 | Ivy Bridge | ivb | Desktop 3rd Generation Core Processor (Ivy Bridge CPU / Panther Point PCH)
0x154 | Ivy Bridge | ivb | Mobile 3rd Generation Core Processor (Ivy Bridge CPU / Panther Point PCH)
...
Platform: 4th Generation Core Processor (Haswell U/Y)
VID: 8086
DID: 0A04
Additional command-line options:
    --platform (-p): use it if you know the platform but CHIPSEC doesn’t auto detect the platform
    --ignore_platform (-i): avoid platform detection when using platform agnostic functionality (e.g. access to UEFI variables)

## Slide 174: HW Abstraction Layer (HAL)
HAL is the set of components providing access to various hardware resources on the platform
HAL components abstract HW access specific to OS environment and expose it via a set of common APIs consumed by all modules in any OS environment
HAL components are OS unaware and invoke common helper functions from OS agnostic oshelper.py
HAL components can be basic primitives or complex
  Basic primitive HAL components provide access to basic HW resource (Example: CPU I/O, MMIO, etc.)
  Complex HAL components use basic primitive HAL to implement access to higher level HW resources (Example: SPI access is implemented via MMIO access)

## Slide 175: HW Abstraction Layer (HAL)
File name | Description
hal/pci.py | Access to PCIe configuration space
hal/physmem.py | Access to physical memory
hal/msr.py | Access to CPU resources (for each CPU thread): Model Specific Registers (MSR), IDT/GDT
hal/mmio.py | Access to MMIO (Memory Mapped IO) BARs and Memory-Mapped PCI Configuration Space (MMCFG)
hal/spi.py | Access to SPI Flash parts
hal/ucode.py | Microcode update specific functionality
hal/io.py | Access to Port I/O Space
hal/smbus.py | Access to SMBus Controller in the PCH
hal/uefi.py | Main UEFI component using platform specific and common UEFI functionality
hal/uefi_common.py | Common UEFI functionality (EFI variables, db/dbx decode, etc.)
hal/uefi_platform.py | Platform specific UEFI functionality (parsing platform specific EFI NVRAM, capsules, etc.)
hal/interrupts.py | CPU Interrupts specific functions (SMI, NMI)
hal/cmos.py | CMOS memory specific functions (dump, read/write)
hal/cpuid.py | CPUID information
hal/spi_descriptor.py | SPI Flash Descriptor binary parsing functionality

## Slide 176: HAL: Basic HW Access
Basic HAL primitives is a set of HAL components which provide access to basic HW resources which are used to access any other HW resources
Each basic HAL primitive has its own OS native functions (e.g. in kernel module) implementing access to corresponding HW resource specific to that OS
Basic HAL primitives are IO, MEM, MSR, MMIO, PCIE, CR, CPUID, etc.
All other HAL components are complex and can be implemented using the above set of basic HAL primitives
Basic primitives can be accessed through Chipset instance:
cs = chipsec.chipset.cs()
pci_devs = cs.pci.enumerate_devices()

## Slide 177: HAL Example: SPI Flash Memory Access
SPI Flash Memory Access is a HAL component which implements access to system SPI flash memory devices
Current SPI HAL implementation uses hardware sequencing access (which predefines SPI flash opcodes and can operate in descriptor mode only)
Exposes the following API:
    read_spi, write_spi, erase_spi_block – access to SPI flash
    get_SPI_regions – returns SPI flash regions
    get_SPI_Protected_Range – returns SPI flash protected ranges
    display_SPI_Flash_Descriptor – decodes SPI flash descriptor
Accessed through chipsec_util spi/decode commands

## Slide 178: HAL Example: CPU Configuration Access
SPI Flash Memory Access is a HAL components which implement access to CPU HW resources (MSR, descriptor tables, microcode updates, CPUID, CR, interrupts ..)
Provide the following API:
    msr.read_msr, msr.write_msr – access to CPU MSRs
    msr.get_IDTR, msr.get_GDTR – read IDT/GDT
    ucode.ucode_update_id – read microcode update ID
    cpuid.cpuid – read CPU CPUID
    interrupts.send_SMI_APMC – send SMI through port B2h
    cr.read_cr, cr.write_cr – access to CPU Control Registers
Accessed through chipsec_util spi/cr/ucode/cupid/smi/idt/gdt commands

## Slide 179: HAL Example: UEFI
UEFI HAL components implements functionality to work with UEFI interfaces and structures
    Dumping UEFI Variables at run-time through UEFI API
    Extracting UEFI Variables from NVRAM store in SPI memory dump
    Decoding certificates/hashes from UEFI variables
    Parsing UEFI Volumes with executables from SPI memory dump
    Extracting and decoding S3 resume boot script
Common UEFI API consumed by modules is exposed through chipsec.hal.uefi
UEFI functionality can be common for all UEFI based firmware or can depend on BIOS implementation or UEFI version
    Common UEFI functionality is in hal/uefi_common.py
    BIOS dependent UEFI functionality is in hal/uefi_platform.py
Accessed through chipsec_util uefi command

## Slide 180: Platform Configuration
Each platform (chipset, CPU, devices) has it’s own configuration defined by registers/ranges in I/O, MMIO, PCIe CFG, MSR spaces...
  The same register may be defined at different offsets, even in different places on different platforms
  The definition of the register may change (bits, masks ..)
  Definitions of I/O or MMIO ranges change (location, size ..)
  Each platform may have its own set of internal devices or controllers
We don’t want to re-write modules for every new platform
It would be nice to be able do this (regardless of where register is):
reg = read_register( “MY_REGISER” )
reg_field = read_register_field( “MY_REGISER”, “MY_FIELD” )
CHIPSEC does that using configuration described in XML files for each platform, or per-feature, or common (chipsec/cfg directory)
Look for these lines in the output:
[*] loading common platform config from ‘..\chipsec/cfg\common.xml'..
[*] loading 'hsw' platform config from ‘..\chipsec/cfg\hsw.xml'..

## Slide 181: Platform Configuration: IO, MMIO…
Internal PCIe devices (devices, controllers, interfaces ..)
<pci>
<device name='HOSTCTRL' bus=‘0x0' dev='0x0' fun='0x0'../>
Memory Mapped I/O ranges (BARs)
<mmio>
<bar name=‘SPIBAR'.. reg=‘0xF0‘ enable_bit=‘0‘ ../>
Legacy port I/O ranges (BARs)
<io>
<bar name=‘ABASE'.. reg=‘0x40‘ ../>
Memory ranges
<memory>
<range name=‘LEGACY‘ address=‘0x00‘ size=‘0x100000‘ ../>

## Slide 182: Platform Configuration: Registers
Configuration registers
<registers>
<register name='BC' type='pcicfg' desc='BIOS Control'>
<field name='BIOSWE' bit='0' />
<field name='BLE' bit='1' />
..
<field name='SMM_BWP' bit='5' />
</register>
<register name='HSFS' type='mmio'>
..
<field name='FLOCKDN' bit='15'/>
</register>
<register name='IA32_SMRR_PHYSMASK' type='msr'>
<field name='Valid' bit='11'/>
</register>
</registers>

## Slide 183: Platform Configuration: “Controls”
Controls are important hardware lock bits, hardware protection enables, etc.
<control name=‘FlashLock' register=‘HSFS' field=‘FLOCKDN'/>
Modules can read the value of controls on any platform by the name regardless of where this control is (which register)
flock = chipsec.chipset.get_control(self.cs, 'FlashLockDown')

## Slide 184: CHIPSEC Has Two Entry-Points
chipsec_main.py (module launcher)
    Runs modules/tools automatically in a “security regression suite” mode
    Runs only modules applicable to current platform
    chipsec_main.py [--type BIOS]
    Or individually via “--module” command-line option
    chipsec_main.py --module common.bios_wp
chipsec_util.py (manual utilities)
    Provides manual access to HW resources (io, mem, pci ..)
    Individual utility commands are in utilcmd/*_cmd.py
    chipsec_util.py spi dump spi.bin
    (e.g. spi util command is implemented in spi_cmd.py file)

## Slide 185: Useful Options
-a (--module_args): Specifies arguments to each module individually
-n (--no_driver): Tells CHIPSEC to not launch Windows kernel driver (in case module doesn’t need it)
-x (--xml):Outputs result in JUnit compatible XML form which may be useful to integrate in validation env.
-t (--module_type): Run only modules of a specific type. Examples: BIOS, SMM, SECUREBOOT, HWCONFIG
    New types may be defined in chipsec/module_common.py
-v (--verbose): Logs all output from HAL components, helpers, dumps buffers, logs exception back-traces, etc.

## Slide 186: The Meat: CHIPSEC Modules
Modules encapsulate the main functionality of CHIPSEC:
Tests for known vulnerabilities in firmware
Tests for insufficient or incorrectly configured hardware protections
Hardware/firmware-level security tools
  Fuzzing tools for firmware interfaces/formats
  Manual security checkers (e.g. TE checker, DMA dumper)
  Reside in modules/tools directory are not launched automatically (only through –m command-line option)
PoC exploit modules demonstrating vulnerabilities

## Slide 187: The Meat: CHIPSEC Modules
All modules reside in chipsec/modules directory
Modules can be specific to one or more platforms or common for all supported platforms
  Modules in modules/<platform_code> directory will only be executed on <platform_code> platform
  Modules in modules/common directory will always be executed
Modules can implement is_supported function which can further check for supported platforms, OS environments (legacy vs UEFI boot), etc.

## Slide 188: Raising the Bar for Platform Security
Security Research
Platform Validation
Risk Profile
New Attacks
Test Modules for OEMs/IBVs
End-user Risk
Empowering End-Users to Make a Risk Decision
Source: https://cansecwest.com/slides/2014/Platform%20Firmware%20Security%20Assessment%20wCHIPSEC-csw14-final.pdf

## Slide 189: Summary of Modules in CHIPSEC
Issue | CHIPSEC Module | References
SMRAM Locking | common.smm | CanSecWest 2006
BIOS Keyboard Buffer Sanitization | common.bios_kbrd_buffer | DEFCON 16
SMRR Configuration | common.smrr | ITL 2009, CanSecWest 2009
BIOS Protection | common.bios_wp | BlackHat USA 2009, CanSecWest 2013, Black Hat 2013, NoSuchCon 2013
SPI Controller Locking | common.spi_lock | Flashrom, Copernicus
BIOS Interface Locking | common.bios_ts | PoC 2007
Secure Boot variables with keys and configuration are protected | common.secureboot.variables | UEFI 2.4 Spec , All Your Boot Are Belong To Us (here & here)
Memory remapping attack | remap | Preventing and Detecting Xen Hypervisor Subversions
DMA attack against SMRAM | smm_dma | Programmed I/O accesses: a threat to VMM?, System Management Mode Design and Security Issues
SMI suppression attack | common.bios_smi | Setup for Failure: Defeating Secure Boot
Access permissions to SPI flash descriptor | common.spi_desc | Flashrom
Access permissions to UEFI variables defined in UEFI Spec | common.uefi.access_uefispec | UEFI 2.4 Spec
Module to detect PE/TE Header Confusion Vulnerability | tools.secureboot.te | All Your Boot Are Belong To Us
Module to detect SMI input pointer validation vulnerabilities | tool.smm.smm_ptr | CanSecWest 2015

## Slide 190: 3.3 Developing Modules in CHIPSEC

## Slide 191: Module template
from chipsec.module_common import *
_MODULE_NAME = 'module_template'
class module_template (BaseModule):
def __init__(self):
BaseModule.__init__(self)
def check_something( self ):
self.logger.start_test( "Module Template" )
self.logger.log_passed_check( "Test Passed" )
return ModuleResult.PASSED
def is_supported(self):
return False
# --------------------------------------------------------------------------
# run( module_argv )
# Required function: run here all tests from this module
# --------------------------------------------------------------------------
def run( self, module_argv ):
return self.check_something()
Module starts here.
Can pass arguments to each module
Check if this module can run on this platform/OS
Return result
FAILED
PASSED
WARNING
SKIPPED
DEPRECATED
ERROR
Inherits BaseModule template

## Slide 192: Example: common.spi_lock
from chipsec.module_common import *
TAGS = [MTAG_BIOS]
class spi_lock(BaseModule):
def __init__(self):
BaseModule.__init__(self)
def is_supported(self):
return (self.cs.get_chipset_id() in \
[chipsec.chipset.CHIPSET_FAMILY_CORE,chipsec.chipset.CHIPSET_FAMILY_XEON])
def check_spi_lock(self):
self.logger.start_test( "SPI Flash Controller Configuration Lock" )
spi_lock_res = ModuleResult.FAILED
hsfs_reg = chipsec.chipset.read_register( self.cs, 'HSFS' )
chipsec.chipset.print_register( self.cs, 'HSFS', hsfs_reg )
flockdn = chipsec.chipset.get_register_field( self.cs, 'HSFS', hsfs_reg, 'FLOCKDN' )
if 1 == flockdn:
spi_lock_res = ModuleResult.PASSED
self.logger.log_passed_check( "SPI Flash Controller configuration is locked" )
else:
self.logger.log_failed_check( "SPI Flash Controller configuration is not locked" )
return spi_lock_res
def run( self, module_argv ):
return self.check_spi_lock()
Type of the check (e.g. BIOS security)
Checks SPI controller configuration is locked down

## Slide 193: Logging
Output module’s result:
log_passed/failed/skipped/warn_check()
Various output modes:
log(),error(),warning(),log_bad(),log_good(), log_important()
Turning VERBOSE output mode. Verbose mode logs everything from HAL, OS helpers etc.
self.logger.VERBOSE = True
# chipsec_main.py -m common.spi_lock –-verbose
Turn on/off logging by HAL components
self.logger.HAL
Utility logging (ON by default when CHIPSEC_UTIL is used)
self.logger.UTIL_TRACE
Flushing log output to a file (what if a fuzzer crashes OS?)
self.logger.flush()
self.logger.set_always_flush( True )

## Slide 194: 3.4 Developing Fuzzers for the System Firmware

## Slide 195: Passing arguments to CHIPSEC modules
More complex modules (e.g. tools, fuzzers, PoCs..) may define module specific command-line arguments to be passed by CHIPSEC via “-a” option:
# chipsec_main -m tools.fuzzer –a rnd,1000,0xDEADBEEF
def run( module_argv ):
logger.start_test( “Some fuzzer" )
if len(module_argv) > 2:
_mode = module_argv[0]
_attempts = int(module_argv[1])
_address = int(module_argv[2],16)
fuzz( _mode, _attempts, _address )
return ModuleResult.PASSED

## Slide 196
Training materials are available on Github
https://github.com/advanced-threat-research/firmware-security-training
Yuriy Bulygin @c7zero
Alex Bazhaniuk @ABazhaniuk
Andrew Furtak @a_furtak
John Loucaides @JohnLoucaides

## Slide 197: Security of BIOS/UEFI System Firmware from Attacker and Defender Perspectives Section 4. Common Attack Vectors against System Firmware
Yuriy Bulygin *
Alex Bazhaniuk *
Andrew Furtak *
John Loucaides **
* Advanced Threat Research, McAfee
** Intel

## Slide 198: License
Training materials are shared under Creative Commons “Attribution” license CC BY 4.0
Provide the following attribution:
Derived from “Security of BIOS/UEFI System Firmware from Attacker and Defender Perspective” training by Yuriy Bulygin, Alex Bazhaniuk, Andrew Furtak and John Loucaides available at https://github.com/advanced-threat-research/firmware-security-training

## Slide 199: Section 4. Common Attack Vectors Against BIOS and UEFI Firmware

## Slide 200: So What is System Firmware?
Hardware
I/O
Memory
Network
Graphics
System Firmware
(BIOS, UEFI firmware, Coreboot…)
CPU
Privilege
Operating System
Kernel + Drivers
App
App
Runtime
System
Firmware
(UEFI RT,
SMM)

## Slide 201: How Can System Firmware Be Attacked?
  Inadequate hardware write protections of firmware “ROM”
  Firmware update implementation
  Persistent Configuration (UEFI Variables, CMOS settings)
  Inadequate hardware protections of runtime firmware (System Management Interrupt Handlers)
  Runtime firmware (SMI handlers)
  Resume from sleep states
  Network stack implementation in firmware
  Other interfaces with OS/software, network, devices…

## Slide 202: Do BIOS Attacks Require Kernel Privileges?
Hardware
I/O
Memory
Network
Graphics
UEFI DXE Core / Dispatcher
UEFI OS Loaders
System Firmware (SEC/PEI)
OS Kernel
OS Driver
Malicious App
A matter of finding legitimate signed kernel driver which can be used on behalf of user-mode exploit as a confused deputy.
RWEverything driver signed for Windows 64bit versions (co-discovered with researchers from MITRE)

## Slide 203: 4.1 Attacking UEFI Secure Boot

## Slide 204: 4.1 (1) Attacking Secure Boot via Corruption of Firmware Root Signing Certificate (Platform Key)

## Slide 205: HW protection of FW in ROM
# chipsec_main.py --module common.bios_wp

## Slide 206: Platform Key certificate is stored in the NVRAM potion of SPI flash memory

## Slide 207: Modify PK in SPI if Writes are Allowed
Hardware
I/O
Memory
Network
Graphics
UEFI DXE Core / Dispatcher
UEFI OS Loaders
System Firmware (SEC/PEI)
DXE
Driver
UEFI
Boot Loader
Bootx64.efi
Bootmgfw.efi
Signed BIOS
Update
DXE
Driver
OS Kernel
OS Driver
OS Exploit
Modify UEFI BIOS Firmware in ROM

## Slide 208: Modifying Platform Key in NVRAM
Corrupt Platform Key EFI variable in NVRAM
    Name (“PK”) or Vendor GUID {8BE4DF61-93CA-11D2-AA0D-00E098032B8C}
    AuthenticatedVariableService DXE driver enters Secure Boot SETUP_MODE when correct “PK” EFI variable cannot be located in EFI NVRAM
    Main volatile SecureBoot variable is then set to DISABLE
    DXE ImageVerificationLib then assumes Secure Boot is off and skips Secure Boot checks
    Generic exploit, independent of the platform/vendor
    1 bit modification!

## Slide 210: 4.1 (2) Attacking Secure Boot via Setup UEFI Variable (On/Off, Verification Policies, CSM Enabled, “Clear Keys” control)

## Slide 211: Secure Boot Can Be Turned On/Off in BIOS Setup Options

## Slide 212: Looking for Enable Policy in SPI Dump…
  chipsec_util.py spi dump spi.bin

## Slide 213: Extracting Runtime UEFI Variables…
Secure Boot On Secure Boot Off

## Slide 214: Secure Boot On/Off is Stored in “Setup”
Secure Boot On Secure Boot Off

## Slide 215: Verification Policies are Stored in “Setup”
  Read ‘Setup’ UEFI variable and look for sequences
  04 04 04, 00 04 04, 05 05 05, 00 05 05
  We looked near Secure Boot On/Off Byte!
  Modify bytes corresponding to policies to 00 (ALWAYS_EXECUTE) then write modified ‘Setup’ variable

## Slide 216: Patching Image Verification Policies…
  [CHIPSEC] Reading EFI variable Name='Setup' GUID={EC87D643-EBA4-4BB5-A1E5-3F3E36B20DA9} from 'Setup_orig.bin' via Variable API..
  EFI variable:
  Name : Setup
  GUID : EC87D643-EBA4-4BB5-A1E5-3F3E36B20DA9
  Data :
  ..
  01 01 01 00 00 00 00 01 01 01 00 00 00 00 00 00 |
  00 00 00 00 00 00 01 01 00 00 00 04 04 |
  [CHIPSEC] (uefi) time elapsed 0.000
  [CHIPSEC] Writing EFI variable Name='Setup' GUID={EC87D643-EBA4-4BB5-A1E5-3F3E36B20DA9} from 'Setup_policy_exploit.bin' via Variable API..
  Writing EFI variable:
  Name : Setup
  GUID : EC87D643-EBA4-4BB5-A1E5-3F3E36B20DA9
  Data :
  ..
  01 01 01 00 00 00 00 01 01 01 00 00 00 00 00 00 |
  00 00 00 00 00 00 01 01 00 00 04 00 00 |
  [CHIPSEC] (uefi) time elapsed 0.203
OptionRomPolicy
FixedMediaPolicy
RemovableMediaPolicy

## Slide 217: CSM Enabled With Secure Boot
CSM allows legacy OS to boot on top of UEFI firmware without any Secure Boot checks
Some systems have CSM enabled by default with Secure Boot enabled and fallback to boot from MBR when UEFI signature verification fails
Mitigations: Never load CSM when Secure Boot is enabled

## Slide 218: Other Critical Secure Boot Config Stored in Unprotected Setup UEFI Variable
CSM Enable policy: allows malware to enable CSM with Secure Boot and boot from MBR
“Clear Secure Boot Keys” control: allows malware to clear all keys including PK thus disabling Secure Boot
“Restore Default Secure Boot Keys” control: allows malware to revert all keys and blacklist to potentially insecure “default” values
Mitigations: UEFI firmware must never store setting critical for Secure Boot in unprotected UEFI variables (such as Setup)

## Slide 219: 4.1 (3) Attacking Secure Boot via PE/TE Header Vulnerability

## Slide 220: Does firmware allow unsigned TE executables?
SecureBoot EFI variable doesn’t exist or equals to SECURE_BOOT_MODE_DISABLE? EFI_SUCCESS
File is not valid PE/COFF image? EFI_ACCESS_DENIED
SecureBootEnable NV EFI variable doesn’t exist or equals to SECURE_BOOT_DISABLE? EFI_SUCCESS
SetupMode NV EFI variable doesn’t exist or equals to SETUP_MODE? EFI_SUCCESS

## Slide 221: PE/TE Header Handling by the BIOS
  Decoded UEFI BIOS image from SPI Flash

## Slide 222: PE/TE Header Confusion Issue
  TE format doesn’t support signatures so BIOS has to deny loading such image
  In practice, BIOS implementations may differ…
  ExecuteSecurityHandler calls GetFileBuffer to read an executable image
  Which reads the image, checks if it has a valid PE/COFF header and returns EFI_LOAD_ERROR if not
  In case of an image load error, ExecuteSecurityHandler returns EFI_SUCCESS (0)
  Signature Checks are Skipped!

## Slide 223: PE/TE Header Confusion Attack
    Convert malicious PE/COFF EFI executable (bootkit.efi) to TE by replacing the image header
    Replace OS boot loaders with resulting TE EFI executable
    Vulnerable BIOS skips signature check for this executable
    Malicious bootkit.efi loads & patches original OS boot loader

## Slide 224: Exercise 4.1
Bypassing UEFI Secure Boot (PE/TE)

## Slide 225: 4.2 Attacking SPI Flash Protections

## Slide 226: BIOS Range is Not Protected in SPI
BIOS Write Protections often still not properly enabled on many systems
SMM based write protection of entire BIOS region is often not used: BIOS_CONTROL[SMM_BWP]
If SPI Protected Ranges (mode agnostic) are used (defined by PR0-PR4 in SPI MMIO), they often don’t cover entire BIOS & NVRAM
Some platforms use SPI device specific write protection but only for boot block/startup code or SPI Flash descriptor region
Mitigations:
Set BIOS_CONTROL[SMM_BWP]  1
Program SPI flash protected ranges (PRx) to cover BIOS range
References: Persistent BIOS Infection (used flashrom on legacy BIOS), Evil Maid Just Got Angrier, BIOS Chronomancy, A Tale Of One Software Bypass Of Windows 8 Secure Boot

## Slide 227: Checking with common.bios_wp
[*] running module: chipsec.modules.common.bios_wp
[x][ =======================================================================
[x][ Module: BIOS Region Write Protection
[x][ =======================================================================
[*] BIOS Control = 0x02
[05] SMM_BWP = 0 (SMM BIOS Write Protection)
[04] TSS = 0 (Top Swap Status)
[01] BLE = 1 (BIOS Lock Enable)
[00] BIOSWE = 0 (BIOS Write Enable)
[!] Enhanced SMM BIOS region write protection has not been enabled (SMM_BWP is not used)
[*] BIOS Region: Base = 0x00500000, Limit = 0x007FFFFF
SPI Protected Ranges
------------------------------------------------------------
PRx (offset) | Value | Base | Limit | WP? | RP?
------------------------------------------------------------
PR0 (74) | 87FF0780 | 00780000 | 007FF000 | 1 | 0
PR1 (78) | 00000000 | 00000000 | 00000000 | 0 | 0
PR2 (7C) | 00000000 | 00000000 | 00000000 | 0 | 0
PR3 (80) | 00000000 | 00000000 | 00000000 | 0 | 0
PR4 (84) | 00000000 | 00000000 | 00000000 | 0 | 0
[!] SPI protected ranges write-protect parts of BIOS region (other parts of BIOS can be modified)
[!] BIOS should enable all available SMM based write protection mechanisms or configure SPI protected ranges to protect the entire BIOS region
[-] FAILED: BIOS is NOT protected completely
# chipsec_main.py --module common.bios_wp

## Slide 228: SMI Suppression Attack (If SMM Based BIOS WP is Not Used)
Some systems write-protect BIOS by disabling BIOS Write-Enable (BIOSWE) and setting BIOS Lock Enable (BLE) but don’t use SMM based write-protection BIOS_CONTROL[SMM_BWP]
SMI event is generated when Update SW writes BIOSWE=1
Possible attack against this configuration is to block SMI events
E.g. disable all chipset sources of SMI: clear SMI_EN[GBL_SMI_EN] if BIOS didn’t set GBL_SMI_LOCK: Setup for Failure: Defeating SecureBoot
Another variant is to disable specific TCO SMI source used for BIOSWE/BLE (clear TCO_EN in SMI_EN if BIOS didn’t set TCO_LCK)
Mitigations:
Set BIOS_CONTROL[SMM_BWP]  1 and lock SMI configuration (set GBL_SMI_LCK, TCO_LCK)

## Slide 229: Checking with common.bios_smi
[*] running module: chipsec.modules.common.bios_smi
[x][ =======================================================================
[x][ Module: SMI Events Configuration
[x][ =======================================================================
[-] SMM BIOS region write protection has not been enabled (SMM_BWP is not used)
[*] PMBASE (ACPI I/O Base) = 0x0400
[*] SMI_EN (SMI Control and Enable) register [I/O port 0x430] = 0x00002033
[13] TCO_EN (TCO Enable) = 1
[00] GBL_SMI_EN (Global SMI Enable) = 1
[+] All required SMI events are enabled
[*] TCOBASE (TCO I/O Base) = 0x0460
[*] TCO1_CNT (TCO1 Control) register [I/O port 0x468] = 0x1800
[12] TCO_LOCK = 1
[+] TCO SMI configuration is locked
[*] GEN_PMCON_1 (General PM Config 1) register [BDF 0:31:0 + 0xA0] = 0x0A14
[04] SMI_LOCK = 1
[+] SMI events global configuration is locked
[+] PASSED: All required SMI sources seem to be enabled and locked!
# chipsec_main.py --module common.bios_smi

## Slide 230: Unlocked SPI Flash Config. / PRx
Some BIOS rely on SPI Protected Ranges (PR0-PR4 registers in SPI MMIO) to provide write protection of regions of SPI Flash
SPI Flash Controller configuration including PRx has to be locked down by BIOS via Flash Lockdown
If BIOS doesn’t lock SPI Controller configuration (by setting FLOCKDN bit in HSFS SPI MMIO register), malware can disable SPI protected ranges re-enabling write access to SPI Flash
Mitigations:
Set HSFS[FLOCKDN]  1

## Slide 231: Checking with common.spi_lock
[*] running module: chipsec.modules.common.spi_lock [x][ ======================================================= [x][ Module: SPI Flash Controller Configuration Lock [x][ ======================================================= [*] HSFSTS register = 0x0004E008 FLOCKDN = 1 [+] PASSED: SPI Flash Controller configuration is locked
# chipsec_main.py --module common.spi_lock

## Slide 232: Insecure Access Permissions in SPI Flash Descriptor
Master Read/Write Access to Flash Regions
--------------------------------------------------------
Region | CPU/BIOS | ME | GBe
--------------------------------------------------------
0 Flash Descriptor | R | R |
1 BIOS | RW | |
...
Access permissions to SPI flash descriptor
SPI flash memory is operating in descriptor mode, i.e. when valid flash descriptor is present in SPI flash
In descriptor mode, flash descriptor defines access permissions to various regions in SPI flash by different SPI bus masters, e.g. by CPU host software such as BIOS or OS
FD itself is a region and is access permission to FD allows writes from BIOS/OS after manufacturing then any code at BIOS/OS level can modify it

## Slide 233: Checking with common.spi_desc
[*] running module: chipsec.modules.common.spi_desc
[x][ =======================================================================
[x][ Module: SPI Flash Region Access Control
[x][ =======================================================================
[*] FRAP = 0x00004A4B << SPI Flash Regions Access Permisions Register (SPIBAR + 0x50)
[00] BRRA = 4B << BIOS Region Read Access
[08] BRWA = 4A << BIOS Region Write Access
[16] BMRAG = 0 << BIOS Master Read Access Grant
[24] BMWAG = 0 << BIOS Master Write Access Grant
[*] Software access to SPI flash regions: read = 0x4B, write = 0x4A
[+] PASSED: SPI flash permissions prevent SW from writing to flash descriptor
# chipsec_main.py --module common.spi_desc

## Slide 234: Exercise 4.2
BIOS/SPI Flash Protections

## Slide 235: 4.3 Attacking BIOS Update

## Slide 236: Exploiting Unsigned BMP Image File
Unsigned sections within BIOS update (e.g. boot splash logo BMP image)
BIOS displayed the logo before SPI Flash write-protection was enabled
EDK ConvertBmpToGopBlt() integer overflow followed by memory corruption during DXE while parsing BMP image
Copy loop overwrote #PF handler and triggered #PF
References:
Attacking Intel BIOS

## Slide 237: UEFI Exploit via .BMP Logo File
High DRAM
Page Tables
GDT
BMP boot logo file
Source: Attacking Intel BIOS by Rafal Wojtczuk & Alexander Tereshkin
UEFI copy loop
IDT / #PF ISR
Destination buffer
Page Fault due to access to unmapped page takes to overwritten #PF handler
BMP destination buffer overflow direction
BMP copy to dest buffer

## Slide 238: RBU Packet Parsing Vulnerability
Legacy BIOS with signed BIOS update
OS schedules BIOS update placing new BIOS image in DRAM split into RBU packets
Upon reboot, BIOS Update SMI Handler reconstructs BIOS image from RBU packets in SMRAM and verifies signature
Buffer overflow (memcpy with controlled size/dest/src) when copying RBU packet to a buffer with reconstructed BIOS image
References:
BIOS Chronomancy: Fixing the Core Root of Trust for Measurement
Defeating Signed BIOS Enforcement

## Slide 239: EDK2 Capsule BOF Vulnerabilities
Attacker sets up a capsule in memory, and when capsule update is called, BIOS parses the data provided by the attacker
Capsule Coalescing – when the blocks of a capsule are made contiguous, an integer overflow allowed attackers to control a memory copy operation.
Capsule Envelop – when blocks of the capsule are parsed, an integer overflow allowed attackers to cause a small allocation and large memory copy operation.
References:
Extreme Privilege Escalation on Windows 8/UEFI Systems

## Slide 240: 4.4 Attacking SMRAM

## Slide 241: Unlocked Compatible/Legacy SMRAM
D_LCK bit in SMRAMC register locks down configuration of Compatible SMM range (a.k.a. CSEG)
SMRAMC[D_OPEN]=0 forces access to legacy SMM space decode to system bus rather than to DRAM where SMI handlers are when CPU is not in System Management Mode (SMM)
When D_LCK is not set by BIOS, SMM space decode can be changed to open access to CSEG if CPU is not in SMM
References:
Using CPU SMM to Circumvent OS Security Functions
Using SMM For Other Purposes

## Slide 242: Compatible SMM Space: Normal Decode
0xBFFFF
Compatible SMRAM (CSEG)
SMM access to CSEG is decoded to DRAM, non-SMM access is sent to system bus
0xA0000
Non SMM access
SMRAMC [D_LCK] = 1
SMRAMC [D_OPEN] = 0
Source: Using CPU SMM to Circumvent OS Security Functions, Using SMM For Other Purposes

## Slide 243: Compatible SMM Space: Unlocked
0xBFFFF
Compatible SMRAM (CSEG)
Non-SMM access to CSEG is decoded to DRAM where SMI handlers can be modified
0xA0000
Non SMM access
SMRAMC [D_LCK] = 0
SMRAMC [D_OPEN] = 1
Source: Using CPU SMM to Circumvent OS Security Functions, Using SMM For Other Purposes

## Slide 244: Detecting with common.smm
[*] running module: chipsec.modules.common.smm [x][ ========================================================== [x][ Module: SMM memory (SMRAM) Lock [x][ ========================================================== [*] SMRAM register = 0x1A ( D_LCK = 1, D_OPEN = 0 ) [+] PASSED: SMRAM is locked
# chipsec_main.py --module common.smm

## Slide 245: SMRAM “Cache Poisoning” Attack
CPU executes from cache if memory type is cacheable
Ring0 exploit can make SMRAM cacheable (variable MTRR)
Ring0 exploit can then populate cache-lines at SMBASE with SMI exploit code (ex. modify SMBASE) and trigger SMI
CPU upon entering SMM will execute SMI exploit from cache
Mitigations: CPU System Management Range Registers (SMRR) forcing UC and blocking access to SMRAM when CPU is not in SMM. BIOS has to enable SMRR
References:
Attacking SMM Memory via Intel Cache Poisoning
Getting Into the SMRAM: SMM Reloaded

## Slide 246: Checking with common.smrr
[*] running module: chipsec.modules.common.smrr
[x][ =======================================================================
[x][ Module: CPU SMM Cache Poisoning / SMM Range Registers (SMRR)
[x][ =======================================================================
[+] OK. SMRR are supported in IA32_MTRRCAP_MSR
[*] Checking SMRR Base programming..
[*] IA32_SMRR_BASE_MSR = 0x00000000BD000006
BASE = 0xBD000000
MEMTYPE = 6
[+] SMRR Memtype is WB
[+] OK so far. SMRR Base is programmed
[*] Checking SMRR Mask programming..
[*] IA32_SMRR_MASK_MSR = 0x00000000FF800800
MASK = 0xFF800000
VLD = 1
[+] OK so far. SMRR are enabled in SMRR_MASK MSR
[*] Verifying that SMRR_BASE/MASK have the same values on all logical CPUs..
[CPU0] SMRR_BASE = 00000000BD000006, SMRR_MASK = 00000000FF800800
[CPU1] SMRR_BASE = 00000000BD000006, SMRR_MASK = 00000000FF800800
[CPU2] SMRR_BASE = 00000000BD000006, SMRR_MASK = 00000000FF800800
[CPU3] SMRR_BASE = 00000000BD000006, SMRR_MASK = 00000000FF800800
[+] OK so far. SMRR MSRs match on all CPUs
[+] PASSED: SMRR protection against cache attack seems properly configured

## Slide 247: SMRAM Memory Remapping Attack
Remap Window is used to reclaim DRAM range below 4Gb “lost” for Low MMIO
Defined by REMAPBASE/REMAPLIMIT registers in Memory Controller PCIe configuration space
MC remaps Reclaim Window access to DRAM below 4GB (above Top Of Low DRAM)
If not locked, OS malware can reprogram target of reclaim to overlap with SMRAM (or something else)
Mitigations: BIOS has to lock down Memory Map registers including REMAP*, TOLUD/TOUUD
References:
Preventing & Detecting Xen Hypervisor Subversions

## Slide 248: Memory Remapping: Normal Memory Map
Memory Reclaim/Remap Range
Low MMIO Range
TOLUD
4GB
SMRAM
REMAPBASE
REMAPLIMIT
Access is remapped to DRAM range ‘lost’ to MMIO (memory reclaimed)
Access
Source: Preventing & Detecting Xen Hypervisor Subversions

## Slide 249: Memory Remapping: Attacking SMRAM
Memory Reclaim/Remap Range
Low MMIO Range
TOLUD
4GB
SMRAM
REMAPBASE
REMAPLIMIT
Target range of memory reclaim changed to SMRAM
Access
Source: Preventing & Detecting Xen Hypervisor Subversions

## Slide 250: Checking with remap
[*] running module: chipsec.modules.remap
[x][ =======================================================================
[x][ Module: Memory Remapping Configuration
[x][ =======================================================================
[*] Registers:
[*] TOUUD : 0x000000011E600001
[*] REMAPLIMIT: 0x000000011E500001
[*] REMAPBASE : 0x0000000100000001
[*] TOLUD : 0xDFA00001
[*] TSEGMB : 0xDD000001
[*] Memory Map:
[*] Top Of Upper Memory: 0x000000011E600000
[*] Remap Limit Address: 0x000000011E5FFFFF
[*] Remap Base Address : 0x0000000100000000
[*] 4GB : 0x0000000100000000
[*] Top Of Low Memory : 0x00000000DFA00000
[*] TSEG (SMRAM) Base : 0x00000000DD000000
[*] checking memory remap configuration..
[*] Memory Remap is enabled
[+] Remap window configuration is correct: REMAPBASE <= REMAPLIMIT < TOUUD
[+] All addresses are 1MB aligned
[*] checking if memory remap configuration is locked..
[+] TOUUD is locked
[+] TOLUD is locked
[+] REMAPBASE and REMAPLIMIT are locked
[+] PASSED: Memory Remap is configured correctly and locked
# chipsec_main.py --module remap

## Slide 251: SMRAM Redirection via GFx Aperture
If BIOS doesn’t lock down memory config, boundary separating DRAM and MMIO (TOLUD) can be moved somewhere else. E.g. malware can move it below SMRAM to make SMRAM decode as MMIO
Graphics Aperture can then be overlapped with SMRAM and used to redirect MMIO access to memory range defined by PTE entries in Graphics Translation Table (GTT)
When CPU accesses protected SMRAM range to execute SMI handler, access is redirected to unprotected memory range somewhere else in DRAM
Mitigations: Similarly to Remapping Attack, BIOS has to lock down HW memory configuration (i.e. TOLUD) to mitigate this attack
References: System Management Mode Design and Security Issues (GART)

## Slide 252: Access in SMM: Normal Memory Map
Low MMIO Range
TOLUD
4GB
SMRAM
CPU executes instructions (mov) from SMRAM normally
mov ebx,imm32
Code fetch at SMBASE in SMM
Graphics Aperture
GTT MMIO
Access to GFx Aperture
GFx Memory
Access to GFx aperture (MMIO) is redirected to GFx DRAM range per GTT PTEs
GTT PTEs
Source: System Management Mode Design and Security Issues

## Slide 253: Access in SMM: GFx Aperture Redirection
Low MMIO Range
TOLUD
4GB
SMRAM
CPU executes instructions from fake SMRAM redirected to by MMIO GFx Aperture per malicious GTT PTEs
mov ebx,imm32
Code fetch at SMBASE in SMM
Graphics Aperture
GTT MMIO
GFx Memory
Fake SMRAM
GTT PTEs
Source: System Management Mode Design and Security Issues

## Slide 254: DMA Attacks on SMRAM
Protection from inbound DMA access is guaranteed by programming TSEG range
If BIOS doesn’t lock down TSEG range configuration, malware can move TSEG outside of where actual SMRAM is
Then program one of DMA capable devices (e.g. GPU device) or Graphics Aperture to access SMRAM
Mitigations: BIOS has to lock down configuration required to define range protecting SMRAM from inbound DMA access (e.g. TSEG range)
References:
Programmed I/O accesses: a threat to Virtual Machine Monitors?
System Management Mode Design and Security Issues

## Slide 255: DMA Access to SMRAM
Low MMIO Range
TOLUD
4GB
SMRAM
DMA access to SMRAM is blocked due to TSEG covering SMRAM
TSEG Base
GFx Mem Base

## Slide 256: DMA Access to SMRAM: DMA Attacks
Low MMIO Range
TOLUD
4GB
SMRAM
DMA access to SMRAM is not blocked as TSEG Base moved
Graphics Aperture
GTT MMIO
Access to GFx Aperture is redirected to SMRAM
TSEG Base
GFx Mem Base
GTT PTEs

## Slide 257: Checking with smm_dma
[*] running module: chipsec.modules.smm_dma
[x][ =======================================================================
[x][ Module: SMRAM DMA Protection
[x][ =======================================================================
[*] Registers:
[*] PCI0.0.0_TOLUD = 0xDFA00001 << Top of Low Usable DRAM (b:d.f 00:00.0 + 0xBC)
[*] PCI0.0.0_BGSM = 0xDD800001 << Base of GTT Stolen Memory (b:d.f 00:00.0 + 0xB4)
[*] PCI0.0.0_TSEGMB = 0xDD000001 << TSEG Memory Base (b:d.f 00:00.0 + 0xB8)
[*] IA32_SMRR_PHYSBASE = 0xDD000006 << SMRR Base Address MSR (MSR 0x1F2)
[*] IA32_SMRR_PHYSMASK = 0xFF800800 << SMRR Range Mask MSR (MSR 0x1F3)
[*] Memory Map:
[*] Top Of Low Memory : 0xDFA00000
[*] TSEG Range (TSEGMB-BGSM) : [0xDD000000-0xDD7FFFFF]
[*] SMRR Range (size = 0x00800000): [0xDD000000-0xDD7FFFFF]
[*] checking locks..
[+] TSEGMB is locked
[+] BGSM is locked
[*] checking TSEG alignment..
[+] TSEGMB is 8MB aligned
[*] checking TSEG covers entire SMRR range..
[+] TSEG covers entire SMRAM
[+] PASSED: TSEG is properly configured. SMRAM is protected from DMA attacks
# chipsec_main.py --module smm_dma

## Slide 258: 4.5 Attacking Hardware Configuration

## Slide 259: BIOS Top Boot-Block Swap Attack
Top Swap Mode allows fault-tolerant update of the BIOS boot-block
Enabled by BUC[TS] in Root Complex MMIO range
Chipset inverts A16 line (A16-A20 depending on the size of boot-block) of the address targeting ROM, e.g. when CPU fetches reset vector on reboot
Thus CPU executes from 0xFFFEFFF0 inside “backup” boot-block rather than from 0xFFFFFFF0
Top Swap indicator is not reset on reboot (requires RTC reset)
When not locked/protected, malware can redirect execution of reset vector to alternate (backup) boot-block
Mitigations: BIOS has to lock down Top Swap configuration (BIOS Interface Lock in General Control & Status register) & protect swap boot-block range in SPI
References: BIOS Boot Hijacking and VMware Vulnerabilities Digging

## Slide 260: BIOS Top Boot-Block Swap Attack
Original BIOS Boot-Block
0xFFFFFFF0
CPU normally fetches reset vector at FFFFFFF0h
0xFFFEFFF0
Alternate BIOS Boot-Block
(BUC[TS] = 1)
When TS is not locked:
Malware sets BUC[TS]
Out of reset, CPU starts at reset vector
Chipset inverts A16
CPU fetches instr. from alternate BB (at FFFEFFF0h) instead of FFFFFFF0h
Source: BIOS Boot Hijacking and VMware Vulnerabilities Digging

## Slide 261: Checking with common.bios_ts
[*] running module: chipsec.modules.common.bios_ts
[x][ =======================================================================
[x][ Module: BIOS Interface Lock and Top Swap Mode
[x][ =======================================================================
[*] BC = 0x2A << BIOS Control (b:d.f 00:31.0 + 0xDC)
[00] BIOSWE = 0 << BIOS Write Enable
[01] BLE = 1 << BIOS Lock Enable
[02] SRC = 2 << SPI Read Configuration
[04] TSS = 0 << Top Swap Status
[05] SMM_BWP = 1 << SMM BIOS Write Protection
[*] BIOS Top Swap mode is disabled
[*] BUC = 0x00000000 << Backed Up Control (RCBA + 0x3414)
[00] TS = 0 << Top Swap
[*] RTC version of TS = 0
[*] GCS = 0x00000021 << General Control and Status (RCBA + 0x3410)
[00] BILD = 1 << BIOS Interface Lock Down
[10] BBS = 0
[+] PASSED: BIOS Interface is locked (including Top Swap Mode)
# chipsec_main.py --module common.bios_ts

## Slide 262: 4.6 (1) Attacking SMI Handlers: SMI Call-Outs

## Slide 263: SMI Call-Out Vulnerabilities
OS level exploit stores payload in F-segment below 1MB (0xF8070 physical address)
Exploit has to also reprogram PAM to write to F-segment
Then triggers SW SMI via APMC port (I/O 0xB2)
SMI handler does CALL 0F000:08070 in SMM
References:
In 2009, SMI call-out vulnerabilities were discovered by Rafal Wojtczuk and Alex Tereshkin in EFI SMI handlers (Attacking Intel BIOS) and by Filip Wecherowski in legacy SMI (BIOS SMM Privilege Escalation Vulnerabilities)
Also discussed by Loic Duflot in System Management Mode Design and Security Issues
In 2015, researchers from LegbaCore found that many modern systems are still vulnerable to these issues How Many Million BIOS Would You Like To Infect (paper)

## Slide 264: Legacy SMI Call-Out Vulnerabilities
14 call-out vulnerabilities in one SMI handler!
BIOS SMM Privilege Escalation Vulnerabilities

## Slide 265: Legacy SMI Handlers Calling Out of SMRAM
Phys Memory
SMRAM
CALL F000:8070
Legacy BIOS Shadow
(F/ E-segments)
PA = 0xF0000
1 MB

## Slide 266: SMI Handlers Calling Out of SMRAM
Phys Memory
SMRAM
CALL F000:8070
Legacy BIOS Shadow
(F/ E-segments)
PA = 0xF0000
1 MB
Code fetch
in SMM

## Slide 267: SMI Handlers Calling Out of SMRAM
Phys Memory
SMRAM
CALL F000:8070
Legacy BIOS Shadow
(F/ E-segments)
PA = 0xF0000
1 MB
0xF8070: payload
0F000:08070 = 0xF8070 PA
Code fetch
in SMM

## Slide 268: UEFI SMI Call-Outs

## Slide 269: Modern EFI Firmware Also Affected
Untrusted Address Space
SMRAM
How Many Million BIOS Would You Like To Infect by LegbaCore
Untrusted UEFI RT/OS Code and Data
Trusted SMM Code and Data
UEFI services
UEFI RT API called by SMM code

## Slide 270: Statically analyzing SMI handlers for call-outs
Legacy SMI handlers do far calls to BIOS functions in F/E – segments (0xE0000 – 0xFFFFF physical memory) with specific code segment selectors

## Slide 271: Statically analyzing SMI handlers for call-outs
Searching where EFI DXE SMM drivers reference/fetch outside of SMRAM range of addresses with IDAPython plugin by LegbaCore:
How Many Million BIOS Would You Like To Infect by LegbaCore

## Slide 272: Dynamically detecting SMM call-outs
  DXE SMI drivers may call Runtime, Boot or DXE services API
  Find Runtime, Boot and DXE service tables containing UEFI API function pointers in memory (EFI System Table)
  Patch each function with detour code chaining the original function
  Enumerate and invoke all SMI handlers
  If SMI handler calls-out to some UEFI API, patch will get invoked
  Difficulties with this approach:
  it needs enumeration of all SMI handlers (with proper interfaces)
  SMI handlers may call functions not in RT/BS/DXE service tables

## Slide 273: Hooking runtime UEFI services…

## Slide 274: BIOS developers can easily detect call-outs
A “simple” ITP debugger script to step on branches and verify that target address of the branch is within SMRAM
Enable SMM Code Access Check HW feature on pre-production systems based on newer CPUs to weed out all “intended” code fetches outside of SMRAM from SMI drivers
NX based soft SMM Code Access Check patches by Phoenix look promising

## Slide 275: Using Paging to detect SMM call-outs
NX based soft SMM Code Access Check patches by Phoenix
SMM paging/NX are enabled when CPU enters SMM
PTEs outside of SMRAM have XD=1
#PF is signaled when SMI handler attempts to fetch from any page outside of SMRAM
XD == 1
Page Fault
SMRAM
#PF handler is executed inside SMRAM
Code fetch from a page outside SMRAM causes #PFault due to XD=1

## Slide 276: 4.6 (2) Attacking SMI Handlers: SMI Input Pointers

## Slide 277: SMI Input Pointer Vulnerabilities
When OS triggers SMI (e.g. SW SMI via I/O port 0xB2) it passes arguments to SMI handler via general purpose registers
OS may also pass an address (pointer) to a structure through which an SMI handler can read arguments & returns result
SMI handlers traditionally were not validating that such pointers are outside of SMRAM
If an exploit passes an address which is inside SMRAM, SMI handler may write onto itself on behalf of the exploit
References: A New Class of Vulnerability in SMI Handlers

## Slide 278: Pointer Arguments to SMI Handlers
Phys Memory
SMI Handlers in SMRAM
OS Memory
SMI Handler writes result to a buffer at address passed in RBX…
RAX (code)
RBX (pointer)
RCX (function)
RDX
RSI
RDI
SMI handler specific structure
SMI

## Slide 279: Pointer Vulnerabilities
Phys Memory
SMI Handlers in SMRAM
OS Memory
Exploit tricks SMI handler to write to an address inside SMRAM
RAX (code)
RBX (pointer)
RCX (function)
RDX
RSI
RDI
Fake structure inside SMRAM
SMI

## Slide 280: What can exploit overwrite in SMRAM?
Depending on the vulnerability, caller may control address to write, the value written, or both.
Often the caller controls the address (and knows offset off of the address) but doesn’t completely control the values written to the address by the SMI handler
What can an exploit overwrite in SMRAM without crashing?
    SMI entry point at SMBASE + 8000h
    Internal SMI handler’s state/flags inside SMRAM
    Contents of SMM state save area (registers)
Current value of SMBASE MSR is also saved in SMM state save at SMBASE + FEF8h area by CPU upon SMI
Saved value of SMBASE is restored upon executing RSM
Exploit can relocate SMRAM! Overwrite saved SMBASE to relocate SMRAM to unprotected memory location on next SMI

## Slide 281: How does exploit know where to write?
Exploit needs to know location of saved SMBASE
Dump contents of SMRAM
  Use another vulnerability (e.g. S3 boot script) to disable SMRAM protections and use DMA or graphics to read SMRAM
  Dump SPI flash contents, extract DXE SMM binaries and find SMRAM Init there
  Use similar SMI pointer read/write vulnerability
  Use hardware ITP offline
Find SMM state save area for each logical CPU
  SMM state save is at SMBASE + FC00h but SMBASE is different per CPU thread and per BIOS and some offset of TSEG/SMRR base
  Find SMI entry point (@ SMBASE + 8000h)
  Exploit can guess several locations of SMBASE (SMRR_PHYSBASE = SMBASE or SMM entry point, blind iteration through all offsets within SMRAM as potential saved SMBASE value)
  Or exploit can invoke SMI handler with known values in GPRs, then find where they are saved in SMRAM

## Slide 282: How does the attack work?
Phys Memory
SMI Handler
OS Memory
CPU stores current value of SMBASE in SMM save state area on SMI and restores it on RSM
RAX (code)
RBX (pointer)
RCX (function)
SMI handler specific structure
SMI
SMBASE
SMM State Save Area
Saved SMBASE value
SMI Entry Point (SMBASE + 8000h)

## Slide 283: How does the attack work?
Phys Memory
SMI Handler
OS Memory
Exploit prepares fake SMRAM with fake SMI handler outside of SMRAM
Fake SMI handler
SMBASE
Saved SMBASE value
SMM State Save Area
SMI Entry Point (SMBASE + 8000h)

## Slide 284: How does the attack work?
Phys Memory
OS Memory
SMI Handler
Exploit triggers SMI w/ RBX pointing to saved SMBASE address in SMRAM
SMI handler overwrites saved SMBASE on exploit’s behalf with address of fake SMI handler outside of SMRAM (e.g. 0 PA)
RAX (code)
RBX (pointer)
RCX (function)
SMI
SMBASE
Fake SMI handler
Saved SMBASE value
SMM State Save Area
SMI Entry Point (SMBASE + 8000h)

## Slide 285: How does the attack work?
Phys Memory
OS Memory
SMI Handler
Exploit triggers another SMI
CPU executes fake SMI handler at new entry point outside of original protected SMRAM because SMBASE location changed
SMI
SMBASE
Fake SMI handler
Saved SMBASE value
SMM State Save Area
New SMI Entry Point

## Slide 286: How does the attack work?
Phys Memory
OS Memory
SMI Handler
(SMRAM is not protected)
Fake SMI handler disables original SMRAM protection (disables SMRR)
Then restores original SMBASE values to switch back to original SMRAM
SMBASE
Fake SMI handler
Original saved SMBASE value
SMM State Save Area
New SMI Entry Point

## Slide 287: How does the attack work?
Phys Memory
OS Memory
SMI Handler
(SMRAM is not protected)
The SMRAM is restored but not protected by HW anymore
Any SMI handler may be installed/modified by malware
SMBASE
SMI Entry Point (SMBASE + 8000h)

## Slide 289: Input Pointers in EDKII: CommBuffer
  CommBuffer is a memory buffer used as a communication protocol between OS runtime and DXE SMI handlers
  Pointer to CommBuffer is stored in “UEFI” ACPI table in ACPI NVS memory accessible to OS
  Contents of CommBuffer are specific to SMI handler. Variable SMI handler read UEFI variable GUID, Name and Data from CommBuffer
Vulnerability | Ref | Affected | Reported by
CommBuffer SMM Overwrite/Exposure (3 issues) | Tianocore | EDK2 | Intel ATR
TOCTOU (race condition) Issue with CommBuffer (2 issues) | Tianocore | EDK2 | Intel ATR
SMRAM Overwrite in Fault Tolerant Write SMI Handler (2 issues) | Tianocore | EDK2 | Intel ATR
SMRAM Overwrite in SmmVariableHandler (2 issues) | Tianocore | EDK2 | Intel ATR

## Slide 290: Attacking CommBuffer Pointer
  SecurityPkg/VariableAuthenticated/RuntimeDxe:
SmmVariableHandler (
...
SmmVariableFunctionHeader = (SMM_VARIABLE_COMMUNICATE_HEADER *)CommBuffer;
switch (SmmVariableFunctionHeader->Function) {
case SMM_VARIABLE_FUNCTION_GET_VARIABLE:
SmmVariableHeader = (SMM_VARIABLE_COMMUNICATE_ACCESS_VARIABLE *)
SmmVariableFunctionHeader->Data;
Status = VariableServiceGetVariable (
...
(UINT8 *)SmmVariableHeader->Name + SmmVariableHeader->NameSize
);
VariableServiceGetVariable (
...
OUT VOID *Data
)
...
CopyMem (Data, GetVariableDataPtr (Variable.CurrPtr), VarDataSize);
SMRAM
CommBuffer

## Slide 291: Mitigating CommBuffer Attack
  SMI Handlers often have multiple commands, calling a different function for each command and take command specific arguments
  Note the calls to SmmIsBufferOutsideSmmValid. This checks for addresses to overlap with SMRAM range
SmiHandler() {
// check CommBuffer is outside SMRAM
if (!SmmIsBufferOutsideSmmValid(CommBuffer, Size)) {
return EFI_SUCCESS;
}
switch(command)
case 1: do_command1(CommBuffer);
case 2: do_command2(CommBuffer);
…
SMRAM
CommBuffer

## Slide 292: CommBuffer TOCTOU Issues
SMI handler checks that it won’t access outside of CommBuffer
What if SMI handler reads CommBuffer memory again after the check
DMA engine (for example GFx) can modify contents of CommBuffer
InfoSize = .. + SmmVariableHeader->DataSize + SmmVariableHeader->NameSize;
if (InfoSize > *CommBufferSize - SMM_VARIABLE_COMMUNICATE_HEADER_SIZE) {
Status = VariableServiceGetVariable (
...
(UINT8 *)SmmVariableHeader->Name + SmmVariableHeader->NameSize
);
VariableServiceGetVariable (
...
OUT VOID *Data
)
...
if (*DataSize >= VarDataSize) {
CopyMem (Data, GetVariableDataPtr (Variable.CurrPtr), VarDataSize);
Time of Check
Time of Use

## Slide 293: Validate input addresses before using them!
  Read pointer issues are also exploitable to expose SMRAM contents
  SMI handlers have to validate each address/pointer (+ offsets) they receive from OS prior to reading from or writing to it including returning status/error codes
    E.g. use/implement a function which validates address + size for overlap with SMRAM similar to SmmIsBufferOutsideSmmValid in EDKII

## Slide 294: Exercise 4.3
Security of SMI Handler Firmware

## Slide 295: Exercise 4.4
Attacking SMI Handlers

## Slide 296: 4.7 Attacking UEFI Variables

## Slide 297: Where does firmware store its settings?
UEFI BIOS stores persistent config as ”UEFI Variables” in NVRAM part of SPI Flash chip
UEFI Variables can be Boot-time or Run-time
Run-time UEFI Variables are accessible by OS via run-time Variable API (via SMI Handler)
OS exposes UEFI Variable API to [privileged] user-mode applications
SetFirmwareEnvironmentVariable
/sys/firmware/efi/efivars/ or /sys/firmware/efi/vars

## Slide 298: Lots of settings..
Secure Boot certificates
(PK, KEK, db, dbx)
Setup
BootOrder
AcpiGlobalVariable

## Slide 299: Dangerous Contents in UEFI Variables
Secure Boot configuration settings (see our All Your Boot Are Belong To Us)
Addresses to structures/buffers which firmware reads from or writes to during boot
Policies for hardware protections & locks such as BIOS Write Protection, Flash LockDown, BIOS Interface Lock
Policies disabling security features
Values of hardware configuration registers which firmware locks down
Data which firmware really really needs to just boot
Secrets: BIOS passwords in clear
Image Source: KEEP CALM-O-MATIC

## Slide 300: This cannot be good…
Overwrite early firmware code/data if (physical addresses) pointers are stored in unprotected variables
Bypass UEFI and OS Secure Boot if its configuration or keys are stored in unprotected variables
Bypass or disable hardware protections if their policies are stored in unprotected variables
Make the system unable to boot (brick) if setting essential to boot the system are stored in unprotected variables

## Slide 301: Who needs a Setup variable, anyway?
VU#758382
Storing Secure Boot settings in Setup could be bad
Now user-mode malware can clobber contents of Setup UEFI variable with garbage or delete it
Malware may also clobber/delete default configuration StdDefaults
The system may never boot again
The attack has been co-discovered with researchers from LegbaCore (Corey Kallenberg, Xeno Kovah) and MITRE Corporation (Sam Cornwell, John Butterworth).
Source: Setup For Failure

## Slide 302: Variable Attribute Checks in CHIPSEC
[*] running module: chipsec.modules.common.uefi.access_uefispec
[x][ =======================================================================
[x][ Module: Access Control of Variables Defined in UEFI Spec
[x][ =======================================================================
[*] Testing UEFI variables ..
[*] Variable BootOrder
[*] Variable dbx
[*] Variable ConOut
[*] Variable db
[*] Variable PK
[*] Variable BootCurrent
[*] Variable Timeout
[*] Variable KEK
[*] Variable Boot0000
[*] Variable Boot0001
[*] Variable SecureBoot
[*] Variable ConIn
..
[+] PASSED: All checked UEFI spec variables are protected according to spec
# chipsec_main.py --module common.uefi.access_uefispec

## Slide 303: Exercise 4.5
Security of UEFI Variables

## Slide 304: 4.8 Attacking Firmware S3 Resume

## Slide 305: VU# 976132 (CVE-2014-8274)
Security issues in system firmware due to handling of S3 resume boot script have been independently discovered by other security researchers
Rafal Wojtczuk of Bromium and Corey Kallenberg (@coreykal) of LegbaCore first published Attacks on UEFI Security (paper)
PoC exploit was described and developed by Dmytro Oleksiuk (@d_olex) in Exploiting UEFI boot script table vulnerability
Pedro Vilaça (@osxreverser) found related vulnerability in Mac EFI firmware (SPI Flash Configuration HW lock bit FLOCKDN is gone after resuming from S3)

## Slide 306: Waking the system from S3 “sleep” state
U/EFI System Firmware
Operating System
Platform Init
DXE
UEFI core
& drivers
BDS
Platform Init
S3 Boot
Script Table
Restores
hardware config
Script Engine
NORMAL BOOT
S3 RESUME
Apps

## Slide 307: Searching for ACPI global structure…
AcpiGlobalVariable UEFI variable points to a structure in memory (ACPI_VARIABLE_SET_COMPATIBILITY)
[CHIPSEC] Reading EFI variable Name=‘AcpiGlobalVariable’..
[uefi] EFI variable AF9FFD67-EC10-488A-9DFC-6CBF5EE22C2E:AcpiGlobalVariable:
18 be 89 da

## Slide 308: Searching for “S3 Boot Script”…
Pointer AcpiBootScriptTable at offset 0x18 in the structure ACPI_VARIABLE_SET_COMPATIBILITY points to the script table
typedef struct {
//
// Acpi Related variables
//
EFI_PHYSICAL_ADDRESS AcpiReservedMemoryBase;
UINT32 AcpiReservedMemorySize;
EFI_PHYSICAL_ADDRESS S3ReservedLowMemoryBase;
EFI_PHYSICAL_ADDRESS AcpiBootScriptTable;
..
} ACPI_VARIABLE_SET_COMPATIBILITY;

## Slide 309: “S3 Boot Script” table in memory

## Slide 310: Why “S3 Resume Boot Script”?
To speed up S3 resume, required HW configuration actions are written to an “S3 Resume Boot Script” by DXE drivers instead of running all configuration actions normally performed during boot

## Slide 311: S3 Boot Script is a Sequence of Platform Dependent Opcodes
00 00 00 00 21 00 00 00 02 00 0f 01 00 00 00 00
00 00 c0 fe 00 00 00 00 01 00 00 00 00 00 00 00
00 01 00 00 00 24 00 00 00 02 02 0f 01 00 00 00
00 04 00 c0 fe 00 00 00 00 01 00 00 00 00 00 00
00 00 00 00 08 02 00 00 00 21 00 00 00 02 00 0f
01 00 00 00 00 00 00 c0 fe 00 00 00 00 01 00 00
00 00 00 00 00 10 03 00 00 00 24 00 00 00 02 02
..
01 00 00 00 00 00 00 00 f0 00 02 00 67 01 00 00
20 00 00 00 01 02 30 04 00 00 00 00 21 00 00 00
00 00 00 00 de ff ff ff 00 00 00 00 68 01 00 00
..
d3 d1 4b 4a 7e ff

## Slide 312: Decoding Opcodes
# chipsec_util.py uefi s3bootscript
[000] Entry at offset 0x0000 (length = 0x21):
Data:
02 00 0f 01 00 00 00 00 00 00 c0 fe 00 00 00 00
01 00 00 00 00 00 00 00 00
Decoded:
Opcode : S3_BOOTSCRIPT_MEM_WRITE (0x02)
Width : 0x00 (1 bytes)
Address: 0xFEC00000
Count : 0x1
Values : 0x00
..
[359] Entry at offset 0x2F2C (length = 0x20):
Data:
01 02 30 04 00 00 00 00 21 00 00 00 00 00 00 00
de ff ff ff 00 00 00 00
Decoded:
Opcode : S3_BOOTSCRIPT_IO_READ_WRITE (0x01)
Width : 0x02 (4 bytes)
Address: 0x00000430
Value : 0x00000021
Mask : 0xFFFFFFDE

## Slide 313: S3 Boot Script Opcodes
I/O port write (0x00)
I/O port read-modify-write (0x01)
Memory write (0x02)
Memory read-modify-write (0x03)
PCIe configuration write (0x04)
PCIe configuration read-modify-write (0x05)
SMBus execute (0x06)
Stall (0x07)
Dispatch (0x08)
Dispatch2

## Slide 314: Processor I/O Port Opcodes
S3_BOOTSCRIPT_IO_WRITE/READ_WRITE opcodes in the S3 boot script write or RMW to processor I/O ports
Opcode below sends SW SMI by writing value 0xBD port 0xB2

## Slide 315: “Dispatch” Opcodes
S3_BOOTSCRIPT_DISPATCH/2 opcodes in the S3 boot script jumps to entry-point defined in the opcode

## Slide 316: Opcode Restoring BIOS Write Protection
S3_BOOTSCRIPT_PCI_CONFIG_WRITE opcode in the S3 boot script restores BIOS hardware write-protection (value 0x2A means BIOS hardware write protection is ON)

## Slide 317: Things that can go wrong
Address (pointer) to S3 boot script is stored in a runtime UEFI variable (e.g. NV+RT+BS AcpiGlobalTable)
The S3 boot script itself is stored in unprotected memory (ACPI NVS) accessible to the OS or DMA capable devices
The PEI executable parsing and interpreting the S3 boot script or any other executable needed for S3 resume is running out of unprotected memory
S3 boot script contains Dispatch (Dispatch2) opcodes with entry-points in unprotected memory
EFI firmware “forgets” to store opcodes which restore all required hardware locks and protections in S3 boot script

## Slide 318: Attacking FW on resume from sleep
U/EFI System Firmware
Operating System
Exploit
Exploit modifies S3 boot script table in memory
Upon resume, firmware executes rogue S3 script which disables HW protections
Platform PEI
DXE
UEFI core
& drivers
BDS
Platform PEI
S3 Boot
Script Table
Restores
hardware config
Script Engine
NORMAL BOOT
S3 RESUME
MODIFY

## Slide 319: Lucky you! BIOS protection is ON
PASSED: BIOS is write protected

## Slide 320: Sleep well
Found Boot Script in unprotected memory
Script Opcode restores BIOS Protection == ON
Changing it to OFF

## Slide 321: Oh wait…
FAILED: BIOS is NOT protected completely

## Slide 322: Opcode restoring BIOS Write Protection has been modified
S3_BOOTSCRIPT_PCI_CONFIG_WRITE opcode in the S3 boot script restored BIOS hardware write-protection in OFF state

## Slide 323: Checking with common.uefi.s3bootscript
# chipsec_main.py –m common.uefi.s3bootscript
[x][ ==========================================
[x][ Module: S3 Resume Boot-Script Protections
[x][ ==========================================
[!] Found 1 S3 boot-script(s) in EFI variables
[*] Checking S3 boot-script at 0x00000000DA88A018
[!] S3 boot-script is not in SMRAM
[*] Reading S3 boot-script from memory..
[*] Decoding S3 boot-script opcodes..
[*] Checking entry-points of Dispatch opcodes..
[-] Found Dispatch opcode (offset 0x014E) with Entry-Point: 0x00000000DA5C3260 : UNPROTECTED
[-] Entry-points of Dispatch opcodes in S3 boot-script are not in protected memory
[-] FAILED: S3 Boot Script and entry-points of Dispatch opcodes do not appear to be protected

## Slide 324: Exercise 4.6
Security of Firmware S3 Resume

## Slide 325: 4.9 Other Firmware Issues

## Slide 326: Pre-Boot Passwords Exposed in BIOS Keyboard Buffer
BIOS and Pre-OS applications store keystrokes in legacy BIOS keyboard buffer in BIOS data area (at physical address 0x41E)
BIOS, HDD passwords, Full-Disk Encryption PINs etc.
Some BIOS’es didn’t clear keyboard buffer
References:
Bypassing Pre-Boot Authentication Passwords

## Slide 327: Checking with common.bios_kbrd_buffer
[*] running module: chipsec.modules.common.bios_kbrd_buffer
[x][ =======================================================================
[x][ Module: Pre-boot Passwords in the BIOS Keyboard Buffer
[x][ =======================================================================
[*] Keyboard buffer head pointer = 0x1A (at 0x41A), tail pointer = 0x1C (at 0x41C)
[*] Keyboard buffer contents (at 0x41E):
1e 1f 20 21 22 23 24 25 26 27 28 29 2a 2b 2c 2d | !"#$%&'()*+,-
2e 2f 30 31 32 33 34 35 36 37 38 39 3a 3b 3c 3d | ./0123456789:;<=
[+] PASSED: Keyboard buffer is filled with common fill pattern
* Better check from EFI shell as OS/pre-boot app might have cleared the keyboard buffer
# chipsec_main.py --module common.bios_kbrd_buffer

## Slide 328
Training materials are available on Github
https://github.com/advanced-threat-research/firmware-security-training
Yuriy Bulygin @c7zero
Alex Bazhaniuk @ABazhaniuk
Andrew Furtak @a_furtak
John Loucaides @JohnLoucaides

## Slide 329: Security of BIOS/UEFI System Firmware from Attacker and Defender Perspectives Section 5. Hands-On Learning of EFI Environment
Yuriy Bulygin *
Alex Bazhaniuk *
Andrew Furtak *
John Loucaides **
* Advanced Threat Research, McAfee
** Intel

## Slide 330: License
Training materials are shared under Creative Commons “Attribution” license CC BY 4.0
Provide the following attribution:
Derived from “Security of BIOS/UEFI System Firmware from Attacker and Defender Perspective” training by Yuriy Bulygin, Alex Bazhaniuk, Andrew Furtak and John Loucaides available at https://github.com/advanced-threat-research/firmware-security-training

## Slide 331: Section 5. Hands-On Learning of EFI Environment

## Slide 332: 5.1 UEFI Shell

## Slide 333: Exercise 5.1
Getting Familiar with UEFI Shell

## Slide 334: Booting in UEFI Shell and Using Built-in Shell Commands
Replace bootloader with uefi shell:
$cp /boot/efi/EFI/boot/bootx64.efi /boot/efi/EFI/boot/bootx64.efi.bak
$cp /boot/efi/EFI/boot/shell_bootx64.efi /boot/efi/EFI/boot/bootx64.efi
Reboot system: $shutdown –r now
Test built-in shell commands from UEFI shell (list in next slide)
Recover original bootloader in UEFI shell:
shell> fs0:
shell> rm EFI\boot\bootx64.efi
shell> cp EFI\boot\bootx64.efi.bak EFI\boot\bootx64.efi

## Slide 335: Full UEFI Shell Commands/Apps
Tool | Description
help –b | Displays all UEFI shell internal commands
mode | Displays or changes the console output device mode.
memmap | Displays the memory map maintained by the EFI environment.
dmem | Displays the contents of system or device memory.
mm | Displays or modifies MEM/MMIO/IO/PCI/PCIE address space.
pci | Displays PCI device list or PCI function configuration space.
drivers | Displays the EFI driver list.
dmpstore | Displays all EFI NVRAM variables.
dh | Displays EFI handle information.
openinfo | Displays the protocols and agents associated with a handle.
dblk | Displays the contents of one or more blocks from a block device.
eficompress | Compress a file
efidecompress | Decompress a file
smbiosview | Displays SMBIOS information
loadpcirom | Loads a PCI Option ROM from the specified file.
edit/hexedit | Editor, hex editor
map | Defines a mapping between a user-defined name and a device handle.
vol | Displays the volume information for the file system that is specified by fs.

## Slide 336: 5.2 Building UEFI Firmware with EDK II

## Slide 337: Exercise 5.2
Building EDK2 and flashing SPI image

## Slide 338: Exercise Outline
Pre-requirement: Boot your system from USB stick. Connect your system to minnowboard through Ethernet cable and change IP address of your system to 192.168.1.1/24
Build open source EDK2 BIOS image for MinnowBoard on your system
Copy newly build Flash image to MinnowBoard (use scp command for it)
Flash it onto SPI using CHIPSEC
Read SPI image using CHIPSEC
Read SPI image using Dediprog HW SPI Flash programmer (optional)

## Slide 339: MinnowBoard MAX Build Resources
Documents, Release Nodes, Pre-built Firmware Binary images, Buildable Development Tree, Flash Update Utilities:
http://firmware.intel.com/projects/minnowboard-max
Using EDK II with Native GCC:
http://tianocore.sourceforge.net/wiki/Using_EDK_II_with_Native_GCC

## Slide 340: Create a Full Source Tree
Create a new folder (directory) on the root of your local hard drive (development machine) for use as your work space (In USB stick work space: "/home/user/Desktop/bios").
Checkout packages from: https://svn.code.sf.net/p/edk2/code/branches/UDK2014.SP1/
Download: MinnowBoard_MAX-{version}-Binary.Objects.zip
Download and patch openssl
Download edksetup.sh
Patch Vlv2TbltDevicePkg/bld_vlv.sh depends on GCC version
Or use script: bios_download_and_build.sh

## Slide 341: Apply debug patch
Apply debug patch to Vlv2TbltDevicePkg directory:
$cd Vlv2TbltDevicePkg
$patch –p 0 < ~/Desktop/patches/debug.patch
$cd ..

## Slide 342: Build MinnowBoard UEFI Firmware
Install iASL compiler
Install python, gcc, build-essential, subversion, uuid-dev
Run: $source edksetup.sh
Run:
$cd Vlv2TbltDevicePkg
$chmod +x bld_vlv.sh Build_IFWI.sh GenBiosId
Build EDKII Firmware:
  $./Build_IFWI.sh MNW2 Debug # also use this to rebuild BIOS
Firmware binary MNW2MAX_X64_D_0079_01_GCC.bin should now be in directory Stitch/
$ ls -lah Stitch/
-rw-r--r-- 1 user user 8.0M Jun 4 18:06 MNW2MAX_X64_D_0079_01_GCC.bin
Copy SPI image to MinnowBoard system (use scp command for coping).

## Slide 343: Read SPI Image Using CHIPSEC
Check SPI flash before/after erase and write operations.
CHIPSEC SPI commands:
$ chipsec_util spi dump rom.bin

## Slide 344: Flash Image Onto SPI Using CHIPSEC
Disable BIOS Write Protection in UEFI Setup (DONE)
Enable writes to BIOS region of SPI flash memory
  $python chipsec_util.py spi disable-wp
Erase full SPI flash memory chip
  for(( i=0; i<2048; i++ ))
  do
  R=$(echo "obase=16; $i*4096" | bc)
  python chipsec_util.py spi erase $R;
  done
Write newly built firmware image to SPI flash memory
$python chipsec_util.py spi write 0x0 <NEW_BUILT_BIOS_FILE>

## Slide 345: Changing BIOS WP in UEFI Setup

## Slide 346: Manipulating SPI Image Using Dediprog Hardware SPI Flash Programmer

## Slide 347: DediProg Software

## Slide 348: Manipulating SPI image using Bus Pirate as HW SPI Flash programmer

## Slide 349: Manipulating SPI Image Using Bus Pirate as HW SPI Flash Programmer
brown
purple
gray
red
white
black
Power
uHDMI
Ethernet
power
SD
card
USB
SATA
yellow
red
blue
gray
black
brown
orange
green
purple
white
USB
Minnowboard Max
Bus Pirate

## Slide 350: 5.3 EDK II Debug

## Slide 351: Exercise 5.3
EFI Debug

## Slide 352: Exercise Outline
Serial connection setup
Configure host system for debugging
Debug example with GDB

## Slide 353: Debug & Release Differences
DEBUG has a slower boot than RELEASE because of time it takes to display debug info
DEBUG has a larger image than RELEASE because the embedded debug info
DEBUG uses the serial port for debug string output
DEBUG contains the debug strings
DEBUG contains detailed debug strings that show the boot process and various ASSERT/TRACE errors

## Slide 354: Connect to UART port
To read UART output run minicom:
$minicom -D /dev/ttyUSB0

## Slide 355: Configuring the Debug Host (Done)
UDK debugger configuration:
Download 2013-WW52-UDK.Debugger.Tool-1.4-Linux.zip from:
http://firmware.intel.com/develop/intel-uefi-tools-and-utilities/intel-uefi-development-kit-debugger-tool
Install UDK debugger tool:
$./UDK_Debugger_Tool_v1_4_x86_64.bin
Check/change configuration file: /etc/udkdebugger.conf
$ cat /etc/udkdebugger.conf
[Debug Port]
Channel = Serial
Port = /dev/ttyUSB0
FlowControl = 0
BaudRate = 115200

## Slide 356: GDB on Debug Host System (Done)
Rebuild GDB on HOST:
Download gdb source code:
$ apt-get install gdb-source
$ cp /usr/src/gdb.tar.bz2 ~/Desktop/udk-debugger/
$ cd ~/Desktop/udk-debugger/
$ bzip2 -dc gdb.tar.bz2| tar -xf –
$ cd gdb
Download (from http://expat.sourceforge.net ) and install expat
Configure and build gdb with expat:
$./configure --with-expat --with-python
$ make && make install

## Slide 357: UEFI Firmware Debugging
Run UDK-GDB-SERVER
$/opt/intel/udkdebugger/bin/udk-gdb-server
Reboot Debug Target
Run GDB on Debug Host
$/home/user/Desktop/udk-debugger/gdb/gdb
(gdb) target remote :1234
Remote debugging using :1234

## Slide 358: Source Level Debug
(gdb) source /opt/intel/udkdebugger/script/udk-gdb-script
##############################################################
# This gdb configuration file contains settings and scripts
# for debugging UDK firmware.
# WARNING: Setting pending breakpoints is NOT supported!
# Additional commands for source level debugging will be added!
##############################################################
Loading symbol for address: 0x78e1472c
add symbol table from file "/home/user/Desktop/bios/Build/Vlv2TbltDevicePkg/DEBUG_GCC48/X64/MdeModulePkg/Core/Dxe/DxeMain/DEBUG/DxeCore.debug" at
.text_addr = 0x78dde260
.data_addr = 0x78e180e0
(udb) where

## Slide 359: Example: Setting Breakpoints
Set breakpoint on CoreLoadPeImage/CoreLoadImage functions
(udb) b CoreLoadPeImage
Breakpoint 1 at 0x78de2b22: file /home/user/Desktop/bios/MdeModulePkg/Core/Dxe/Image/Image.c, line 462.
(udb) b CoreLoadImage
Breakpoint 2 at 0x78de477c: file /home/user/Desktop/bios/MdeModulePkg/Core/Dxe/Image/Image.c, line 1409.
(udb) c
Continuing.
Loading symbol for address: 0x78de477c
Breakpoint 2, CoreLoadImage (BootPolicy=0 '\000', ParentImageHandle=0x78d78f18, FilePath=0x78d5f018, SourceBuffer=0x0, SourceSize=0, ImageHandle=0x78d5ee98)
at /home/user/Desktop/bios/MdeModulePkg/Core/Dxe/Image/Image.c:1409
1409 Tick = 0;

## Slide 360: Example: Setting Breakpoints
Set breakpoint to CoreExitBootServices:
(udb) break CoreExitBootServices
Breakpoint 1 at 0x78ddfdac: file /home/user/Desktop/bios/MdeModulePkg/Core/Dxe/DxeMain/DxeMain.c, line 731.
(udb) c
Continuing.
Loading symbol for address: 0x78ddfdac
Breakpoint 1, CoreExitBootServices (ImageHandle=0x768d8798, MapKey=3615) at /home/user/Desktop/bios/MdeModulePkg/Core/Dxe/DxeMain/DxeMain.c:731
731 gTimer->SetTimerPeriod (gTimer, 0);

## Slide 361: Example: Setting Breakpoints
Set breakpoint to DxeImageVerificationHandler which contains PE/TE header confusion vulnerability in Secure Boot implementation
(udb) break DxeImageVerificationHandler
(udb) c
Continuing.
Debug function DxeImageVerificationHandler using step:
(udb) step

## Slide 362: Useful GDB commands
Disassembly:
(gdb) display/i $pc
(gdb) set disassemble-next-line on
(gdb) show disassemble-next-line
(gdb) layout asm(udb)
Other:
(gdb) info breakpoints
(gdb) info args # Print args to the function of the current stack frame
(gdb) list # Shows the current or given source context.
(gdb) info registers # Show registers
(gdb) info frame # Show the stack frame info

## Slide 363: 5.4 EDK II Overview

## Slide 364: EDK II
Most of the source code written in C
Provides Flash Mapping Tool generating Firmware Volumes and the resulting SPI flash image
Build Existing EDK Modules
EDKII projects are made up of packages (DEC files)
Compiles to .EFI files: UEFI/DXE Driver, PEIM, UEFI Application, DXE Library

## Slide 365: MinnowBoard Max EDKII Source Tree
Package concept for each EDK II sub-directory
Platform specific packages (Vlv2..Pkg) are also there
EDK II build process reflects the package
# edksetup
# build -p Nt32Pkg\Nt32Pkg.dsc -a IA32

## Slide 366: EDK II Packages
MdePkg - Include files and libraries for Industry Standard Specifications
MdeModulePkg - Modules only definitions from the Industry Standard Specification are defined in the MdePkg
SecurityPkg – Implements security related functionality (Secure Boot, Authenticated Variables, etc.)
CryptoPkg – Provides crypto functionality
ShellPkg & NetworkPkg - Functionality of shell & network stack
IA32FamilyCpuPkg – Package supporting IA32 family processors
IntelFrameworkPkg - Include files and libraries for those parts of the Intel Platform Innovation Framework for EFI specifications not adopted “as is” by the UEFI or PI specifications
Nt32Pkg – Windows UEFI emulator

## Slide 367: EDKII File Extensions
.DSC - Platform Description file (recipe for creating a package, contains definitions to build the package)
.DEC - Package Declaration file
.INF - Module Definition (defines a component)
.FDF - Flash Description File (describes information about flash parts)
.FV - Firmware volume (FV) binary file

## Slide 368: Platform Configuration Database (PCD)
PCD options define parameters which allow modules to define firmware configuration without recompile/rebuild or source code change
There’s an API to access to PCD options
PCD options can store platform or feature configuration settings

## Slide 369: PCD Example
PCD options are defined in the DEC files in any package
    ./SecurityPkg/SecurityPkg.dec:
    gEfiSecurityPkgTokenSpaceGuid.PcdOptionRomImageVerificationPolicy
    |0x04|UINT32|0x00000001
Values of PCD options are set in DSC files
    [PcdsFixedAtBuild.IA32]
    ...
    gEfiIchTokenSpaceGuid.PcdIchAcpiIoPortBaseAddress|0x400

## Slide 370: 5.5 Building UEFI Applications/Drivers

## Slide 371: Building UEFI Application
UDKII User Manual describes a module building process in Chapter 3.4. You need to create a new package containing the module or add the module to existing package
http://tianocore.sourceforge.net/wiki/EDK_II_User_Documentation
UEFI Driver Wizard is of great help for module creation
http://tianocore.sourceforge.net/wiki/UEFI_Driver_Wizard

## Slide 372: Building UEFI Application
For this exercise, there’s a myapp package and a module generated with UEFI Driver Wizard and located in myapp folder in the UEFI source tree
myapp/
myapp.h
myapp.c
myapp.dec – package declaration file
myapp.dsc – platform build description file
myapp.inf – module information file
myapp.uni – unicode string file

## Slide 373: UEFI Driver Wizard

## Slide 374: Building a UEFI application
Linux:
#!/usr/bin/env bash
source edksetup.sh
build -a X64 -p myapp/myapp.dsc -m myapp/myapp.inf
Windows:
call edksetup.bat
build -a X64 -p myapp\myapp.dsc -m myapp\myapp.inf

## Slide 375: UEFI Shell

## Slide 376: Reading Command-Line Arguments
Some information can be found here:
Creating a Shell Application
http://tianocore.sourceforge.net/wiki/Creating_a_Shell_Application
From ShellLib we’ll use following structure
SHELL_PARAM_ITEM,
and functions
ShellCommandLineParseEx
ShellCommandLineGetFlag
ShellCommandLineGetValue

## Slide 377: Reading Command-Line Arguments
EFI_STATUS EFIAPI ShellCommandLineParseEx ( IN CONST SHELL_PARAM_ITEM * CheckList,
OUT LIST_ENTRY ** CheckPackage,
OUT CHAR16 **ProblemParam OPTIONAL,
IN BOOLEAN AutoPageBreak,
IN BOOLEAN AlwaysAllowNumbers )
Checks the command line arguments passed against the list of valid ones. Optionally removes NULL values first. If no initialization is required, then return RETURN_SUCCESS.
Parameters:
[in] CheckListThe pointer to list of parameters to check.
[out] CheckPackageThe package of checked values.
[out] ProblemParamOptional pointer to pointer to unicode string for the paramater that caused failure.
[in] AutoPageBreakWill automatically set PageBreakEnabled.
[in] AlwaysAllowNumbersWill never fail for number based flags.
Return values:
EFI_SUCCESS The operation completed sucessfully.
EFI_OUT_OF_RESOURCES A memory allocation failed.
EFI_INVALID_PARAMETER A parameter was invalid.
EFI_VOLUME_CORRUPTED The command line was corrupt.
EFI_DEVICE_ERROR The commands contained 2 opposing arguments. One of the command line arguments was returned in ProblemParam if provided.
EFI_NOT_FOUND A argument required a value that was missing. The invalid command line argument was returned in ProblemParam if provided.

## Slide 378: Reading Command-Line Arguments
BOOLEAN EFIAPI ShellCommandLineGetFlag ( IN CONST LIST_ENTRY *CONST CheckPackage,
IN CONST CHAR16 *CONST KeyString )
Checks for presence of a flag parameter.
Flag arguments are in the form of "-<Key>" or "/<Key>", but do not have a value following the key.
If CheckPackage is NULL then return FALSE. If KeyString is NULL then ASSERT().
Parameters:
[in] CheckPackage The package of parsed command line arguments.
[in] KeyStringThe Key of the command line argument to check for.
Return values:
TRUE The flag is on the command line.
FALSE The flag is not on the command line.

## Slide 379: Reading Command-Line Arguments
CONST CHAR16* EFIAPI ShellCommandLineGetValue ( IN CONST LIST_ENTRY *CONST CheckPackage,
IN CONST CHAR16 *CONST KeyString )
Checks for presence of a flag parameter.
Value parameters are in the form of "-<Key> value" or "/<Key> value".
If CheckPackage is NULL then return NULL.
Parameters:
[in] CheckPackage The package of parsed command line arguments.
[in] KeyStringThe Key of the command line argument to check for.
Return values:
NULL The flag is not on the command line.
!=NULL The pointer to unicode string of the value.

## Slide 380: Reading Command-Line Arguments
#define NAME_OPTION (L”-n”)
#define GUID_OPTION (L”-g”)
#define HELP_OPTION (L”-?”)
SHELL_PARAM_ITEM ParamList[] = {
{ NAME_OPTION, TypeValue },
{ GUID_OPTION, TypeValue },
{ HELP_OPTION, TypeFlag },
{ NULL, TypeMax },
};
LIST_ENTRY *ParamPackage;
ShellCommandLineParseEx(ParamList, &ParamPackage, NULL, TRUE, FALSE);

## Slide 381: Reading Command-Line Arguments
CONST CHAR16 *name_str = 0;
CONST CHAR16 *guid_str = 0;
if (ShellCommandLineGetFlag(ParamPackage,NAME_OPTION)){
name_str = ShellCommandLineGetValue (ParamPackage, NAME_OPTION);
}
if (ShellCommandLineGetFlag(ParamPackage, GUID_OPTION )) {
guid_str = ShellCommandLineGetValue (ParamPackage, GUID_OPTION );
}

## Slide 382: Using UEFI Runtime Services
Good reference: http://wiki.phoenix.com/wiki/index.php/EFI_RUNTIME_SERVICES
Global variable gRT, points to runtime service table, declared in
Library/UefiRuntimeServicesTableLib.h
Calling the service function:
gRT->GetVariable((CHAR16*)name_str, &guid,
&attributes, &size, buffer);

## Slide 383: Dependencies
Add include files to myapp.h:
#include <Library/ShellLib.h>
#include <Protocol/EfiShell.h>
#include <Protocol/EfiShellInterface.h>
#include <Protocol/EfiShellParameters.h>

## Slide 384: Dependencies
ShellPkg is used. Add ShellPkg and its dependencies to package files.
Add to myapp.inf [Packages] section
ShellPkg/ShellPkg.dec
Add [LibraryClasses] section
ShellLib to myapp.inf
Specify the location of ShellLib module INF file and dependecies in myapp.dsc [LibraryClasses]:
ShellLib|ShellPkg/Library/UefiShellLib/UefiShellLib.inf
FileHandleLib|ShellPkg/Library/UefiFileHandleLib/UefiFileHandleLib.inf
HiiLib|MdeModulePkg/Library/UefiHiiLib/UefiHiiLib.inf
SortLib|ShellPkg/Library/UefiSortLib/UefiSortLib.inf UefiHiiServicesLib|MdeModulePkg/Library/UefiHiiServicesLib/UefiHiiServicesLib.inf

## Slide 385: Exercise 5.4
Building UEFI Application

## Slide 386: References
TianoCore.org site documentation
http://sourceforge.net/projects/edk2/files/
EDK II INF File Specification, Version 1.2, Intel, 2009.
EDK II DSC File Specification, Version 1.2, Intel, 2009.
EDK II DEC File Specification, Version 1.2, Intel, 2009.
EDK II FDF (Flash Description File) File Specification, Version 1,2, Intel, 2009.
EDK II Build Specification, Version 1.2, Intel, 2009.

## Slide 387
Training materials are available on Github
https://github.com/advanced-threat-research/firmware-security-training
Yuriy Bulygin @c7zero
Alex Bazhaniuk @ABazhaniuk
Andrew Furtak @a_furtak
John Loucaides @JohnLoucaides

## Slide 388: Security of BIOS/UEFI System Firmware from Attacker and Defender Perspectives 6. Mitigations
Yuriy Bulygin *
Alex Bazhaniuk *
Andrew Furtak *
John Loucaides **
* Advanced Threat Research, McAfee
** Intel

## Slide 389: License
Training materials are shared under Creative Commons “Attribution” license CC BY 4.0
Provide the following attribution:
Derived from “Security of BIOS/UEFI System Firmware from Attacker and Defender Perspective” training by Yuriy Bulygin, Alex Bazhaniuk, Andrew Furtak and John Loucaides available at https://github.com/advanced-threat-research/firmware-security-training

## Slide 390: Section 6. Mitigations

## Slide 391: 6.1 UEFI Security Mechanisms

## Slide 392: UEFI Security Mechanisms in SecurityPkg
UEFI Secure Boot (DxeVerificationLib, Chapter 27.2 of UEFI 2.4 Spec)
Authenticated UEFI Variables (Chapter 7 of UEFI 2.4 Spec)
Random Number Generator (UEFI driver implementing the EFI_RNG_PROTOCOL from the UEFI2.4 specification)
User Identification (DXE drivers that support multi-factor user authentication), Chapter 31 of UEFI 2.4 spec
TCG Measured Boot (PEI Modules & DXE drivers implementing Trusted Computing Group measured boot EFI_TCG_PROTOCOL and EFI_TREE_PROTOCOL from the TCG and Microsoft MSDN websites, respectively)
Reference implementation in UDK SecurityPkg: https://svn.code.sf.net/p/edk2/code/trunk/edk2/SecurityPkg

## Slide 393: Other UEFI Security Mechanisms
UEFI Secure “Capsule” Update
  http://comments.gmane.org/gmane.comp.bios.tianocore.devel/8402
Variable Lock Protocol (Read-Only Variables)
  https://github.com/tianocore/edk2/blob/master/MdeModulePkg/Include/Protocol/VariableLock.h
Lock Box (protects memory contents across S3 sleep state):
  https://github.com/tianocore/edk2-MdeModulePkg/blob/master/Include/Protocol/LockBox.h

## Slide 394: Signed UEFI “Capsule” Update

## Slide 395: Signed Firmware Update
Source: Dell Signed Firmware Update (NIST 800-147)
BIOS Update Software Runs
Copy Firmware Update Payload and Signature to Memory
Set update Flag for BIOS
Request OS Reboot
Verify Update Payload Signature
BIOS Update Fail Error Msg
Reset BIOS Update Flag
Continue Boot
Reboot
Update BIOS and Firmware
Sign. Valid
BIOS Update Flag Set
Before Reboot
After Reboot
Yes
Yes
No
No

## Slide 396: Firmware Update Methods
UEFI Signed Capsule Update (update on reboot/S3)
Run-time SMM based update (by an SMI handler)
Update during BIOS Setup or from UEFI Shell
Remote BMC/IPMI Based Update
Update with physical switch

## Slide 397: UEFI “Capsules”
Source: UEFI Spec 2.4 Facilitates Secure Update by Jeff Bobzin (Insyde Software)
EFI_FIRMWARE_MANAGEMENT
_CAPSULE_HEADER
…
DXE Driver n (optional)
Payload 1
…
Payload n
EFI Capsule Header
Capsule Body
DXE Driver 1 (optional)

## Slide 398: UEFI Firmware Secure “Capsule” Update
Capsule update is a runtime service used to update UEFI FW
EFI capsule header
Update capsule
Firmware (optional DXE driver or update payload)
Firmware (optional DXE driver or update payload)
0x00000000
0xFFFFFFFF
UEFI/BIOS code
Update is initiated by update application/OS run‐time
Update application stores update “capsule” in DRAM or HDD on ESP (e.g. \EFI\CapsuleUpdate)
Upon reboot or S3 resume, FW finds and parses update capsule
After FW verifies digital signature of the capsule, FW writes new BIOS FV(s) to SPI flash memory
Source: UEFI Spec Version 2.4 Facilitates Secure Update UEFI Summerfest 2013

## Slide 399: Windows Firmware Update Package
Source : Windows UEFE Firmware Update Platform
UEFI Capsule
Windows Firmware Update Package
INF
CAT
UEFI Capsule
Update Device Firmware (e.g. EC)
Update System Firmware (UEFI FVs)
UEFI DXE Drivers
Signed by Microsoft
Signed by platform manufacturer
Signed by platform manufacturer or ODM
Signed with key matching cert in UEFI “db” variable for Secure Boot
Signed by Independent HW vendor (IHV)

## Slide 400: Firmware Update Rollback Protection
Version 1
Version 2
Version 3
Version 1
Version 2
Version 3
Version 4
Version 1
Version 2
Version 3
Version 4
Version 5
Each version fixes some issues with the previous. Since none are known to have security flaws, each new version allows updates to all older versions.
In V4, one of the issues fixed in V3 is realized to be a security fix. V4 will not allow updates to earlier versions, even V3 since it allows update to V2.
Version 5 can now accept only versions 5 and 4.
“Fence”

## Slide 401: Protecting UEFI Variables

## Slide 402: Protecting UEFI Variables
Separate critical settings from other and stored in different variables
If a variable is only used by the FW then it shouldn’t be Runtime
Make variables, not updateable by the OS, “read-only” (Variable Lock)
Use authenticated variables or Pcd for security settings
Don’t store debug/validation config. (e.g. HW locks) in variables
Whenever possible, allow only predefined values written to the variables
Validate contents of the variables (e.g. check pointers)
Have default config to allow system to boot if variable is corrupted
No sensitive data like BIOS passwords in variables in clear
Update of some variables may require physically present user
Other integrity checks on the contents of critical variables

## Slide 403: Why Authenticating Variables?
Secure Boot stores Platform Key (PK), Key Exchange Keys (KEK), white-list and black-list (db, dbx) in UEFI Variables
These need to be updateable yet protected from unauthorized software changing them
UEFI Authenticated Variable allows update/removal of authenticated variables only if new variable is signed and corresponding public cert already present in NVRAM (e.g. in KEK)
Counter or Time Based Authenticated Variable to prevent from replay attacks

## Slide 404: UEFI Variable Update
Source: A Tour Beyond Implementing UEFI Auth Variables in SMM with EDKII (Jiewen Yao, Vincent Zimmer)
SMM Variable Handler
SMM Comm Header
Variable Comm Header
VarAccess Comm Data
Data []
GUID[]
Name[]
Header GUID
Message Lengh
Function Id
Return Status
GUID
Data Size
Name Size
Attributes
Name[]
Data[]
SmmGetVar()
SmmSetVar()
……
Crypto Service
Flash Access
OS
Consumer
UEFI Variable
Driver
RING 0
OS
Runtime
Memory
Communication
Buffer
SMRAM
GetVariable()
SetVariable()

## Slide 405: UEFI Variable Authentication
Implementing a Secure Boot Path with UEFI by Jeff Bobzin (Insyde Software), UEFI Plugfest 2011
Hash
Sign
Variable
Variable
Digital Signature
Authenticated variable
Private Key
Counter-based authenticated variable
Monotonic counter against replay
SHA256 and RSA-2048
Time-based authenticated variable
EFI_TIME as rollback protection
SHA256 and X.509 certificate chains
  Intermediate certificate support (non-root certificate as trusted certificate)

## Slide 406: Variables Protection Attributes
Boot Service (BS)
  Accessible to DXE drivers / Boot Loaders at boot time
  No longer accessible at run-time (after ExitBootServices)
Authenticated Write Access
  Digitally signed with MonotonicCount incrementing each successive variable update to protect from replay attacks
  List of signatures supported by the firmware is stored in SignatureSupport variable
Time Based Authenticated Write Access
  Signed with TimeStamp (time at signing) to protect from replay attacks
  TimeStamp should be greater than TimeStamp in existing variable
  Used by Secure Boot: PK verifies PK/KEK update, KEK verifies db/dbx update
  certdb variable stores certificates to verify non PK/KEK/db(x) variables

## Slide 407: Time Based Authenticated Variables
Source: A Tour Beyond Implementing UEFI Auth Variables in SMM with EDKII (Jiewen Yao, Vincent Zimmer)
PKCS #7
Input VariableData
Authentication
ContentInfo
Certificate
SignInfo
Time Stamp
Type
Certificate
Data Content
N/A
X.509
Certificate
Signed Hash
(VariableName, VariableGuid, Attributes, TimeStamp, DataContent)

## Slide 408: Authenticated Variable Update Flow
Source: A Tour Beyond Implementing UEFI Auth Variables in SMM with EDKII (Jiewen Yao, Vincent Zimmer)
SetVariable
Return ERROR
ProcessVariable
ProcessVarWithPk
ProcessVarWithKek
UpdateVar
ProcessVarWithPk
Is PK?
Is KEK?
Is db/dbx?
PASS?
PASS?
PASS?
PASS?
Return ERROR
Return ERROR
UpdateVar
UpdateVar
Yes
Yes
Yes
Yes
Yes
Yes
No
No
No
No
No
No
No
Yes

## Slide 409: UEFI Variable Lock Protocol (Read-Only Variables)

## Slide 410: UEFI Read-Only Variables
EDKII implements VARIABLE_LOCK_PROTOCOL which provides a mechanism to make some variables “Read-Only” during Run-time OS
DXE drivers make UEFI variables Read-Only using RequestToLock() API before EndOfDxe event
After EndOfDxe event (e.g. during OS runtime), all registered variables cannot be updated or removed (enforced by SetVariable API)
Lock is transient, firmware has to request locking variables every boot. Before EndOfDxe variables are not locked

## Slide 411: Variable Lock Flow
Source: A Tour Beyond Implementing UEFI Auth Variables in SMM with EDKII (Jiewen Yao, Vincent Zimmer)
EarlyPei
RO Variable
EarlyDxe
RO Variable
RWC Variable
RWCL Variable
RWL Variable
RWC Variable
RW Variable
PEI PHASE
DXE PHASE
RT PHASE
SMM PHASE
ReadOnly
VariablePpi
Variable
ArchProtocol
VariableWrite
ArchProtocol
EndOfDxe
ExitBootService
Read only Variable Services
Read Write Variable Services With Reclaim
Variable Lock
Do not have variable Reclaim

## Slide 412: Protecting S3 Resume Boot Script (LockBox)

## Slide 413: EDK2 LockBox Overview
LockBox is a protected storage inaccessible to OS or DMA even across S3 sleep state
LockBox can be backed by anything (e.g. ReadOnly NV UEFI variable or encrypted media)
Current implementation uses SMRAM as LockBox
Firmware copies data it needs to protect from the OS and DMA to SMRAM via SaveLockBox() API
SMM LockBox is used in EDKII reference implementation to protect the S3 Resume Boot Script across S3 transition
UEFI LockBox details: A Tour Beyond BIOS Implementing S3 Resume with EDKII

## Slide 414: Saving S3 Boot Script to LockBox
SMRAM
EFI_BOOT_SCRIPT
SCRIPT_TABLE
PRIVATE_DATA
…
TableBase
TableLength
AtRuntime (TRUE)
InSmm (FALSE)
Script Header
Script Len (Opt)
Opcode 1
Opcode 2
Terminate Opcode
SAVE
EFI_BOOT_SCRIPT
Script Header
Script Len (Opt)
Opcode 1
Opcode 2
Terminate Opcode
SCRIPT_TABLE
PRIVATE_DATA
…
TableBase
TableLength
AtRuntime (TRUE)
InSmm (TRUE)

## Slide 415: Saving S3 Boot Script to LockBox
SaveBootScriptDataToLockBox():
…
//
// mS3BootScriptTablePtr->TableLength does not include EFI_BOOT_SCRIPT_TERMINATE, because we need add entry at runtime.
// Save all info here, just in case that no one will add boot script entry in SMM.
//
Status = SaveLockBox (
&mBootScriptDataGuid,
(VOID *)mS3BootScriptTablePtr->TableBase,
mS3BootScriptTablePtr->TableLength +
sizeof(EFI_BOOT_SCRIPT_TERMINATE)
);
ASSERT_EFI_ERROR (Status);
Status = SetLockBoxAttributes (&mBootScriptDataGuid, LOCK_BOX_ATTRIBUTE_RESTORE_IN_PLACE);
https://svn.code.sf.net/p/edk2/code/trunk/edk2/MdeModulePkg/Library/PiDxeS3BootScriptLib/BootScriptSave.c

## Slide 416: 6.2 Hardware Based Firmware Protections

## Slide 417: Protection From SMM Cache Attacks

## Slide 418: System Management Range Registers (SMRR)
2 MSRs: SMRR_PHYSBASE, SMRR_PHYSMASK
Physical address PA hits SMRR range when:
PA & SMRR_PHYSMASK == SMRR_PHYSBASE & SMRR_PHYSMASK
Force region of memory defined by SMRR as un-cacheable (UC) for non-SMM software access (e.g. from OS) to prevent cache fills in the range
Non-SMM memory writes are dropped, non-SMM memory reads return all F’s
If CPU is in SMM, SMRR define memory type (typically WB)

## Slide 419: SMM Code Access Check

## Slide 420: Mitigating SMM Call-Outs
Don’t call any function outside of protected SMRAM
    Violates “No read down” rule of classical Biba integrity model
Enable SMM Code Access Check CPU protection
    Available starting in Haswell based CPUs
    Available if MSR_SMM_MCA_CAP[58] == 1
    When enabled, attempts to execute code not within the ranges defined by the SMRR while inside SMM result in a Machine Check Exception

## Slide 421: Blocking Code Fetch Outside of SMRAM
Phys Memory
SMRAM
CALL F000:8070
Legacy BIOS Shadow
(F/ E-segments)
PA = 0xF0000
1 MB
0xF8070: payload
0F000:08070 = 0xF8070 PA
Code fetch
in SMM  causes MC exception

## Slide 422: Function Pointers Outside of SMRAM (DXE SMI)
Phys Memory
SMRAM
mov ACPINV+x, %rax
call *0x18(%rax)
ACPI NV Area
payload
1. Read function pointer from ACPI NVS memory (outside SMRAM)
Pointer to payload
2. Call function pointer (payload outside SMRAM)
-- causes MCE!

## Slide 423: Paging based SMM code access check
NX based soft SMM Code Access Check patches by Phoenix
SMM paging/NX are enabled when CPU enters SMM
PTEs outside of SMRAM have XD=1
#PF is signaled when SMI handler attempts to fetch from any page outside of SMRAM
XD == 1
Page Fault
SMRAM
#PF handler is executed inside SMRAM
Code fetch from a page outside SMRAM causes #PFault due to XD=1

## Slide 424: Hardware Secure Boot

## Slide 425: Example: Intel® Boot Guard
OEM PI Verification
Using PI Signed
Firmware Volumes Vol 3, section 3.2.1.1
of PI 1.3 Specification
OEM UEFI 2.4 Secure Boot
Chapter 27.2 of
The UEFI 2.4 Specification
http://www.intel.com/content/dam/www/public/us/en/documents/product-briefs/4th-gen-core-family-mobile-brief.pdf
CPU/SOC
(Intel)
Intel Boot Guard
Start Block PEI
(OEM)
Executable
Policy
Policy Engine
Enforces
BIOS DXE/UEFI
(OEM)
Executable
OS Loader/Kernel
(OSV)
Executable
Policy
Policy Engine
Enforces
Policy
Policy Engine
Enforces

## Slide 426: Example: Intel® Boot Guard
CPU loads BootGuard specific Authenticated Code Module (ACM) to validate the initial firmware boot block (IBB)
IBB validation includes signature verification and/or measurement into the TPM PCR
Verified boot uses 2 manifests: OEM public key manifest and IBB manifest structures
OEM programs 256 bits of SHA-256 of RSA public key used by ACM to verify the IBB signature into one-time field programmable fuses at the manufacturing
OEM programs policies into the fuses
    Verified and/or Measured Boot
    ACM or IBB verification failure response

## Slide 427: Verified vs Measured Boot
Credit: Monty Wiseman
Reset
Execute
Execute
Execute
Execute
Execute
Execute
OS/Apps
Verify sig
TPM
Legacy Boot
Measured Boot
Verified Boot
Assumption
OS/Apps
OS/Apps
Check signatures
Check measurements (attestation)
TPM signs “measurements” used to verify against manifest
Verify sig
“Measure”
“Measure”
TPM
TPM
Reset
Reset
Decrypt secrets (unseal)
TPM decrypts secrets to OS (e.g. FDE key)

## Slide 428: Hardware Based System Firmware Update

## Slide 429: Example: Intel® BIOS Guard
Source: http://www.intel.com/content/dam/www/public/us/en/documents/white-papers/security-technologies-4th-gen-core-retail-paper.pdf
OEM signed updated package
SMM
Flash control hardware
BIOS
BIOS Guard runs in
AC-RAM for this function
Enable-able only by BIOS Guard enforced by HW
SPI Flash with BIOS
BIOS Guard update agent

## Slide 430: SMM BIOS Update Trust Boundary
For runtime BIOS Update (e.g. on server platforms), all complex SMI handlers code is in the trust boundary of the firmware update
Different systems have different SMI handlers which makes it difficult to ensure consistent security level of SMI code across all system and security level of firmware update
BIOS Guard reduces SMI handler attack surface, using one signed BIOS Guard authenticated code module (ACM)
Platforms enabling BIOS Guard only need to use one module for a given processor generation

## Slide 431: Trust Boundary with BIOS Guard
BIOS Guard Based
System Firmware Update Trust Boundary
SMM Based
System Firmware Update Trust Boundary
All BIOS until SMM lockdown
Early BIOS
BIOS Guard module
All SMI handlers
(vary between platforms)
Major advantage of Intel BIOS Guard is attack surface reduction from all possible SMI handlers on all platforms to one BIOS Guard ACM module

## Slide 432: BIOS Guard Based Firmware Update
BIOS Guard can update contents of the BIOS region in system SPI flash and EC firmware on EC flash memory
BIOS Guard module is authenticated code module (ACM) executing in internal processor AC RAM
When BIOS Guard is enabled, only BIOS Guard module is able to write to system SPI flash memory
BIOS Guard verifies the signature of a firmware update package signed by a platform manufacturer prior to writing to system SPI flash memory

## Slide 433: 6.3 Trusted (Measured) Boot with Trusted Platform Module

## Slide 434: Secure or Measured Boot?
How do you mitigate risk of a lost/stolen laptop?
    Example: Software based Full Disk Encryption like Microsoft BitLocker
How do you attack full disk encryption?
    Example: Evil Maid attack infecting the firmware or boot loaders to log/steal FDE PIN

## Slide 435: Protecting Against the Evil Maid Attack
  Evil Maid Attack
  Get a system with Trusted Platform Module (TPM)
  You trust TPM (including its firmware) & system firmware (BIOS)
    Problem: Angry Evil Maid Attack
  During measured boot process, initial firmware creates hashes of the next firmware stages and boot loaders what is known as measuring
  Initial firmware is Static Root of Trust for Measurement (STRM)
  FDE enabled boot loader then seals volume encryption key(s) to these measurements in the PCRs
  Thus each boot, the keys can only be decrypted (unsealed) and the volume decrypted when all firmware and boot loaders have the same measurements (hashes)

## Slide 436: Measured Boot
Hash into TPM PCRs instead of signature check
Hardware
I/O
Memory
Network
Graphics
UEFI DXE Core / Dispatcher
UEFI OS Loaders
System Firmware (SEC/PEI)
DXE
Driver
UEFI
Boot Loader
Bootx64.efi
Bootmgfw.efi
Signed BIOS
Update
DXE
Driver
OS Kernel
OS Driver
OS Driver
DXE
OROM
DXE
OROM
UEFI App
UEFI App
Hashing
Driver
Signing
TPM

## Slide 437: Measurements into TPM PCRs
⊗ Initial startup FW at CPU reset vector
PCR[0 ] ← CRTM, UEFI Firmware, PEI/DXE [BIOS], UEFI Boot and Runtime Services, Embedded EFI OROMs, SMI Handlers, Static ACPI Tables
PCR[1 ] ← SMBIOS, ACPI Tables, Platform Configuration Data
PCR[2 ] ← EFI Drivers from Expansion Cards [Option ROMs]
PCR[3 ] ← [Option ROM Data and Configuration]
PCR[4 ] ← UEFI OS Loader, UEFI Applications [MBR]
PCR[5 ] ← EFI Variables, GUID Partition Table [MBR Partition Table]
PCR[6 ] ← State Transitions and Wake Events
PCR[7 ] ← UEFI Secure Boot keys (PK/KEK) and variables (db, dbx..)
PCR[8 ] ← TPM Aware OS specific hashes [NTFS Boot Sector]
PCR[9 ] ← TPM Aware OS specific hashes [NTFS Boot Block]
PCR[10] ← [Boot Manager]
PCR[11] ← BitLocker Access Control

## Slide 438: UEFI Secure Boot vs TCG Trusted Boot
Source: Secure Boot Ecosystem Challenges by Vincent Zimmer
UEFI Secure Boot
UEFI authenticates OS loader (pub key and policy)
Checks signature of before loading
UEFI Secure boot will stop platform boot if signature is not valid
UEFI requires remediation mechanisms if boot fails
UEFI Firmware
UEFI OS Ldr, Drivers
Kernel
Drivers
Apps
TPM
UEFI
Record to PCR
UEFI TCG Measured Boot
UEFI PI measures OS loader & UEFI drivers into TPM PCRs
TCG Trusted boot never fails to boot firmware/OS
Incumbent upon other SW to make security decision using attestation and/or unsealing

## Slide 439: What does it all mean?
Secure Boot
  System firmware looks for authorized signature before execution
  Measured Boot
  System firmware hashes images into PCRs before execution
  Both
  Trust system firmware to do checks (hash or sig check)
  Only do startup checks, not runtime

## Slide 440: Example with Measured Boot
Let’s look at some PCRs
    cat /sys/class/misc/tpm0/device/pcrs
Let’s seal something using the keyctl command:
    the “trusted” keys are encrypted and sealed in the TPM
    options include sealing to PCR values
    keyctl add trusted name “new keylen [options]” ring

## Slide 441
Training materials are available on Github
https://github.com/advanced-threat-research/firmware-security-training
Yuriy Bulygin @c7zero
Alex Bazhaniuk @ABazhaniuk
Andrew Furtak @a_furtak
John Loucaides @JohnLoucaides

## Slide 442: Security of BIOS/UEFI System Firmware from Attacker and Defender Perspectives 7. Hands-On System Firmware Forensics
Yuriy Bulygin *
Alex Bazhaniuk *
Andrew Furtak *
John Loucaides **
* Advanced Threat Research, McAfee
** Intel

## Slide 443: License
Training materials are shared under Creative Commons “Attribution” license CC BY 4.0
Provide the following attribution:
Derived from “Security of BIOS/UEFI System Firmware from Attacker and Defender Perspective” training by Yuriy Bulygin, Alex Bazhaniuk, Andrew Furtak and John Loucaides available at https://github.com/advanced-threat-research/firmware-security-training

## Slide 444: Section 7. Hands-on System Firmware Forensics

## Slide 445: 7.1 Live Forensic / Incident Response
Important: software based forensics is not reliable to detect firmware compromise. Firmware rootkits can interfere with software based forensics.

## Slide 446: Live System Forensics
To perform system firmware forensics, the following components can be extracted & analyzed:
Layout and entire contents of SPI Flash memory
BIOS/UEFI firmware including EFI binaries and NVRAM
Runtime or Boot UEFI Variables (non-volatile and volatile)
UEFI Secure Boot certificates (PK, KEK, db/dbx ..)
UEFI system and configuration tables (Runtime, Boot and DXE services)
UEFI S3 resume boot script table
PCIe option (expansion) ROMs

## Slide 447: Live System Forensics
Settings stored in RTC-backed CMOS memory
ACPI tables
SMBIOS table
HW protection settings (e.g. SPI W/P)
System firmware protection settings (Secure Boot, etc.)
MBR/VBR or UEFI GUID Partition Table (GPT)
Files on EFI system partition (boot loaders)
Contents of TPM Platform Configuration Registers (PCR)
Firmware images from other components such as HDD/SSD, NIC, Embedded Controller, etc.

## Slide 448: Live System Forensics
SPI Flash Memory Contents
chipsec_util spi info
chipsec_util spi dump SPI.bin
chipsec_util spi read <start> <size> BIOS.bin

## Slide 449: Understanding Layout of SPI Flash Memory
# chipsec_util.py spi info
. . .
============================================================
SPI Flash Map
------------------------------------------------------------
BIOS Flash Primary Region
------------------------------------------------------------
BFPREG = 0BFF0500:
Base : 00500000
Limit : 00BFF000
Shadowed BIOS Select: 0
------------------------------------------------------------
Flash Region | FREGx Reg | Base | Limit
------------------------------------------------------------
0 Flash Descriptor | 00000000 | 00000000 | 00000FFF
1 BIOS | 0BFF0500 | 00500000 | 00BFFFFF
2 Intel ME | 04FF0003 | 00003000 | 004FFFFF
3 GBe | 00020001 | 00001000 | 00002FFF
4 Platform Data | 00001FFF | 01FFF000 | 00000FFF
List of Flash Regions
BIOS region

## Slide 450: Extracting Contents of SPI Flash Memory...
Read/Write/Erase SPI flash memory
# chipsec_util.py spi
chipsec_util spi info|dump|read|write|erase [flash_address] [length] [file]
Examples:
chipsec_util spi info
chipsec_util spi dump rom.bin
chipsec_util spi read 0x700000 0x100000 bios.bin
chipsec_util spi write 0x0 flash_descriptor.bin
# chipsec_util.py spi dump spi.dump.bin
# dir spi.dump.bin
Directory of C:\Users\user\Desktop\chipsec\tool
03/05/2015 11:31 PM 8,388,608 spi.dump.bin
1 File(s) 8,388,608 bytes
0 Dir(s) 209,732,562,944 bytes free
SPI flash image
size: 8M
Full dump of SPI flash
CHIPSEC SPI command line interface

## Slide 451: Live System Forensics
BIOS and UEFI System Firmware
chipsec_util uefi var-list
chipsec_util uefi var-find fTA
chipsec_util uefi var-read db D719B2CB.. db.bin
chipsec_util uefi tables
chipsec_util uefi s3bootscript
chipsec_util acpi list
chipsec_util acpi table FADT

## Slide 452: Extracting Persistent EFI Configuration…
# chipsec_util.py uefi var-list
Secure Boot certificates (PK, KEK, db, dbx)
Setup Variable
BootOrder vars
AcpiGlobalVariable

## Slide 453: Extracting UEFI Secure Boot keys…
# chipsec_util.py uefi keys db.bin / dbx.bin / kek.bin

## Slide 454: Locating UEFI System Tables…
# chipsec_util.py uefi tables

## Slide 455: Locating Runtime UEFI Services…
# chipsec_util.py uefi tables

## Slide 456: Locating S3 Resume Boot Script Table…
AcpiGlobalVariable UEFI variable points to a structure in memory (ACPI_VARIABLE_SET_COMPATIBILITY)
[CHIPSEC] Reading EFI variable Name=‘AcpiGlobalVariable’..
[uefi] EFI variable AF9FFD67-EC10-488A-9DFC-6CBF5EE22C2E:AcpiGlobalVariable:
18 be 89 da
# chipsec_util.py uefi s3bootscript

## Slide 457: Extracting S3 Boot Script Table…
# chipsec_util.py uefi s3bootscript

## Slide 458: Decoding S3 Boot Script Opcodes…
# chipsec_util.py uefi s3bootscript
[000] Entry at offset 0x0000 (length = 0x21):
Data:
02 00 0f 01 00 00 00 00 00 00 c0 fe 00 00 00 00
01 00 00 00 00 00 00 00 00
Decoded:
Opcode : S3_BOOTSCRIPT_MEM_WRITE (0x02)
Width : 0x00 (1 bytes)
Address: 0xFEC00000
Count : 0x1
Values : 0x00
..
[359] Entry at offset 0x2F2C (length = 0x20):
Data:
01 02 30 04 00 00 00 00 21 00 00 00 00 00 00 00
de ff ff ff 00 00 00 00
Decoded:
Opcode : S3_BOOTSCRIPT_IO_READ_WRITE (0x01)
Width : 0x02 (4 bytes)
Address: 0x00000430
Value : 0x00000021
Mask : 0xFFFFFFDE

## Slide 459: Extracting CMOS Settings…
# chipsec_util.py cmos dump

## Slide 460: Locating ACPI Tables…
# chipsec_util.py acpi list

## Slide 461: Live System Forensics
Platform Hardware Configuration
chipsec_util pci enumerate
chipsec_util mmio list
chipsec_util mmio dump GTTMMADR
chipsec_util io list
chipsec_util cpu info
chipsec_util cpu cupid
chipsec_util ucode id

## Slide 462: Live System Forensics
Operating System
chipsec_util idt
chipsec_util gdt
chipsec_util cpu pt
chipsec_util mem read 0x41E 0x20 kbrd_buffer.bin
chipsec_util mem pagedump 0xFED00000 0x100000

## Slide 463: Live System Forensics
Platform Components
chipsec_util cmos dump
chipsec_util ec dump
chipsec_util ec read 0x2F
chipsec_util tpm state
chipsec_util tpm command pccrread 0
chipsec_util spd detect
chipsec_util spd dump
chipsec_util smbus read 0xA0 0x0 0x100

## Slide 464: Live System Forensics
Virtual Machine Monitor (VMM) Configuration
chipsec_util iommu list
chipsec_util iommu config
chipsec_util iommu pt
chipsec_util vm status
chipsec_util vm pt

## Slide 465: Live System Forensics
Checking Platform Configuration
chipsec_main
chipsec_main –m common.bios_wp
chipsec_main –m common.smrr
chipsec_main –m common.spi_lock
chipsec_main –m common.spi_desc
chipsec_main –m common.secureboot.variables
chipsec_main –m common.uefi.s3bootscript
chipsec_main –m remap
chipsec_main –m smm_dma

## Slide 466: Exercise 7.1
Online Forensics (UEFI Firmware and SPI Flash Contents)

## Slide 467: 7.2 Offline Forensic of Firmware Images
Important: ensure that firmware images were obtained using trusted hardware tools (that haven’t been tampered with)

## Slide 469: Where to Start From?
Option 1: Find original firmware image
    Check BIOS update (capsule) image or the BIOS image on the platform manufacturer’s web-site
    Check BIOS security advisories to understand how the firmware could be compromised and infected
    Compare multiple images including suspect and clean
Option 2: Extract a known good SPI memory image from a clean system (or from multiple systems)
Option 3: Make SPI memory dumps before and after the infection if you have an infector/dropper

## Slide 470: Analyzing firmware images
Decode two images:
  # chipsec_util.py decode original_bios.bin
  # chipsec_util.py decode current_bios.bin
Extracted binaries and other artefacts extracted from the images are stored in directories: original_bios.bin.dir, current_bios.bin.dir
Compare the contents of the two directories with any tool of choice:
  # diff –qr original_bios.bin.dir current_bios.bin.dir
Analyze/compare extracted EFI executables and analyze/compare extracted NV variables
    Contents of NVRAM (NV EFI variables) are dynamic and will differ between platform reboots (and even within the same boot)
    BIOS update images downloaded from the manufacturer’s web-site typically don’t contain NVRAM
    Update images may not contain non-BIOS regions of SPI flash memory (e.g. flash descriptor)

## Slide 471: BIOS/Firmware Forensics: Offline
Offline system firmware analysis
chipsec_util uefi keys PK.bin
chipsec_util uefi nvram vss bios.bin
chipsec_util uefi decode rom.bin
chipsec_util decode rom.bin
chipsec_util spidesc spi.bin

## Slide 472: Extracting EFI Executables
# chipsec_util.py decode spi.dump.bin
spi.dump.bin.dir
1_180000-7FFFFF_BIOS.bin.dir - SPI Flash Region
FV
06_8C8CE578-8A3D-4F1C-9935-896185C32DD3.dir - FV (FW volume)
F7D22BCA-1BCA-5591-CC8B-1CA98F2890FE.FV_PEIM-06.dir - EFI Executable
01_S_PE32.pe32.efi - Section

## Slide 473: UEFI FW Volume (FV) Structure
Volume offset : 0x00600000
File system GUID : 8C8CE578-8A3D-4F1C-9935-896185C32DD3
Volume length : 0x00080000 (524288)
Attributes : 0x0003FEFF
Header length : 0x00000048
Checksum : 0xE6AE (0xE6AE)
Extended Header Offset : 0x00000000
File offset : 0x00600048
Name : 92685943-D810-47FF-A112-CC8490776A1F
Type : 0x04
Attributes : 0x00000040
State : 0xF8
Checksum : 0xEAA3 (0xEAA3)
Size : 0x00E6DC (59100)
Section offset : 0x00600060
Name : S_PE32
Type : 0x10
File offset : 0x0060E728
Name : DF8556F0-3A61-11DE-8A39-0800200C9A66
Type : 0x06
Attributes : 0x00000040
State : 0xF8
Checksum : 0xA86D (0xA86D)
Size : 0x001E04 (7684)
Section offset : 0x0060E740
Name : S_PEI_DEPEX
Type : 0x1B
Section offset : 0x0060E748
Name : S_PE32
Type : 0x10
Firmware Volume
EFI Binary
Section

## Slide 474: Flash Descriptor
# chipsec_util.py spidesc fd.bin
[spi_fd] Valid SPI flash descriptor found at offset 0x00000000
+ 0x0000 Reserved : FFFFFFFFFFFFFFFFFFFFFFFFFFFFFF
+ 0x0010 Signature: 0x0FF0A55A
...
Flash Regions
--------------------------------------------------------
Region | FLREGx | Base | Limit
--------------------------------------------------------
0 Flash Descriptor | 00000000 | 00000000 | 00000FFF
1 BIOS | 07FF0180 | 00180000 | 007FFFFF
2 Intel ME | 017F0003 | 00003000 | 0017FFFF
3 GBe | 00020001 | 00001000 | 00002FFF
4 Platform Data | 00007FFF | 07FFF000 | 00000FFF (not used)
+ 0x0060 Master Section:
========================================================
+ 0x0060 FLMSTR0 : 0x0A0B0000
+ 0x0064 FLMSTR1 : 0x0C0D0000
+ 0x0068 FLMSTR2 : 0x08080118
Master Read/Write Access to Flash Regions
--------------------------------------------------------
Region | CPU/BIOS | ME | GBe
--------------------------------------------------------
0 Flash Descriptor | R | R |
1 BIOS | RW | |
2 Intel ME | | RW |
3 GBe | RW | RW | RW
4 Platform Data | | |
Access permissions to SPI flash regions

## Slide 475: Reading EFI Configuration
# chipsec_util.py uefi nvram nvar rom.dump.bin
Path to extracted/parsed NVRAM contents:
NVRAM dump: rom.dump.bin.dir\nvram_nvar.nvram.bin
Decoded variables: rom.dump.bin.dir\nvram_nvar.nvram.lst
Format of NVRAM and variables are platform/BIOS specific.
CHIPSEC supports multiple types of NVRAM (evsa, nvar, vss, vss_new)

## Slide 476: Decoding NVRAM from SPI dump
# type nvram_nvar.nvram.lst
...
--------------------------------
EFI Variable (offset = 0x4ec4):
--------------------------------
Name : Setup
Guid : EC87D643-EBA4-4BB5-A1E5-3F3E36B20DA9
Attributes: 0x7 ( NV+BS+RT )
Data:
01 5b 00 53 00 5b 00 01 01 72 00 68 00 72 00 01 | [ S [ r h r
01 50 00 46 00 50 00 01 01 50 00 46 00 50 00 01 | P F P P F P
01 f8 11 18 15 b8 0b 10 0e b8 0b 10 0e 90 01 d0 |
07 00 00 00 00 e8 03 d0 07 02 fa 00 00 28 64 00 | (d
03 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 |
00 00 00 00 00 00 00 00 00 01 00 00 00 00 00 00 |
00 00 00 01 00 00 01 01 01 01 01 01 00 00 00 00 |
00 00 00 00 01 02 00 01 00 00 00 00 00 00 00 00 |
00 00 00 00 00 01 02 01 08 00 00 00 00 00 00 00 |
00 00 01 00 00 00 00 00 00 00 00 00 00 00 00 00 |
00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 |
00 00 00 00 00 00 00 00 01 00 00 01 01 00 00 00 |
00 00 00 00 00 00 00 00 00 01 00 00 00 00 00 00 |
00 01 01 20 00 00 00 00 00 00 00 00 00 00 00 00 |
00 00 00 00 00 00 01 01 00 00 00 01 01 00 01 00 |
01 00 00 00 00 00 00 00 00 00 00 00 01 00 0a 00 |
00 01 00 00 02 01 00 01 00 00 00 01 00 00 00 00 |
...

## Slide 477: Exercise 7.2
Offline Firmware Image Forensics

## Slide 478: Case Study: ]HackingTeam[ UEFI Rootkit

## Slide 479: Case Study: HackingTeam’s UEFI Rootkit
Leaked emails reveal Uefi_windows_persistent.zip with UEFI based firmware image
The image contains unexpected sections:
    rkloader DXE driver executable
    NTFS DXE driver executable
    Unnamed PE executable
Initial analysis by ATR from July 2015

## Slide 480: Case Study: HackingTeam’s UEFI Rootkit

## Slide 481: Case Study: HackingTeam’s UEFI Rootkit
From leaked source code, we can see that the “rkloader” is a DXE driver that is automatically executed during boot
The module simply registers a callback (on the “READY_TO_BOOT” event) to execute the malicious payload

## Slide 482: Case Study: HackingTeam’s UEFI Rootkit
The callback then loads a UEFI application, which does the following:
  Check for infection by looking for UEFI variable “fTA”
  Use NTFS module to drop a backdoor (scoute.exe) and RCS agent (soldier.exe) onto the filesystem

## Slide 483: Case Study: HackingTeam’s UEFI Rootkit
Installation options
  Physical Access and a SPI programmer
  Booting a USB image to erase and reprogram firmware. Requires unlocked (vulnerable) firmware
Impact
  Automatic reinfection after removal of remote access components
  Detection
  Look for fTA UEFI variable with GUID
  8BE4DF61-93CA-11d2-aa0d-00e098302288
  Examine SPI image for additional DXE modules

## Slide 484: Exercise 7.3
Solve UEFI Crack Me

## Slide 485
Training materials are available on Github
https://github.com/advanced-threat-research/firmware-security-training
Yuriy Bulygin @c7zero
Alex Bazhaniuk @ABazhaniuk
Andrew Furtak @a_furtak
John Loucaides @JohnLoucaides

## Slide 486: Security of BIOS/UEFI System Firmware from Attacker and Defender Perspectives Miscellaneous Training Materials
Yuriy Bulygin *
Alex Bazhaniuk *
Andrew Furtak *
John Loucaides **
* Advanced Threat Research, McAfee
** Intel

## Slide 487: License
Training materials are shared under Creative Commons “Attribution” license CC BY 4.0
Provide the following attribution:
Derived from “Security of BIOS/UEFI System Firmware from Attacker and Defender Perspective” training by Yuriy Bulygin, Alex Bazhaniuk, Andrew Furtak and John Loucaides available at https://github.com/advanced-threat-research/firmware-security-training

## Slide 488: MinnowMax Platform and EDKII

## Slide 489: MinnowMax
Open hardware platform
Baytrail single or dual core
From http://firmware.intel.com/projects
This project focus in on the firmware source code (and binary modules) required to create the boot firmware image for the MinnowBoard MAX. The UEFI Open Source (EDKII project) packages for MinnowBoard MAX are available at http://tianocore.sourceforge.net/wiki/EDK2. To learn more about getting involved in the UEFI EDKII project visit the How to Contribute page.
The source code builds using Microsoft Visual Studios and GNU C Compiler (for both 32 and 64 bit images) - production and debug execution environments. The source code builds the same UEFI firmware image shipping on MinnowBoard MAX.
- See more at: http://firmware.intel.com/projects#sthash.1oOc8srY.dpuf

## Slide 490: MinnowBoard Interfaces
Source: https://01.org/android-ia/guides/android-5.x-lollipop-bring-guide

## Slide 491: USB Ports in MinnowBoard
2 USB ports: USB3 on bottom and USB2 on top

## Slide 492: UART Pinout Configuration

## Slide 493: Connect to UART port

## Slide 494: UART configuration
Baud rate – 115200
Flow control – 0
To read UART output
On Windows use: PUTTY or Tera Term
On Linux run minicom:
$minicom -D /dev/ttyUSB0

## Slide 495: Successfully launch Linux

## Slide 496: UEFI shell
For come to Setup Screen type exit & enter in the UEFI shell:

## Slide 497: Boot from USB Device

## Slide 498: MinnowBoard Configuration
Students need to configure Ethernet card in laptops with 192.168.1.1/24 IP address
Access to MinnowBoard board through SSH (22 port).
Recommended clients: PUTTY, MobaXterm
MinnowBoard Network configuration:
IP address: 192.168.1.2
Gateway: 192.168.1.1

## Slide 499: MinnowBoard File System
~/Desktop/bios – MinnowBoard EDK2 FW sources
~/Desktop/chipsec – CHIPSEC framework
~/Desktop/image – binary BIOS images
~/Desktop/udk-debugger – udk-debugger installer & config
~/Desktop/patches – BIOS patches
~/Desktop/tools – misc useful BIOS/UEFI utilities
~/Desktop/exercises – materials for exercises

## Slide 500: Useful UEFI Setup Options

## Slide 501: Changing Boot Order On MinnowMax

## Slide 502
Training materials are available on Github
https://github.com/advanced-threat-research/firmware-security-training
Yuriy Bulygin @c7zero
Alex Bazhaniuk @ABazhaniuk
Andrew Furtak @a_furtak
John Loucaides @JohnLoucaides